| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | AE re-targeting |
| Source:* | LG Electronics |
| Contact: | Seungmyeong Jeong, seungmyeong.jeong@lge.com |
| Date:* | 2014-01-10 |
| Abstract:* | Local CSE performs re-targeting of incoming requests targeted to AEs |
| Agenda Item:* | TBD |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate this text into the TS. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

The concept of AE re-targeting is to provide a mechanism that all request messages for AE shall be targeted a local CSE first and then the CSE re-targets the messages to the AE. With this, address of AE (i.e., point of access) is exposed only to the local CSE, and the local CSE forwards messages only from the Originators who has proper access rights to the <application> resource.

Resource type name <application> seems to be replaced by <ae>, this needs more discussion.

- Proposal

Start of new text 1

### 7.3.3		Application Entity Re-targeting

#### 7.3.3.1	Application Entity Point of Access (AE-PoA)

An Originator shall send a request to an AE by targeting <application> resource on a local CSE, if the local CSE verifies access rights of the Originator to the <application> resource, the local CSE shall re-target the request to the address specified as AE Point of Access (AE-PoA). The AE-PoA is initially configured in <application> resource when the AE registers to the local CSE. If the <application> resource does not contain an AE-PoA, a request to the AE cannot be re-targeted to the AE.

Figure 7.3.3-1: Re-targeting a request to an AE

End of new text 1

Start of changed text 1

### 9.6.18	 Resource Type Application

The <application> resource represents information about an Application Entity known to a given Common Services Entity.

Editor's Note: Cont ARC #594R05 did not include the pictorial representation for this resource. The following picture has been generated by the Rapporteour. The original contributor to verify if something is missing.

Figure 9.6.18-1: Structure of <Application> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicitly in Table 9.6.18-1 (0 indicates the optionality of the child resource).

Table 9.6.18-1: Child resources of <Application> resource

| Child Resource Name of <Application> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See section 9.6.9. |
| [variable] | <container> | 0..n | See section 9.6.3. |
| [variable] | <group> | 0..n | See section 9.6.5. |
| [variable] | <accessRight> | 0..n | See section 9.6.2. |
| software_[i] | <mgmtObj> | 1..n | See section 9.6.10 for <mgmtObj>. This resource represents the software component (or components, if the multiplicity is greater than 1) that compose the application. This mgmtObj shall have at least the following <parameters> child resources of its “parameters” subresource: - name (multiplicity 1) - version (multiplicity 1) - state (multiplicity 1) |
| [variable] | <commCapabilities> | 1..n | Resource <commCapabilities> needs to be defined. This resource describes the communication capabilities (essentially the protocols) supported and used by the corresponding Application Entity over the Mca reference point to this CSE. |

The <Application> resource shall contain the attributes described in Table 9.6.18-2.

Table 9.6.18-2: Attributes of <Application> resource

| Attribute Name of <Application> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RO | See section 9.6.1 where this common attribute is described. |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (eg. “HeatingMonitoring”) |
| App-ID | 1 | RO | Application Identifier |
| App-Inst-ID | 1 | RO | When the application resource refers to an actual application instance in the executing environment. |
| aePoA | 0..1 | RW | AE Point of Access that local CSE re-targets a request that was originally targeted <application> resource |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is managed and understood by the application; to be passed to the application |

End of changed text 1