| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | Addition of Registration Table |
| Source:* | Philip Jacobs, Cisco Systems Inc., Barbara Pareglio, NEC Labs |
| Contact: | phjacobs@cisco.com, Barbara.Pareglio@neclab.eu |
| Date:* | 2014-01-10 |
| Abstract:* | This contribution adds a table to the detailed CSF clause to show which entities register with which other entities R01 modified table entries R02 modified to address conf call feedback |
| Agenda Item:* | Contributions |
| Work item(s): | WI-0002 |
| Document(s) Impacted* | TS-0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Decide whether to include the table |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

In clause 6.2.9.2, there is mention of 6 registrations including entities: Device, AE, Local CSE, Remote CSE, MN, ASN, IN. However there is no mention of registration for Node-less AEs<->IN-CSE, ADN-AE<->MN-CSE, ADN-AE<->IN, MN-CSE<->MN-CSE, or ASN-CSE<->MN-CSE, or NSE.

It would be helpful to mention all entities and indicate which ones register. Therefore the addition of a table is proposed.  Text is proposed regarding registration for NSEs.

---------------------------Start of modification 1 -------------------------

#### 6.2.9.2	Detailed Descriptions

Registration is the process of delivering AE or CSE information to another CSE for being able to use the M2M Services.

The CSE on an Application Service Node or on a Middle Node shall perform registration with the CSE in the Infrastructure Node in order to be able to use M2M services offered by the CSE in the Infrastructure Node. An Application on an Application Service Node or on a Middle Node shall perform registration locally with the corresponding CSE in order to use M2M services offered by that CSE. The same holds for the registration of an Application on the Infrastructure Node. An Application on an Infrastructure Node shall perform registration locally with the associated CSE on Infrastructure Node. A registered Application shall be able to have interactions with its local CSE without the need to have the local CSE registere with other CSEs. Such registrations are applicable to a single M2M Service Provider Domain.

A CSE on an Application Service Node or on a Middle Node shall perform registration with the CSE on an Infrastructure Node and vice versa. As a result of successful CSE registration, the CSEs on ASN/Middle Node and Infrastructure Node establish a peering relationship and shall be able to exchange context information.

A (physical) Device shall be able to register with its local CSE for registering its properties/attributes. Such registration enables correlation of Devices Identities such as M2M-Node-ID with the CSE-ID.

Editor’s Note: The need for Device Registration and the relationship with CSE Registration are FFS.

Editor’s Note: The use of External ID in Registration is FFS.

The following Table shows which oneM2M entity types may register with which other entity types.

Table 6.2.9.2-1: Entity Registration

| Originator | Receiver | Uni/Bi-directional |
| --- | --- | --- |
| ADN-AE | MN-CSE, IN-CSE | Uni-directional |
| ASN-AE | ASN-AE | Uni-directional |
| MN-AE | MN-CSE | Uni-directional |
| IN-AE | IN-CSE | Uni-directional |
| Nodeless AE | IN-CSE | Uni-directional |
| ASN-CSE | MN-CSE, IN-CSE | Bi-directional |
| MN-CSE | ASN-CSE, MN-CSE, IN-CSE | Bi-directional |
| IN-CSE | ASN-CSE, MN-CSE | Bi-directional |

An ADN-AE is allowed to register to one CSE (MN-CSE or IN-CSE) at one time.

An ASN-CSE is allowed to register with one other CSE (MN-CSE or IN-CSE) at one time.

Regarding registration with an NSE, the nature of the relationship between NSE and CSE is not the M2M Service registration as defined in this section. However establishing this relation is one of the steps of the registration between CSEs which reside in different node types. How this relation is established is mandated by the specific underlying network used.

Registration information shall be able to include:

    - Reachability schedules, which are elements of a node’s policy, and specify when messaging may occur between nodes. Reachability schedules may be used in conjunction with other policy elements. When reachability schedules are not present in a node then that node is expected to be always reachable.

The following is included in the Registration information:

  - Identifier

  - Reachability

Editor’s note: Further Registration information is FFS.

---------------------------End of modification 1 -------------------------

# Comments

ADN-AE to ASN-CSE is not supported per Figure 6-1