| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Huawei, China Unicom |
| Format:* | ARC8.3 |
| Date:* | 2014-01-15 |
| Contact:* | Qi Yu (yuqi@huawei.com); Changwei Hu (hucw5@chinaunicom.cn ) |
| Reason for Change/s:* | This contribution proposes to add the missing parameters at section8.1.2.1 and 8.1.5. R01: Add Notify column. |
| Clause/Sub Clause Affected* | 8.1.2.1 and 8.1.5 |
| Agenda Item:* | ARC |
| Work item(s): | WI0002 |
| Document(s) Impacted* | oneM2M-TS 0001 Technical Architecture v 0.3.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Background

Some parameters are missing at section 8.1.2.1 and 8.1.5.

======================== START 1ST CHANGE ===========================

#### 8.1.2.1	Summary of Request Message Parameters

Table 8.1.2.1-1summarises the parameters specified in section 8.1.2 for the Request message, showing any differences as applied to C, R, U or D operations. “M” indicates mandatory, “O” indicates optional, “N/A” indicates “not applicable”.

Table 8.1.2.1-1: Summary of Request Message Parameters

| Request Message Parameter \ Operation | Create: a new resource is created | Retrieve: an existing resource is read and the result is provided | Update: the content of an existing resource is replaced with new content | Delete: an existing resource and all its sub-resources are deleted | Notify: the content / address is transferred |
| --- | --- | --- | --- | --- | --- |
| To (to) – the address of the target resource on the target CSE | M | M | M | M | M |
| From (fr) – the identifier of the message Originator | M | M | M | M | M |
| Request Identifier (ri) – uniquely identifies a Request message | M | M | M | M | M |
| Resource Type (rt) - of resource to be created | M | N/A | N/A | N/A | N/A |
| Content (cn) - to be transferred | O | O | M | N/A | M |
| Originating Timestamp (ot) - when the message was built | O | O | O | O | O |
| Request Expiration Timestamp (rqet) – when the request message expires | O | O | O | O | O |
| Result Expiration Timestamp (rset) -when the result message expires | O | O | O | O | O |
| Operational Execution Time (oet) - the time when the specified operation is to be executed by the target CSE. | O | O | O | O | O |
| Response Type (rt) – local CSE response shall either indicate that the Request was accepted, or include the operation result | O | O | O | O | O |
| Result Destination (rd) – either a reference to where the result is stored, or the result is sent to the Originator | O | O | O | O | N/A |
| Result Persistence (rp) - the duration for which the reference containing the responses is to persist | O | O | O | O | N/A |
| Result Content (rc) – the expected components of the result | O | O | O | O | N/A |
| Lifespan (ls) - time after which the system should not deliver the message | O | O | O | O | O |
| Event Category (ec) – indicates how and when the system should deliver the message | O | O | O | O | O |
| Delivery Aggregation (da) - aggregation of requests to the same target CSE is to be used | O | O | O | O | O |
| Group Request Identifier (gid)-Identifier added to the group request that is to be fanned out to each member of the group. | O | O | O | O | O |

======================== END 1ST CHANGE =============================

======================== START 2nd CHANGE ===========================

### 8.1.5	Summary of Response Message Parameters

Table 8.1.5-1 summarises the parameters specified in sections 8.1.1 and 8.1.3 for the Response messages, showing any differences as applied to successful C, R, U or D operations, and unsuccessful operations. “M” indicates mandatory, “O” indicates optional, “N/A” indicates “not applicable”.

Table 8.1.5-1: Summary of Request Message Parameters

| Response Message Parameter \ Success or not | Successful Operation: Create: a new resource is created | Successful Operation: Retrieve: an existing resource is read and the result is provided | Successful Operation: Update: the content of an existing resource is replaced with new content | Successful Operation: Delete: an existing resource and all its sub-resources are deleted | Successful operation: Notify: the content / address is transferred | Unsuccessful Operation |
| --- | --- | --- | --- | --- | --- | --- |
| To (to) –the identifier of the Originator | O | O | O | O | O | O |
| From (fr) – the identifier of the Receiver | O | O | O | O | O | O |
| Request Identifier (ri) – uniquely identifies a Request message | M | M | M | M | M | M |
| Result (rs) - operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., | M | M | M | M | M | M |
| Status codes (cs) - (e.g., authorization timeout, etc.) | O | O | O | O | O | O |
| Response Address (ra) - address for the temporary storage of end node Responses. | O | O | O | O | N/A | N/A |
| Content (cn) - to be transferred | O (The address and/or the content of the created resource) | M (the retrieved resource content or aggregated contents of discovered resources) | O (The content replaced in an existing resource) | O (The content actually deleted) | N/A | N/A |
| Originating Timestamp (ot) - when the message was built | O | O | O | O | O | O |
| Result Expiration Timestamp (rset) – when the message expires | O | O | O | O | N/A | O |

======================== END 2nd CHANGE =============================