| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | NEC, Cisco |
| Format:* | TP9 |
| Date:* | 2014-01-21 |
| Contact:* | Barbara Pareglio (barbara.pareglio@neclab.eu);Philip Jacobs (phjacobs@cisco.com) |
| Reason for Change/s:* | Modification to the CREATE procedure for accommodating Registration |
| Clause/Sub Clause Affected* |  |
| Agenda Item:* | Contribution |
| Work item(s): |  |
| Document(s) Impacted* | oneM2M-TS 0001 Technical Architecture v 0 3 2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Discussion

Introduction

The current specification implies that a sort of registration of AEs and CSEs exists, but there is no procedure defined for it.  The contribution proposes changes to the common CREATE procedure for accommodating application registration function.

Proposal

This contribution proposes:

- Modification in section 10.1 for adjusting the basic procedure which distinguish the CREATE procedure for Registration and for non-registration.

======================== START 1ST CHANGE ===========================

### 10.1.1		CREATE (C)

The CREATE procedure shall be used by an Originator (CSE or AE) to create a resource on a Receiver CSE (also called the hosting CSE). The procedure will be divided in two, since there is a need to distinguish between registration related creation and non-registration related procedures.

The registration related procedure is only applicable for the following resource types:

- <Application>, and

- <RemoteCse>

10.1.1.1	 Non-registration related CREATE procedure

This procedure is valid for all resources which are not related to registration.

Originator requests to create a resource by using the CREATE method. See section 8.1.2 for the information to be included in the Request message.

Receiver, after ensuring that the Originator has been authenticated and that the request is allowed by the given privileges, shall validate the receive request and shall create the resource. The creation of the resource shall only be allowed if the Originator has the appropriate privileges, from the Access Rights of the addressed target CSE, to create such a resource. The receiver shall use, if present, the suggested name from the information parameter nm in the request. If the suggested name of the resource cannot be use (i.e a resource with that name alredy exists) the Receiver shall reject the CREATE request. If the request does not provide the optional nm, then the Receiver shall create the resource and assign a name to it.

Figure 10.1.1-1: Procedure for CREATEing a Resource

Step 001: The Originator shall send the following information in the CREATE Request message:

op: 	C (Create);

to: 	URI of  the target resource where the new resource should be created

fr: 	ID of the Originator  (either the AE or CSE)

Editor's Note: AE or CSE may not have the ID upon its registration request. Alternative information for fr is FFS.

ty:	type the resource to be created

cn: 	attributes of the resource to be provided by the Originator:

Editorr’s note: which parameters are deducted to be mandatory/optional in the request is for FFS. Section 8.1 should provide a generic mechanism to identify mandatory params for a request by looking at how the resource is defined. E.g. If the attribute in the resource definition is identified as mandatory and it is of type RW, then it is also intended as mandatory in the request.

Editor’s Note: references to elements defined in sect 8 have been added here. They may be removed if we decide to move sect 8.1.2-4 to stage 3 doc. In this case, these references will be removed and sect 1 of this document would replace sect 8.1.2-4 in the TS-0001.

Step 002:  The Receiver shall:

- Authenticate and authorized the request

- Verify that the identifier, if provided by the Originator in the Create Request message, does not already exist in its resource structure.

- Assign an identifier to the resource to be created if a valid identifier is not provided by the Originator.

- Assign/modify values for certain attributes of the resource, where allowed by the resource itself..

Editor’s note: which parameter is allowed to be provided by the Receiver CSE is for FFS. There are few cases: the WO, RO and in some cases the Receiver may also changes the RW attributes, e.g. the expirationTime or the max number of instances which could be related to subscription agreements or policies.

- On successful validation of the Create Request, the Receiver shall create the requested resource.

Step 003: The Receiver shall respond with a Response message shall contain the following information:

to: Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

fr: Optional. ID of the Receiver.

cn: URI and optionally the content of the created resource. The Receiver shall provide the content if the created resource contains attributes which were modified by the Receiver.

See sections 8.1.3 and 8.1.4 for the information to be included in the Response message.

General Exceptions:

- The Originator is not registered with the Receiver CSE. The Receiver responds with an Error.

- The Originator is not authorised to Create a resource on the Receiver. The Receiver responds with an Error.

- The resource with the specified name (if provided) already exists at the Receiver. The Receiver responds with an Error.

- The provided information in cn is not accepted by the Receiver (e.g. missing mandatory parameter). The Receiver responds with an Error.

10.1.1.2	 Registration related CREATE procedure

This section described the CREATE procedure for <RemoteSce> and <Application> resource type.

10.1.1.2.1	 SCE Registration procedure

TBD

10.1.1.2.2	 Application Registration procedure

The procedure for application registration follows the procedure described in section 10.1.1.1 with the following exception:

Receiver, after ensuring that the Originator has been authenticated the Receiver shall always allow the creation of the <application> resource since at registration there are no appropriate privileges associated with the application yet. The receiver shall use, if present, the suggested name from the information parameter nm in the request. If the suggested name of the resource cannot be use (i.e a resource with that name alredy exists) the Receiver shall reject the CREATE request. If the request does not provide the optional nm, then the Receiver shall create the resource and assign a name to it.

Step 001: The Originator shall send the following information in the CREATE Request message:

fr: 	either App-Inst-ID if already known, or AE token needed for authentication and authorization of the AE

Editor's Note: AE may not have the ID upon its registration request. Need to verify that Token is used from WG4.

### 10.1.2	RETRIEVE (R)

The RETRIEVE operation shall be used for retrieving the information stored for any of the attributes for a resource at the Receiver CSE. The Originator CSE or AE may also request to retrieve only a specific attribute or part of an attribute by including the identity of such attribute in the Request message.

Editor's Note: The statement in the para above is not clear. Is this operation targeted for retrieving ALL attributes for a resource together (as a Group) or for specific attributes only? Depending on the answer, the text above needs to be updated. The text in the para that follows assumes that this operation is for retrieving all attributes for a resource. If the Request is for retrieving only a specific attribute, then the identity of such attribute is included in the Request message.

Originator requests to retrieve all attributes of the target resource by using RETRIEVE Request.  See section 8.1.2 for the information to be included in the Request message. If only specific attribute(s) or part of an attribute needs to be retrieved, the address of such attribute (e.g., the URI) shall also be included in the Request message.

Receiver performs local processing to verify the existence of requested resource and checks permissions for retrieving the information related to the resource. After the successful verification, the Receiver shall return the requested information, else an error indication shall be returned.

Figure 10.1.2-1: 	Procedure for RETRIEVing a Resource

Step 001:	The Originator shall request to RETRIEVE a resource from the Receiver.

op:	R (Retrieve)

to: 	URI of the target resource

fr:	 ID of the Originator

NOTE: If a specific attribute(s) or part of an attribute needs to be retrieved, the address of such attribute(s) (e.g., URI) shall also be included in the cn information. Details are FFS, possibly for WG3 to specify (WG2 to confirm this text).

Step 002:	The Receiver shall verify the existence of the resource and check if the Originator is authorised to retrieve the resource.

Step 003:	The Receiver shall respond with a Response message that shall contain the representation of the resource, and the following information:

to: Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

fr: Optional. ID of the Receiver.

cn: 	content of resource retrieved

General Exceptions:

1.	The Originator is not authorized to retrieve the resource. The Receiver responds with an Error.

2.	The resource does not exist. The Receiver responds with an Error.

### 10.1.3	UPDATE (U)

The UPDATE operation shall be used for updating the information stored for any of the attributes at a target resource. Especially important is the "expirationTime", since a failure in refreshing this attribute may result in the deletion of the resource. Alternatively, the Originator CSE or AE can request to update only a specific attribute or part of an attribute at the target resource.

Originator requests to update any of the attributes at the target resource by using UPDATE Request message. The Originator shall send new (proposed) values for the attribute(s) that need to be updated.  See section 8.1.2 for the information to be included in the Request message.

Receiver after verifying the existence of the addressed resource, the validity of the attributes provided and the permissions to modify them, shall update the attributes provided and shall return a Response message to the Originator with the operation results as specified in section 8.1.3.

Figure 10.1.3-1: 	Procedure for UPDATing a Resource

Step 001:	The Originator shall send the following information in the UPDATE Request message:

op:	U (Update)

to: 	URI to the target resource

fr: 	ID of the Originator

cn: 	Information to be updated at the target resource

Step 002:	The Receiver shall validate if the Originator is authorised to perform the modification to the target resource. On successful validation, the Receiver shall update the resource as requested.

Step 003:	The Receiver shall respond with a Response message that  shall contain the following information:

to: Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

fr: Optional. ID of the Receiver.

rs: 	Operation result

General Exceptions:

1.	The Originator is not authorized to update the resource. The Receiver responds with an Error.

2.	The resource does not exist. The Receiver responds with an Error.

### 10.1.4	DELETE (D)

The DELETE operation shall be used by an Originator CSE or AE to delete a resource at a Receiver CSE. The delete procedure shall consist of the deletion of all related information of the target resource.

Originator requests to delete a resource by using a DELETE Request message. See section 8.1.2 for the information to be included in the Request message.

Receiver shall verify the existence of the requested resource, and the permissions for deleting the resource. The Receiver shall remove the target resource and shall return a Response message to the Originator with the appropriate operation results as specified in section 8.1.3.

Figure 10.1.4-1:  Procedures for DELETING a Resource

Step 001:	The Originator shall send a DELETE Request message to the Receiver.

op:	D (Delete)

to: 	URI of the target resource

fr: 	ID of the Originator

Step 002:	The Receiver shall verify the existence of the requested resource and if the Originator is authorised to delete the resource. On successful validation, the Receiver shall remove the resource.

Step 003:	The Receiver shall respond with a Response message that shall contain the following information:

to: Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

fr: Optional. ID of the Receiver.

rs: 	Operation result

General Exceptions:

1.	The Originator is not authorized to update the resource. The Receiver responds with an Error.

2.	The resource does not exist. The Receiver responds with an Error.

### 10.1.5	NOTIFY (N)

The NOTIFY operation shall be used for notifying information.

Originator: The Originator requests to notify information by using NOTIFY method. See section 8.1.2 for the information to be included in a Request message.

Receiver: The Receiver responds to the Originator with the operation results as specified in section 8.1.3.

Figure 10.1.5-1: Procedure for NOFIFYing Information

Step 001: A notification to be sent to the Receiver is triggered in the Originator.

Step 002: The Originator shall send the following information in the NOTIFY Request message:

op:	N (Notify)

to: 	Address where the notification should be sent to

fr:	ID of the Originator

cn:	Notification data and/or Notification reference

- Editor’s Note: cn needs to be updated in section 8.1 to include references to information.

Step 003: The Receiver responds with a Response message that shall contain the following information:

rs: 	operation result

General Exceptions:

1.	If the notification cannot be sent to the URI then error response will be provided by the CSE Receiver.

- Editor’s note: General exceptions are FFS in particular for notification failures.

======================== END 1st  CHANGE =============================

# Comments

To check, preference to just return the URI.