| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC |
| Title:* | CSEBase Resource Type |
| Source:* | LG Electronics, Telecom Italia |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com Lupano Michele, Telecom Italia, michele.lupano@telecomitalia.it |
| Date:* | 2014-01-14 |
| Abstract:* | This contribution proposes CSEBase resource type. R01: change the figure to align with attribute/child resource tables R02: Make terminology consistent within the specification. |
| Agenda Item:* | ARC |
| Work item(s): | WI 0002 |
| Document(s) Impacted* | Technical Specification – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes new section for missing CSEBase resource type.

============================Start of 1st Change==============================

### 9.6.X	 Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE.

Figure 9.6.19-1: Structure of <CSEBase> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.X-1 (0 indicates the optionality of the child resource).

Table 9.6.X-1: Child resources of <CSEBase> resource

| Child Resource Name of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCse> | 0..n | See section 9.6.19. |
| [variable] | <node> | 1 | See section 9.6.17. |
| [variable] | <application> | 0..n | See section 9.6.18. |
| [variable] | <container> | 0..n | See section 9.6.3. |
| [variable] | <group> | 0..n | See section 9.6.5. |
| [variable] | <accessRight> | 0..n | See section 9.6.2. |
| [variable] | <subscription> | 0..n | See section 9.6.9. |
| [variable] | <mgmtObj> | 0..n | See section 9.6.10. |
| [Variable] | <mgmtCmd> | 0..n | See section 9.6.12. |
| [Variable] | <locationPolicy> | 0..n | See section 9.6.7. |

Editor’s note: this list should be updated. Which resource types are added is FFS.

Editor’s note: how to extend functionality is FFS.

The <CSEBase> resource shall contain the attributes described in Table 9.6.X-2.

Table 9.6.X-2: Attributes of <CSEBase> resource

| Attribute Name of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| accessRightID_[i] (aRI_[i]) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| supportedResourceType (sRT) | 1 | RO | List of the resource types which are supported in CSE. this attribute contains subset of resource types listed in section 9.2 |
| pointOfAccess_[i] (poA_[i]) | 0..n | RW | represents the list of physical addresses to be used for remote CSEs to connect to this CSE (e.g. IP address, FQDN). This attribute is used to announce its value to remote CSEs. |

============================End of 1st Change===============================

============================Start of 2nd Change==============================

### 9.6.9	Resource Type subscription

The <subscription> resource contains subscription information for its subscribed-to resource.

The list of subscribable resources is as follows.

- <entity> resource (see section TBD)

- <Application> resource (see section 9.6.18)

- <accessRight> resource (see section 9.6.2)

- <container> resource (see section 9.6.3)

- <group> resource (see section 9.6.5)

- <CSEBase> resource (see section 9.6.X)

============================End of 2nd Change==============================

============================Start of 3rd Change==============================

### 9.6.19	Resource Type remoteCSE

A <remoteCse> resource shall represent a remote CSE that is registered to the local CSE. CSE resources shall be located directly under the <CSEBase>.

Conversely each registered CSE shall also be represented as a sub-set of <remoteCse> resource in the registering CSE's <CSEBase>.

For example, when CSE1 registers with CSE2, there will be two <remoteCse> resources created: one in CSE1 <CSEBase1>/<remoteCse2> and one in CSE2 <CSEBase2>/<remoteCse1>.

Note that the creation of the two resources does not imply mutual registration. The <CSEBase1>/<remoteCse2> is only local to CSE1 and is for its internal use.

Figure 9.6.19-1: Structure of <remoteCSE> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicitly in Table 9.6.19-1 (0 indicates the optionality of the child resource).

Table 9.6.19-1: Child resources of <remoteCSE> resource

| Child Resource Name of <remoteCSE> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <Application> | 0..n | See section 9.6.18. |
| [variable] | <container> | 0..n | See section 9.6.3. |
| [variable] | <group> | 0..n | See section 9.6.5. |
| [variable] | <accessRight> | 0..n | See section 9.6.2. |
| [variable] | <subscription> | 0..n | See section 9.6.9. |
| [variable] | <mgmtObj> | 0..n | See section 9.6.10. |

The <remoteCSE> resource shall contain the attributes described in Table 9.6.19-2.

Table 9.6.19-2: Attributes of <remoteCSE> resource

| Attribute Name of <remoteCSE> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| pointOfAccess (poA) | 0..n | RW | For server capable remote CSE it represents the list of physical addresses to be used to connect to it (e.g. IP address, FQDN). The attribute is absent if the remote CSE is not server capable. |
| CSEBase (csB) | 1 | WO | The URI of the <CSEBase>of the original CSE represented by remote CSE. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |

<remoteCse> and announced <remoteCse> shall have different resourceType coding.

- Editor’s Note on CSE-ID: an alignment between CSE-ID and baseURI is needed.

- Editor’s Note on baseURI: the alignment with naming convention proposed for inter-M2M service provider is needed.

- Editor’s Note on child resources: child resources of <remoteCse> resource can accommodate listed resources and their announced versions.

============================End of 3rd Change==============================

============================Start of 4th Change==============================

## 9.1	General Principles

The following are the general principles for the design of the resource model.

- The "type" of all resource shall be specified. New resource types shall be supported as the need for them is identified;

- The root of the resource structure in a CSE shall be assigned an absolute address, such as <baseURI>;

- The resource structure shall be kept reasonably simple. In particular:

- <Application> Resources belonging to the local CSE shall be located directly under the baseURI resource,

- <Access Right> Resources belonging to the local CSE shall be located either directly under the baseURI resource, or under an <Application> resource.

- <Group> resources belonging to the local CSE shall be located either directly under the baseURI resource, or under an <Application> resource.

- <remoteCSE> resources representing a remote CSE shall be located directly under the baseURI resource,

- <Container> Resources belonging to the local CSE shall be located either under the baseURI resource or, or under an <Application> resource, or under another <container> resource;

Editor’s note: This section may need fixing due to inconsistency.

Editor’s note: local CSE terminology needs discussing.

============================End of 4th Change==============================

# Comments

mgmtCmd, locationPolicy are added based upon TS.

Change: baseRoot ( CSEBase