| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | NEC, CISCO |
| Format:* | TP9 |
| Date:* | 2014-02-07 |
| Contact:* | Barbara Pareglio (barbara.pareglio@neclab.eu), Phil Jacobs (phjacobs@cisco.com) |
| Reason for Change/s:* | Introducing Registration procedure for RemoteCSE |
| Clause/Sub Clause Affected* |  |
| Agenda Item:* | Contribution |
| Work item(s): |  |
| Document(s) Impacted* | oneM2M-TS 0001 Technical Architecture v 0 3 2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Discussion

Introduction

The current specification implies that a sort of registration of AEs and CSEs exists, but there is no procedure defined for it.  The contribution proposes all the changes in the specification for adding RemoteCSE operations on the resource.

Proposal

This contribution proposes to add the procedure for the registration of a CSE and it describes all operations allowed on the <RemoteCSE> resource. The new section shall belong to 10.2, the order is not particularly important.

This specifically consists in providing the following changes:

- Add in section 10.2 the operations that can be performed as a consequence of registration: including the 4 CRUD operations on CSE.

- For making the section less error-prone, reference to the appropriate procedure from section 10.1  (or others) is added and only deviations from those procedures are indicated in these sections.

===================== START 1ST CHANGE  (NEW SECTION) ========================

### 10.2.X	<RemoteCSE> Resource

#### 10.2.X.1	Create <RemoteCSE>, aka CSE Registration

This flow is used for creating a <RemoteCSE> resource. It is part of the registration procedure for remote CSEs on the local CSE (which is also the hosting CSE), as described in section 10.1.1.2.1

Originator:  A CSE.

Receiver : once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), the Receiver shall grant the request after successful verification of the request

Table 10.2.1.1-1 <remoteCSE> CREATE flow

| CREATE: Description |
| --- |
| Pre-Conditions | The Originating CSE has to be successfully authenticated and the access to the receiver has been granted. The Originating CSE has an assigned CSE-ID.. |
| Information on Request message | All parameters defined in table 8.1.2.1-1 are applicable plus specifically: fr: CSE-ID. nm: the name of the <remoteCSE> resource is optional cn: the resource content shall provide the information as defined in section 9.6.19. The following attributes from section 9.6.19 are mandatory for the request: “resourceType” which shall be set to the appropriate tag that identify the <remoteCse> resource as defined in 9.6.1 “CSE-ID”: which contains the CSE-ID “cseType” The following attributes from section 9.6.19 are optional for the request: “expirationTime” “accessRightID” “labels” “pointOfAccess” |
| Local processing on Hosting CSE | No change from the basic CREATE procedure (section 10.1.1) |
| Information on Response message | All parameters defined in table 8.1.2.1-1 are applicable as indicated in the table with the specific details for: cn: URI of the created <remoteCSE> resource, according to section 10.1.1 |
| Post-Conditions | Two new <remoteCSE> resources are created, one on the targeted CSE (Receiver) and one under the <CSEBase> of the Originator that correspond to the CSE of the Receiver. |
| Exceptions | All exception described in the basic CREATE procedure (section 10.1.1) are applicable. |

#### 10.2.1.2	Retrieve <remoteCSE>

This flow is used for retrieving the representation of the <remoteCSE> resource with its attributes.

Originator: An AE or a CSE.

Receiver: once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), the Receiver shall retrieve the <remoteCSE> resource.

Table 10.2.1.2-1 <remoteCSE> RETRIEVE flow

| RETRIEVE: Description |
| --- |
| Pre-Conditions | The targeted <remoteCSE> has been created (as part of the registration) |
| Information on Request message | All parameters defined in table 8.1.2.1-1 are applicable plus specifically: cn: void |
| Local processing on Hosting CSE | No change from the basic RETRIEVE procedure (section 10.1.2) |
| Information on Response message | All parameters defined in table 8.1.2.1-1 are applicable plus specifically: cn: attributes of the <remoteCse> resource as defined in section 9.6.19. |
| Post-Conditions | No changes on the resource as consequence of the RETRIEVE operation |
| Exceptions | All exception described in the basic RETRIEVE procedure (section 10.1.2) are applicable. |

#### 10.2.1.3	Update <remoteCSE>, aka Re-registration

This flow is used for updating the attributes and the actual data of an <remoteCSE> resource.

Originator: An AE or a CSE.

Receiver: once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), , the Receiver shall update the <remoteCSE> resource.

Table 10.2.1.3-1 <remoteCSE> UPDATE flow

| UPDATE: Description |
| --- |
| Pre-Conditions | The targeted <remoteCSE> has been created (as part of the registration) |
| Information on Request message | All parameters defined in table 8.1.2.1-1 are applicable plus specifically: cn: attributes of the <remoteCSE> resource as defined in 9.6.19 which need be updated, with the exception of the parameters which are RO (Read Only) or WO (Write Once) in table 9.6.1.19-2. |
| Local processing on Hosting CSE | No change from the basic UPDATE procedure (section 10.1.3) |
| Information on Response message | No change from the basic UPDATE procedure (section 10.1.3) |
| Post-Conditions | The <remoteCSE> resource contains the new information |
| Exceptions | All exception described in the basic UPDATE procedure (section 10.1.3) are applicable. |

#### 10.2.1.4	Delete <remoteCSE>, aka CSE De-Registration

This flow is used for de-registering and deleting the <remoteCSE> resource with all related information.

Originator: An AE or a CSE.

Receiver: once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), the Receiver shall delete the <remoteCSE>.

Table 10.2.1.4-1 <remoteCSE> DELETE flow

| DELETE: Description |
| --- |
| Pre-Conditions | The targeted <remoteCSE> has been created (as part of the registration) |
| Information on Request message | All parameters defined in table 8.1.2.1-1 are applicable |
| Local processing on Hosting CSE | No change from the basic DELETE procedure (section 10.1.4). For <remoteCSE>, if the resource is deleted then the Hosting CSE should also delete the correspondent DNS entry, if it exists. |
| Information on Response message | No change from the basic DELETE procedure (section 10.1.4) |
| Post-Conditions | The targeted resource and all the children resources shall not exist anymore. Also all the related credential are deleted. Editor’s note: if and how credentials are cleaned is FFS, in scope of WG4. |
| Exceptions | All exception described in the basic DELETE procedure (section 10.1.4) are applicable. |

======================== END 1st CHANGE =============================