| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | Qualcomm Inc. (TIA) , LG Electronics |
| Format:* | CR against TS0001v0.3.2 including change marks |
| Date:* | 2014-02-08 |
| Contact:* | Josef Blanz (jblanz@qti.qualcomm.com) Hongbeom Ahn (hongbeom.ahn@lge.com) |
| Reason for Change/s:* | Adding a new resource type to support provisioning of CMDH related policies for setting limits to CMDH related parameters in requests issued to this CSE from local entities. |
| Clause/Sub Clause Affected* | 9.6 |
| Agenda Item:* |  |
| Work item(s): | WI-0002 Architecture |
| Document(s) Impacted* | Architecture TS 0001v0.3.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed changes into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### Rationale

### Please refer to contribution ARC-2014-0098R03-CMDH_Policies.ppt for all details on the rationale.

### The intention with this CR is to create the needed resource structures for being able to provision CMDH-related policies that govern the allowed limits for values of CMDH-related parameters in requests issued by local Originators into entities of the oneM2M architecture via Device or Application and Service Management. These resources would only be set / modified by managing entities of the Infrastructure Domain. It is expected that these resources would appear only as sub-resources to certain management object resources.

### ==================== Start Text Proposal ===================

### 9.6	Specified Resource Types

### 9.6.X	Resource Type cmdhLimits

The <cmdhLimits> resource type is used to define limits for CMDH related parameter values used in requests issued by local Originators (registered AEs or functions inside the CSE itself). When an incoming request is processed that does not comply with the limits defined by the corresponding <cmdhLimits> resource, the request can either be rejected by the CSE or the CSE can replace the CMDH-parameters that are outside the limits with appropriate values.

Figure 9.6.X-.1: Structure of <cmdhLimits> resource 
(only resource specific attributes are shown)

The resource <cmdhLimits> shall contain child resources according to their multiplicity shown in Table 9.6.X-1. A value of "0" for multiplicity indicates the child resource is optional.

Table 9.6.X-1: Child resources of <cmdhLimits> resource

| Child Resource Name of <cmdhLimits> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <cmdhParamLimits> | 1..n | See section 9.6.Y where the type of this child resource is described. |

The resource <cmdhLimits> shall contain attributes according to their multiplicity shown in Table 9.6.X-2.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.X-2: Attributes of <cmdhLimits> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aR) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| scope (sc) | 1 | RW | The scope attribute defines for which requests the limits contained in <cmdhParamLimits> child resources of this <cmdhLimits> resource shall be applied. The scope attribute is a list of zero or more local App-Inst-IDs, App-IDs, or the strings ‘limitsAE’ or ‘limitsCSE’. When an App-Inst-ID appears in the scope attribute, the CMDH parameter limits defined inside <cmdhParamLimits> child resources are applicable for requests issued by that specific Application Instance. When an App-ID appears in the scope attribute, the CMDH parameter limits defined inside <cmdhParamLimits> child resources are applicable for requests issued by any instance of Applications with that App-ID unless already covered by another <cmdhLimits> resource with a scope containing its specific App-Inst-ID. When the string ‘limitsAE’ appears in the scope attribute, CMDH parameter limits defined inside <cmdhParamLimits> child resources are applicable for all local AEs that are not listed with their specfifc App-Inst-ID or App-ID in the scope attribute of any other provisioned <cmdhLimits> resource. When the string ‘limitsCSE’ appears in the scope attribute, CMDH parameter limits defined inside <cmdhParamLimits> child resources are applicable for all requests that are originating from within the hosting CSE. Each App-Inst-ID, App-ID shall appear at most once in any of the scope attributes of any of the provisioned <cmdhLimits> resources on the hosting CSE. The strings ‘limitsAE’ or ‘limitsCSE’ shall appear exactly once in any of the scope attributes of any of the provisioned <cmdhLimits> resources on the hosting CSE. |

9.6.Y	Resource Type cmdhParamLimits

The <cmdhParamLimits> resource type is used to represent a specific set of limits for allowed values of CMDH related parameters that can be referenced in a parent <cmdhLimits> resource.

Figure 9.6.Y-.1: Structure of <cmdhParamLimits> resource 
(only resource specific attributes are shown)

The resource <cmdhParamLimits> shall contain attributes according to their multiplicity shown in Table 9.6.Y-1.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.Y-1: Attributes of <cmdhParamLimits> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aR) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| contextCondition (cC) | 0..1 | RW | Represents the Dynamic Context condition under which the CMDH parameter limits defined inside this <cmdhParamLimits> resource are applicable. If the Dynamic Context condition is met at the time of processing an incoming request, the hosting CSE shall apply the limits defined inside this <cmdhParamLimits> resource. If this attribute is not present, the CMDH parameter limits defined inside this <cmdhParamLimits> resource are applicable in case no or more than one other <cmdhParamLimits> sibling resources exist that contain a contextCondition attribute representing a condition that is met at the time of processing an incoming request. In each <cmdhLimits> parent resource, exactly one <cmdhParamLimits> child resource without ‘contextCondition’ attribute shall be provisioned. |
| limitsEventCategory (lEC) | 1 | RW | Allowed vlaues for the event category parameter (‘ec’) in a request of any of the originators indicated in the scope attribute of the parent <cmdhLimits> resource. This can be in form of a range N..M or a list of individual values or a mix of that. |
| limitsRequestExpTime (lRqET) | 1 | RW | Range of allowed values for the request expiration time parameter (‘rqet’) in a request of any of the originators indicated in the scope attribute of the parent <cmdhLimits> resource. The range is expressed in the form of a minimum and a maximum duration relative to the time of receiving the incoming request. An infinite maximum duration shall be possible. |
| limitsResultExpTime (lRsET) | 1 | RW | Range of allowed values for the result expiration time parameter (‘rset’) in a request of any of the originators indicated in the scope attribute of the parent <cmdhLimits> resource. The range is expressed in the form of a minimum and a maximum duration relative to the time of receiving the incoming request. An infinite maximum duration shall be possible. |
| limitsDelAggredation | 1 | RW | List of allowed values for the delivery aggregation parameter (‘da’) in a request of any of the originators indicated in the scope attribute of the parent <cmdhLimits> resource. |

# Comments

Inconsistent definition of this common attribute across different resource types:

Found 1, 0..n, 1..n
Should it be just 1 and contain a list of accessRight-IDs with 0 or more entries?

Inconsistent definition of this common attribute across different resource types:

Found 1, 0..n, 1..n
Should it be just 1 and contain a list of accessRight-IDs with 0 or more entries?