| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | M2M-Node-ID attribute for non-CSE Capable AEs |
| Source:* | Rajesh Bhalla, ZTE |
| Contact: | rabhalla@ztetx.com |
| Date:* | 2014-02-17 |
| Abstract:* | This contribution proposes M2M-Node-ID attribute to be included in <application> resource. Such M2M-Node-ID attribute is needed for ADN-AEs that need to be capable of being triggered by IN-CSE. Such ADN-AEs will typically be registered with IN-CSE directly. |
| Agenda Item:* | Input Contributions |
| Work item(s): | WI-0002 |
| Document(s) Impacted* | TS-0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discuss and adopt. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 1.		Background

This contribution proposes "M2M-Node-ID" attribute to be included in <application> resource. Such M2M-Node-ID attribute is needed for ADN-AEs that need to be capable of being triggered by IN-CSE. Such ADN-AEs will typically be registered with IN-CSE directly.

==============  Start of first change  ==========================

### 9.6.18	Resource Type Application

The <application> resource represents information about an Application Entity known to a given Common Services Entity.

Figure 9.6.18-1: Structure of <Application> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicitly in Table 9.6.18-1 (0 indicates the optionality of the child resource).

Table 9.6.18-1: Child resources of <Application> resource

| Child Resource Name of <Application> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See section 9.6.9. |
| [variable] | <container> | 0..n | See section 9.6.3. |
| [variable] | <group> | 0..n | See section 9.6.5. |
| [variable] | <accessRight> | 0..n | See section 9.6.2. |
| software_[i] | <mgmtObj> | 1..n | See section 9.6.10 for <mgmtObj>. This resource represents the software component (or components, if the multiplicity is greater than 1) that compose the application. This mgmtObj shall have at least the following <parameters> child resources of its “parameters” subresource: - name (multiplicity 1) - version (multiplicity 1) - state (multiplicity 1) |
| [variable] | <commCapabilities> | 1..n | Resource <commCapabilities> needs to be defined. This resource describes the communication capabilities (essentially the protocols) supported and used by the corresponding Application Entity over the Mca reference point to this CSE. |

The <Application> resource shall contain the attributes described in Table 9.6.18-2.

Table 9.6.18-2: Attributes of <Application> resource

| Attribute Name of <Application> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| labels | 0..1 | RO | See section 9.6.1 where this common attribute is described. |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (eg. “HeatingMonitoring”) |
| App-ID | 1 | RO | Application Identifier |
| App-Inst-ID | 1 | RO | When the application resource refers to an actual application instance in the executing environment. |
| M2M-Node-ID | 0..1 | RO | Applicable for ADN-AEs that register with IN-CSE, and those that need to be triggerable by IN-CSE. Globally unique ID of the ADN hosting such AE. |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is managed and understood by the application; to be passed to the application |

==============  End of first change  ==========================