| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | Addition of resource summary table |
| Source:* | Philip Jacobs, Cisco Systems Inc. |
| Contact: | phjacobs@cisco.com |
| Date:* | 2014-02-09 |
| Abstract:* | This contribution proposes to add a summary table to clause 9.6 Specified Resource Types |
| Agenda Item:* | Contributions |
| Work item(s): | WI-0002 |
| Document(s) Impacted* | TS-0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Decide whether to include the text and revise the table |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

Now that we have 20 resources defined. It would be helpful for readers to first get an introduction in clause 9.6 to resources, that includes a short resource description, related child resource types and parent resource types. The following text and table is proposed.

## 9.6	Specified Resource Types

---------------------------Start of modification 1 -------------------------

Table 9.6-1 introduces the defined resource types. Details of each resource type follow in the remainder of this clause.

Table 9.6-1 Resource Summary

| Resource Type | Short description | Child resource types | Parent resource types |
| --- | --- | --- | --- |
| accessRight | Permissions for entities’ access modes | subscription | Application, remoteCSE |
| application | Represents information about an AE | subscription, container, group, accessRight, software, commCapabilities | remoteCSE |
| chargeableEvent | Defines the charging policy for a chargeable event |  | chargingPolicy |
| chargingPolicy | Stores charging related policies | chargeableEvent |  |
| chargingRule | Defines rules for charging purpose |  |  |
| container | Shares data instances among entities | container, instance, subscription, | application, container, remoteCSE |
| delivery | Forwards requests from CSE to CSE |  |  |
| execInstance | Represents a successful instance of mgmtCmd |  | execInstances |
| execInstances | Execution instances of the same management command | execInstance | mgmtCmd |
| group | Represents a group of resources | members | Application, remoteCSE |
| instance | Data instance in a container |  | container |
| locationPolicy | Obtains/manages geographical location |  |  |
| members | Virtual resource target for group requests |  | group |
| mgmtCmd | Method to execute management procedures / model commands and RPCs for existing protocols | execInstances |  |
| mgmtObj | Represents individual management functions | parameters | remoteCSE |
| m2mServiceSubscription | Data pertaining to the M2M Service Subscription |  |  |
| node | Represents specific Node information | schedule, others | application (in ADN) |
| parameters | Parameters/attributes for management purposes | parameters | mgmtObj, parameters |
| remoteCSE | Represents a remote CSE registered to the local CSE | application, container, group, accessRight, subscription, mgmtObj |  |
| request | Expresses/access context of an issued Request |  |  |
| schedule | Contains scheduling information for delivery of messages |  | node, subscription |
| subscription | Information of subscribed-to resources | schedule | accessRight, application, container, group, remoteCSE |

Editor’s Note: This table was based upon revision 0.3.2 and may be missing information from subsequent agreed contributions. It is expected to be updated as we further define resources.

---------------------------End of modification 1 -------------------------