| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC |
| Title:* | Call Flows for Service Charging and Accounting (SCA) |
| Source:* | InterDigital, Telecom Italia |
| Contact: | Guang Lu (Guang.Lu@InterDigital.com); Enrico Scarrone <enrico.scarrone@telecomitalia.it> |
| Date:* | <2014-2-18> |
| Abstract:* | This document defines call flows for the service layer Charging and Account (SCA) CSF |
| Agenda Item:* | 6 - Contributions |
| Work item(s): |  |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Rationale

This contribution reflected the converged view from offline discussions about the use of resources for  the SCA functionalities.

The service layer should be able to provide “charging” as a service to applications, i.e. provides statistics that can be used by applications for charging purposes. Two resources are defined to support this feature: <statsConfig> and <statsCollect>. This contribution defines the call flows for these resources.

2. Proposed Changes

------------------------------------------BEGINNING OF CHANGE 1 ----------------------------------------

10.2.X  Service Charging and Accounting Procedures

10.2.X.1 Introduction

This section is informative and provides an use case example to explain how the Infrastructure Node provides

statistics for applications using the <statsConfig> and <statsCollect> resources as defined in clause 9.6.15.

10.2.X.1.1 Service Event-based Statistics Collection for Applications

Figure 10.2.X.1-2 shows an example of service layer event-based charging based on the Infrastructure Node.

Step 1-2: A statistics colloection resource called <statsConfigSCA1> was created at the IN-CSE by a billing application. Note that the <statsConfig> can also be provisioned. In this use case, the <statsConfigSCA1> has the <eventConfig> sub-resource. For this specific use case, the <eventConfig> can be set as following: The “eventID” is set with a unique ID to differentiate from other chargeable events. The “eventType” defines what event will trigger the generation of service statistics collection record and is set to “Data Operation” for this case. “eventStart” and “eventEnd” apply to timer based event so they will not be included in this event. “transactionType” will be “RETRIEVE”. “dataSize” does not apply so it is not included.

Step 3-5: In this example, AE1 already registered to IN-CSE. IN-CSE can make the statistics collection configuration accessible by application. Based on the <statsConfigSCA1>, AE1 creates a statistics collection trigger for itself, stored in <statsCollectAE1>. AE1 will fill in the information for the collection rule. For example, it fills the “collectingEntityID” with the App-ID of AE1, and the “collectedEntityID” empty, which means to collect for any entities. “status” is set to “Active”. The “statsModel” is “event-based”. The “subscriberID” is set to the M2M-Sub-ID for AE1. The “eventID” is set with the same ID value as the “eventID” in the  <statsConfigSCA1>.  This event collection trigger can be saved at the IN-CSE and IN-CSE will assign a unique ID in attribute “statsCollectID”.

Step 6-8: When the configured event happens, i.e. when AE2 performed a RETRIEVE operation to the data owned by AE1 at IN-CSE, the event is recorded by IN-CSE. The SCA CSF at IN-CSE generates a service statistics collection record that sends it to AE1. AE1 can choose to use such information for its own billing.

Step 9: The billing application can update or retrieve the charging policies and collection scenarios that it has the access right.

Figure 10.2.X.1-2: Event-based Statistics Collection for Applications

10.2.X.2 CREATE <statsConfig>

This procedure shall be used for the Originator to establish a set of configurations for statistics collection at the Receiver.

The configuratoins shall be stored at the  <statsConfig> resource and each instance of the <statsConfig> resource shall represent a specific configuration.

Editor’s Note: The texts below provide examples on how to populate the sub-resources and attributes. Many of the attributes are enumeration type and the exact values will be defined in Stage 3.

Originator: The Originator shall be an application or the IN-CSE that wants to set up the statistics collection configurations. According to the definition of the <statsConfig> , the Originator shall:

- for Event based collection provide the sub-resource <eventConfig>

This sub-resource is used to define different events to be collected, each identified by a unique “eventID”.

eventID: The “eventID” shall uniquely identify an event. The Originator may provide a value in the Request. The Receiver shall verify whether the ID is unique or not, and if not, provides a new value.

eventType: The “eventType” is a mandatory attribute. The Originator shall provide an eventType. An example of an eventType is “Data Operation”, which means that chargeable events information recording is triggered when the charged entity conducts a data operation. “Data Operation” can be further refined by the “transactionType” attribute.

eventStart: The “eventStart” is an optional attribute. The Originator shall provide a start time for the event only if the “eventType” is set to “Timer based”.

eventEnd: The “eventEnd” is an optional attribute. The Originator shall provide an end time for the event only if the “eventType” is set to “Timer based”.

transactionType: The “transactionType” is an optional attribute. Examples of “transactionType” can be “CREATE”, “RETRIEVE”.

dataSize: The “dataType” is an optional attribute. The Originator shall provide a value for it only if the “eventType” is set to “Storage based”.

Receiver: The Receiver shall be an IN-CSE containing the SCA CSF. The Receiver shall validate whether the Originator has proper permissions for creating a <statsConfig> resource, and whether the values provides in the Request message are valid. Upon successful validation, the Receive shall create a new <statsConfig> resource with the provided values.

Table 10.2.x.2 CREATE Call Flow

|  | Description |
| --- | --- |
| Call flow type | CREATE |
| Pre-conditions | Originator needs to create a <statsConfig> resource at the Receiver |
| Information on Request message | op: Create fr: ID of the Originator to: URI of the parent of the target resource to be created cn: contain the resource representation of <statsConfig> The Originator can provide the <eventConfig> sub-resource to enable event-based configuration for statistics collection The Originator may specify other Optional parameters as discussed in [section 8.1.2 Request] |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

10.2.X.3. RETRIEVE <statsConfig>

The RETRIEVE call flow shall be used for the Originator to retrieve the existing <statsConfig> resource from the Receiver.

Originator: The Originator shall be an application that is allowed to retrieve configuration information available for application from the SCA CSF within a CSE.

Receiver: The Receiver shall be the IN- CSE containing the SCA CSF. The Receiver shall verify if the Originator has the READ permission on the <statsConfig> resource targeted. Upon successful validation, the Receiver CSE shall respond to the Originator with the resource representation.

Table 10.2.x.3-1 RETRIEVE Call Flow

|  | Description |
| --- | --- |
| Call flow type | RETRIEVE |
| Pre-conditions | Originator needs to retrieve the <statsConfig> resource at the Receiver |
| Information on Request message | op: Retrieve fr: ID of the Originator to: URI of the <statsConfig> resource or its attribute or sub-resource to be retrieved cn: void The Originator may specify other Optional parameters as discussed in [section 8.1.2 Request] |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

10.2.X.4. UPDATE <statsConfig>

An UPDATE procedure on the <statsConfig> resource is used for the Originator to update charging related policies at the Receiver.

Originator: The Originator shall be the application that created the <statsConfig> resource. The same application shall be able to update the resource.

Receiver: The Receiver shall be a CSE containing the SCA CSF. The Receiver shall check if the Originator has the WRITE permission to update the addressed resource.

Table 10.2.x.4-1 UPDATE Call Flow

|  | Description |
| --- | --- |
| Call flow type | UPDATE |
| Pre-conditions | The Originator needs to update the charging policies that it established at the Receiver by using the <statsConfig> resource |
| Information on Request message | op: Update fr: ID of the Originator to: URI of the <statsConfig> resource or its attribute or sub-resource to be updated cn: the Originator provides the sub-resource or attributes to be updated The Originator can update attributes under <eventConfig> to update event-based configuration for statistics collection The Originator may specify other Optional parameters as discussed in [section 8.1.2 Request] |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

10.2.X.5. DELETE <statsConfig>

Originator: The Originator shall be the application that created the <statsConfig> resource.

Receiver: The Receiver shall be a CSE containing the SCA CSF.

Table 10.2.x.5-1 DELETE Call Flow

|  | Description |
| --- | --- |
| Call flow type | DELETE |
| Pre-conditions | Originator needs to DELETE the <statsConfig> resource at the Receiver |
| Information on Request message | op: Delete fr: ID of the Originator to: URI of the <statsConfig> resource to be deleted cn: void The Originator may specify other Optional parameters as discussed in [section 8.1.2 Request] |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

10.2.X.6  CREATE <statsCollect>

This procedure shall be used for the Originator to establish collection scenarios at the Receiver.

The collection scenarios are stored at the  <statsCollect> resource. Multiple collection scenarios can be created based on one <statsConfig>.

Originator: The Originator shall be an application that wants to set up the collection scenarios to the SCA CSF in a CSE. According to the definition of the <statsCollect>  resource, the Originator shall populate the attributes defined for the <statsCollect> resource except for “statsCollectID”. (see clause 9.6.15.3). The “statsCollectID” shall be unique in the same service provider domain. To ensure the uniqueness, the IN-CSE shall create the statsCollectID.

Here are other attributes in the <statsCollect> resources:

collectingEntityID: The “collectingEntityID” is a mandatory attribute. The Originator shall provide the ID as defined in  clause 7.1 to identify the entity that charges.

collectedEntityID: The “collectedEntityID” is a mandatory attribute. The Originator shall provide the ID as defined in  clause 7.1 to identify the entity that being charged.

status: The “status” is a mandatory attribute. The Originator shall set the value for this attribute to specify the status of the rule. Examples of values can be “ACTIVE”, “INACTIVE”.

statsModel: The “statsModel” is a mandatory attribute. The Originator shall set the value to indicate a collection model. Examples of values can be “subscriber-based”, “event-based”.

subscriberID: The “subscriberID” is a mandatory attribute. It is the service subscriber ID for the collected entity. The Originator shall provide the “M2M-Sub-ID” as defined in clause 7.1.

collectPeriod: The “collectPeriod” is an optional attribute. It applies to the subscriber-based charging model. The Originator shall provide a value of the information recording collection period. An example of the value can be “monthly”.

eventID: The “eventID” is an optional attribute. The Originator shall provide a value only if the “statsModel” is “event-based”. The Originator shall provide the eventID that is defined in the resource <statsConfig>. Since there can be many different chargeable events defined by different charging policies, the eventID uniquely identifies the specific chargeable event for this charging rule.

Receiver: The Receiver shall be an IN-CSE containing the SCA CSF. The Receiver shall validate whether the Originator has proper permissions for creating a <statsCollect> resource. Upon successful validation, create a new <statsCollect> resource with the provided attributes. The IN-CSE shall also create a unique “statsCollectID”.

Once a <statsCollect> is crated and the “status” is “ACTIVE, the SCA CSF in the IN-CSE shall generate service statistics collection record when the conditions defined by the rules are met.

Table 10.2.x.6-1 CREATE Call Flow

|  | Description |
| --- | --- |
| Call flow type | CREATE |
| Pre-conditions | Originator needs to create a <statsCollect> resource at the Receiver |
| Information on Request message | op: Create fr: ID of the Originator to: URI of the parent of the target resource to be created cn: contain the resource representation of <statsCollect> The Originator may specify other Optional parameters as discussed in [section 8.1.2 Request] |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

10.2.X.7  RETRIEVE <statsCollect>

The RETRIEVE call flow shall be used for the Originator to retrieve the existing <statsCollect> resource from the Receiver.

Originator: The Originator shall be an application that is allowed to retrieve the charging rule information from the SCA CSF within a CSE.

Receiver: The Receiver shall be the IN- CSE containing the SCA CSF. The Receiver shall verify if the Originator has the READ permission on the <statsCollect> resource targeted. Upon successful validation, the Receiver CSE shall respond to the Originator with the resource representation.

Table 10.2.x.7-1 RETRIEVE Call Flow

|  | Description |
| --- | --- |
| Call flow type | RETRIEVE |
| Pre-conditions | Originator needs to retrieve the <statsCollect> resource at the Receiver |
| Information on Request message | op: Retrieve fr: ID of the Originator to: URI of the <statsCollect> resource or its attribute to be retrieved cn: void The Originator may specify other Optional parameters as discussed in [section 8.1.2 Request] |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

10.2.X.8 UPDATE <statsCollect>

An UPDATE procedure on the <statsCollect> resource is used for the Originator to update charging related policies at the Receiver.

Originator: The Originator shall be the application that created the <statsCollect> resource. The same application shall be able to update the resource.

Receiver: The Receiver shall be a CSE containing the SCA CSF. The Receiver shall check if the Originator has the WRITE permission to update the addressed resource.

Table 10.2.x.8-1 UPDATE Call Flow

|  | Description |
| --- | --- |
| Call flow type | UPDATE |
| Pre-conditions | The Originator needs to update the collection scenarios that it established at the Receiver by updating the <statsCollect> resource |
| Information on Request message | op: Update fr: ID of the Originator to: URI of the <statsCollect> resource or its attribute to be updated cn: the Originator provides the attributes to be updated The Originator may specify other Optional parameters as discussed in [section 8.1.2 Request] |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

10.2.X.9. DELETE <statsCollect>

Originator: The Originator shall be the application that created the <statsCollect> resource.

Receiver: The Receiver shall be a CSE containing the SCA CSF.

Table10. 2.X.9-1 DELETE Call Flow

|  | Description |
| --- | --- |
| Call flow type | DELETE |
| Pre-conditions | Originator needs to DELETE the <statsCollect> resource at the Receiver |
| Information on Request message | op: Delete fr: ID of the Originator to: URI of the <statsCollect> resource to be deleted cn: void The Originator may specify other Optional parameters as discussed in [section 8.1.2 Request] |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

------------------------------------------END OF CHANGE 1 ----------------------------------------

------------------------------------------BEGINNING OF CHANGE 2 -----------------------------

10.X.X.X. Service Statistics Collection Record

The following table defines the Information Elements can be included in a Service statistics collection record.

The contents of each Service statistics collection record are decided by the specific collection scenario that

triggered the information recording.

Editor’s Note: More contents can be added when more chargeable events are specified.

Table x.x.: Information Elements for Service Statistics Collection Record

| Information Element | Mandatory / optional | Description |
| --- | --- | --- |
| statsCollectID | M | It is the unique ID that identifies a specific statistics collection scenario, which triggers information recording for a specific event. |
| collectingEntityID | M | This is the unique ID of the entity that collects the statistics. It can be an application ID (app-ID) or CSE-ID |
| collectedEntityID | M | This is the unique ID of the entity whose service layer operation statistics are being collected. It can be an application ID (app-Inst-ID) or CSE-ID |
| subscriberID | M | The M2M service subscription ID M2M-Sub-ID if the collected entity |
| event | O | This indicates a specific event type in each record, such as timer based, data operation, storage triggering. It is only present if the statModel is “event based” |
| eventStart | O | The start time for the recording the M2M event record |
| eventEnd | O | The end time for the recording the M2M event record |
| transactionType | O | Specifies the detailed type of a transaction, such as CREATE, RETRIEVE, etc. |
| dataSize | O | Storage Memory in Kbytes, where applicable, to store data associated events with container related operations |
| Vendor Specific Information | O | Defines Vendor specific information |