| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#9 |
| Title:* | Aggregation of notification |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin |
| Date:* | 2014-1-8 |
| Abstract:* | The contribution describe the procedures for subscription through group and how group aggregate notifications from multiple members. |
| Agenda Item:* | TBD |
| Work item(s): | WI0001 |
| Document(s) Impacted* | TS0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into the TS if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

##### 10.3.3.10	Subscribe and Un-Subscribe <Members> of a group

This procedure shall be used for receiving information about modifications of all member resources belonging to an existing <group> resource.

Originator: shall request to create a subscription resource under all member resources belonging to an existing <group> resource by using a CREATE verb. The request shall address the child resource <members> of the specific <group> resource of a group hosting CSE appended with the ID of the <subscription> resource to be created to subscribe to the modifications of all member resources. The request shall include an empty aggregationURI attribute if the originator wants the group hosting CSE to aggregate the notifications. The request shall include the required information and may include the optional information as described in subscription management clause 10.3.8. The originator may be an AE or a CSE.

Group Hosting CSE: For the subscribe/un-subscribe procedure, the Group Hosting CSE shall:

Check if the originator has WRITE permission in the <accessRight> resource referenced by the membersAccessRightID in the group resource. In the case membersAccessRightID is not provided the access right defined for the group resource shall be used.

If the subscription resource in the request contains an aggregationURI attribute, assign an URI to the aggregationURI of the subscription resource. In case the aggregationURI attribute has a value, maintain the mapping of the generated aggregationURI and the former aggregationURI.

Upon successful validation, obtain the URIs of all member resources from the attribute membersList of the addressed <group> resource and fan out requests to the member hosting CSEs addressing the obtained URIs appended with the ID of the <subscription> resource to be created.

If the group hosting CSE determines that multiple member resources belong to one CSE according to the URIs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group hosting CSE creating a <group> resource on the member hosting CSE to collect all the members on that member hosting CSE.

After receiving the responses from the member hosting CSEs, respond to the originator with the aggregated results and the associated memberIds.

Member Hosting CSEs: For the subscribe/un-subscribe procedure, the Member Hosting CSE shall treat the request received from the group hosting CSE as a normal SUBSCRIBE request on the addressed member resource as if it comes from the original originator. Therefore the member hosting CSE shall:

Check if the original originator has the READ permission on the member resource.

Upon successful validation, perform the subscribe procedures for the corresponding type of member resource as described in clause 10.3.8.2.

Send the corresponding response to the group hosting CSE.

Table 10.2.x.10: bulk Subscribe/Un-subscribe

|  | Description |
| --- | --- |
| Call flow type | CREATE |
| Pre-conditions | none |
| Information on Request message | op: C fr: Identifier of the AE or CSE that initiates the request. to: The URI of the <members> resource appended with the ID of the <subscription> resource to be created. |
| Local processing on Hosting CSE | Fan out requests to each member hosting CSE addressing the obtained URI from the attribute members of the group resource appended with the ID of the <subscription> resource to be created. Generate request identifier and include the identifier in the fanned out requests in the case of sub groups. |
| Information on Response message | Converged responses from member hosting CSEs. |
| Post-condition | none |
| Exceptions | Same request with identical request identifier received. Originator does not have the access right to access the bulk resource. |

##### 10.3.3.11	Aggregate the notifications by group

This procedure is used for the group hosting CSE to aggregate the notifications from member hosting CSEs and forward the aggregated notification to the subscriber.

Member Hosting CSEs: Whenever the resource that is subscribed-to is modified in a way that matches the policies as is specified in clause 10.3.9, notification needs to be sent to the subscribe, the Member Hosting CSE shall:

If the subscription resource contains aggregationURI, notify the subscriber at the aggregationURI and include the notificationURI in the notification. Otherwise, notify at the URI represented by the attribute notificationURI.

Group Hosting CSE: For the notification procedure, the Group Hosting CSE shall:

On receiving the notifications from the member hosting CSEs at the aggregationURI, validate if the notification is sent from its member resource and contain a notificationURI attribute.

Upon successful validation, aggregate the notifications which have the same notificationURI address of a single subscriber. Send the aggregated notification to the subscriber according to the notificationURI in the notification. In the case the addressed group is the member of another group through which the subscription is created the notification shall be sent according to the mapping of the aggregationURI of the two group hosting CSEs.

Editor’s Note: The policy defined in <subscription> resource may not be still valid after the aggregation by group. How to guarantee the validity of the policies is FFS together with the way to guarantee the validity of the policies in store and forward occasions.

Wait for the response. After receiving the response, split the response and respond the member hosting CSE separately.

The group hosting CSE may stop aggregating the notifications when the expirationTime of the corresponding subscription expires.

Subscriber: shall treat every notification extracted from the aggregated notification as a separate notification received from the subscribed resource and generate corresponding responses. The subscriber shall aggregate the responses to these notifications and send the aggregated response to the group hosting CSE.