| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#9 |
| Title:* | Annex for management resources |
| Source:* | Huawei Technologies Co., Ltd. LG Electronics |
| Contact: | Jiaxin Yin, yinjiaxin@huawei.com Seungkyu Park, seungk.park@lge.com |
| Date:* | 2014-2-8 |
| Abstract:* | The contribution adds an annex for the management related resources. |
| Agenda Item:* | TBD |
| Work item(s): | WI0002 |
| Document(s) Impacted* | TS0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the texts to TS0001 if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# Annex C: (Normative) <mgmtObj> Resource Instances Description

## C.1	oneM2M Management Functions

This clause describes the management functions supported by oneM2M. These functions are fulfilled by defining instances of <mgmtObj> resources. The instances are resources of <mgmtObj> type with specific designing to support different management capabilities through operations defined by oneM2M. The instances are service layer information models for the purpose of management. The instances can then be used within the M2M service layer or they can be further mapped to existing management technologies such as OMA DM, OMA LWM2M and BBF TR-069 to enable the management of devices with OMA or BBF compliant management clients.

NOTE: The resource instances defined in this section are all of type <mgmtObj>. The instances are distinguished by attribute mgmtDefinition. The names of the instances are not fixed.

## C.2	Resource Firmware

Figure C.2-1: Structure of Firmware resource 
(only resource specific attributes are shown)

The Firmware resource shall contain the attributes described in Table C.2-2.

Table C.2-2: Attributes of Firmware resource

| Attribute Name of <mgmtObj> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | Has fixed value “Firmware” to indicate the resource is for firmware management. |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |
| Version | 1 | RW | The version of the firmware. |
| Name | 1 | RW | The name of the firmware to be used on the device. |
| URL | 1 | RW | The URL from which the firmware image can be downloaded. |
| Update | 1 | RW | The action that downloads and installs a new firmware in a single operation. |
| UpdateStatus | 1 | RO | Indicates the status of the update. |

Editor’s Note: The state machine diagram is to be added according to section 6.2.4.2.3. The names of the attributes also need to be aligned with the wording in the same section.

## C.3	Resource Software

Figure C.3-1: Structure of Software resource 
(only resource specific attributes are shown)

The Software resource shall contain the attributes described in Table C.3-2.

Table C.3-2: Attributes of Software resource

| Attribute Name of <mgmtObj> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | Has fixed value “Software” to indicate the resource is for software management. |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |
| Version | 1 | RW | The version of the software. |
| Name | 1 | RW | The name of the software to be used on the device. |
| URL | 1 | RW | The URL from which the software package can be downloaded. |
| Install | 1 | RW | The action that downloads and installs new software in a single operation. |
| InstallStatus | 1 | RO | Indicates the status of the install. |
| Activate | 0..1 | RW | The action that activates software previously installed. |
| Deactivate | 0..1 | RW | The action that deactivates software. |
| ActiveStatus | 0..1 | RW | The status of active or deactivate action. |

## Editor’s Note: The state machine diagram is to be added according to section 6.2.1.2.3. The names of the attributes also need to be aligned with the wording in the same section.

## C.4	Resource Memory

Figure C.4-1: Structure of Memory resource 
(only resource specific attributes are shown)

The Memory resource shall contain the attributes described in Table C.4-2.

Table C.4-2: Attributes of Memory resource

| Attribute Name of <mgmtObj> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | Has fixed value “Memory” to indicate the resource is for memory management. |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |
| memAvailable | 1 | RW | The current available amount of memory. |
| memTotal | 1 | RW | The total amount of memory. |

## C.5	Resource AreaNwkInfo

Figure C.5-1: Structure of AreaNwkInfo resource 
(only resource specific attributes are shown)

The AreaNwkInfo resource shall contain the attributes described in Table C.5-2.

Table C.5-2: Attributes of AreaNwkInfo resource

| Attribute Name of <mgmtObj> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | Has fixed value “AreaNwkInfo” to indicate the resource is for area network information. |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |
| areaNwkType | 1 | RW | The areaNwkType is an implementation-chosen string that indicates the type of M2M Area Network. |
| listOfDevices | 1 | RW | Indicates the list of devices in the M2M Area Network. The attribute contains references to AreaNwkDeviceInfo resource. From listOfDevices, the topology of the area network can be discovered and retrieved. |

## C.6	Resource AreaNwkDeviceInfo

Figure C.6-1: Structure of AreaNwkDeviceInfo resource 
(only resource specific attributes are shown)

The AreaNwkDeviceInfo resource shall contain the attributes described in Table C.6-2.

Table C.6-2: Attributes of AreaNwkDeviceInfo resource

| Attribute Name of <mgmtObj> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | Has fixed value “AreaNwkDeviceInfo” to indicate the resource is for area network device information. |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |
| devId | 1 | RW | Indicates the id of the device. It could be the id of the hardware or nodeId. |
| devType | 1 | RW | Indicates the type of the device. The attribute also indicates the functions or services that are provided by the device. Examples include temperature sensor, actuator, Zigbee coordinator or Zigbee router. |
| areaNwkId | 1 | RW | The reference to an AreaNwkInfo resource which this device associates with. |
| sleepInterval | 0..1 | RW | The interval between two sleeps. |
| sleepDuration | 0..1 | RW | The time duration of each sleep. |
| status | 0..1 | RW | The status of the device (sleeping or waked up). |
| listOfNeighbors | 1 | RW | Indicates the neighbour devices of the same area network. When modified, the connection relationship of the devices shall be modified accordingly. |

# Text boxes

description

objectPath

objectID

mgmtDefinition

[Firmware]

Version

Name

URL

Update

UpdateStatus

1

0..1

0..1

0..1

1

1

1

1

1

[Software]

mgmtDefinition

objectID

objectPath

description

Version

Name

URL

Install

InstallStatus

1

0..1

0..1

0..1

1

1

1

1

1

Activate

Deactivate

ActivateStatus

1

1

1

[Memory]

mgmtDefinition

objectID

objectPath

description

memAvailable

memTotal

0..1

1

0..1

1

0..1

0..1

0..1

1

1

1

sleepInterval

listOfDevices

areaNwkType

description

objectPath

objectID

mgmtDefinition

[AreaNwkInfo]

0..1

0..1

1

1

[AreaNwkDeviceInfo]

sleepDuration

areaNwkId

deviceType

deviceId

description

objectPath

objectID

mgmtDefinition

0..1

0..1

1

1

1

0..1

0..1

status

listOfNeighbors

0..1

1