| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#9 |
| Title:* | Change to moAttribute |
| Source:* | Huawei Technologies Co., Ltd. China United Network Communications Group Company Limited |
| Contact: | Jiaxin Yin, yinjiaxin@huawei.com Changwei Hu, hucw5@chinaunicom.cn |
| Date:* | 2014-1-23 |
| Abstract:* | The contribution modifies moAttribute to make it clearer. |
| Agenda Item:* | TBD |
| Work item(s): | WI0001 |
| Document(s) Impacted* | TS0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

### 9.6.10	Resource Type mgmtObj

The mgmtObj resource contains management data which represents individual M2M management functions. It represents a general structure to map to external management technology (e.g. OMA DM, BBF TR-069 and LWM2M) data models.

Figure 9.6.10-1: Structure of <mgmtObj> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicitly in Table 9.6.10-1 (0 indicates the optionality of the child resource).

Table 9.6.10-1: Child resources of <mgmtObj> resource

| Child Resource Name of <mgmtObj> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <parameters> | 0..n | See section 9.6.11. Collects multiple parameters or attributes for management purpose. A <parameters> resource can have zero or more other <parameters> sub0resources so as to form hierarchical structure, i.e. the management data for this specific <mgmtObj>. Such structure helps to import existing management objects as defined in OMA DM, BBF TR-069, LWM2M, or any other technology. |

The <mgmtObj> resource shall contain the attributes described in Table 9.6.10-2.

Table 9.6.10-2: Attributes of <mgmtObj> resource

| Attribute Name of <mgmtObj> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | Indicates specific device management functionalities. Editor’s Note: Description needed. |
| objectID | 0..1 | WO | Contains a URN that uniquely identifies the external management technology data model used for this <mgmtObj> resource as well as the managed function and version it represents. This attribute shall be provided during the creation of the <mgmtObj> resource and shall not be modifiable afterwards. This is mandatory for the <mgmtObj>, for which the data model is not specified by oneM2M but mapped from external management technology data model specified in other device management protocols (e.g. OMA-DM, BBF TR-069 and LWM2M). |
| objectPath | 0..1 | WO | Contains the local path of the external management object instance on the managed entity which is represented by the <mgmtObj> resource in the hosting CSE. This attribute shall be provided during the creation of the <mgmtObj>, so that the hosting CSE can correlate the created <mgmtObj> with the external management object instance on the managed entity for further management operations. It shall not be modifiable after creation. The format of this attribute shall be a local external management object path in the form as specified by existing management protocols. (e.g. "./anyPath/Fw1" in OMA DM, "Device.USBHosts.Host.3." in BBF TR-069). |
| oa_[attributeName] | 0..n | RW | Each oa_[attributeName] is mapped from a leaf node of a hierarchical structured management object (including oneM2M data model and the existing management data models) based on the mapping rules below the table. Oa stands for object attribute. |
| description | 0..1 | RW | Text format description of mgmtObj. |

When mapping resources from management technologies to a corresponding <mgmtObj> resource, the following rules shall apply:

- The root resource of external management objects maps to the <mgmtObj> resource

- For child resource of the root resource of specific technology:

- Rule1:  If the child external management object cannot have child external management object, the external management object maps to the oa_[attributeName]  attribute of the <mgmtObj> resource with the same resource name;

- Rule2:  If the child external management object can have another child external management object, the external management object maps to the <parameters> resource with the same resource name.

- For the external management object that is mapped to the <parameters> resource, the child external management object of the external management object are mapped to the oa_[attributeName]  attribute or to the <parameter> resource according to the Rule1 and Rule2.

### 9.6.11	Resource Type parameters

Figure 9.6.11-1: Structure of <parameters> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicitly in Table 9.6.11-1 (0 indicates the optionality of the child resource).

Table 9.6.11-1: Child resources of <parameters> resource

| Child Resource Name of <parameters> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <parameters> | 0..n | See section 9.6.11 |

The <parameters> resource shall contain the attributes described in Table 9.6.11-2.

Table 9.6.11-2: Attributes of <parameters> resource

| Attribute Name of <parameters> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| accessRightID | 1 | RW | See section 9.6.1 where this common attribute is described |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| objectID | 0..1 | WO | See Table 9.6.10.1 |
| objectPath | 0..1 | WO | See Table 9.6.10.1 |
| oa_[attributeName] | 0..n | RW | See Table 9.6.10.1 |
| description | 0..1 | RW | Text format description of mgmtObj. |