| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC |
| Title:* | M2M Service Subscription Resource Type |
| Source:* | Alcatel-Lucent, LG Electronics |
| Contact: | Omar Elloumi, Alcatel-Lucent, omarelloumi@alcatel-lucent.com Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-02-18 |
| Abstract:* | This contribution proposes <m2mServiceSubscription> resource type and its sub-resource <nodeInfo> resource type procedure. |
| Agenda Item:* | ARC |
| Work item(s): | WI 0002 |
| Document(s) Impacted* | Technical Specification – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes <m2mServiceSubscription> resource type and its sub-resource <nodeInfo> resource type.

-----------------------------------FIRST CHANGE----------------------------

#### 6.5.1.1	Public Domain Names and CSEs

To enable the usage of public DNSs as described above, there is a need for a naming convention for public names for CSEs.  This naming convention facilitates the creation of the necessary entries of the public domain names of CSEs in the DNS by the infrastructure node.

CSEs public domain names shall be a sub-domain of the Infrastructure Node public domain name. This naming convention allows the Infrastructure Node to include the needed DNS entry corresponding to the CSE to whom access from other domains is allowed. This would typically occur when the CSE registers with the Infrastructure Node, subject to policies, or administratively. The Infrastructure Node shall also have a public domain name.

Accordingly, the structure of the public domain of the CSEs in any node (Middle Node/Application Service Node) shall follow the following naming convention, which relies on the CSE identifier (CSE-ID) as part of the naming convention to facilitate the entry creation:

    - Infrastructure Node public domain name: <Infrastructure Node CSE Identifier>.<M2M Service Provider domain name>

    - CSE Middle Node public domain name: <Middle Node CSE Identifier>.<Infrastructure Node public domain name>

    - CSE Application  Service Node  public domain name: <Application Service Node CSE Identifier>.<Infrastructure Node public domain name>

Both the CSE Middle Node and the CSE Application Service Node are sub-domains of the Infrastructure Node.

The A/AAAA records in the DNS, as per [i.5], [i.6], and [i.10] shall consist of the public domain name of the CSE and the IP address of the M2M Infrastructure Node, since the M2M Infrastructure Node is the entry point of the M2M Service Provider domain name where it belongs to.

Editors Note: The population of the A/AAAA records are FFS and to be elaborated

#### 6.5.1.1	M2M Service Subscription

The M2M Service Subscription defines the technical part of the contract between an M2M Subscribers (typically an Application provider) and an M2M Service Provider. Each M2M Service Subscription shall have a unique identifier, the M2M-Sub-ID, as specified in 7.1.9. An M2M Service Subscription establishes a link between one or more AEs; one or more M2M Nodes, one or more M2M Service roles as well as subscriber defined groups used for Access Rights.

Editor’s note: change Access Right to Access Control Policy if such a recommendation is made by WG4

An M2M Service is the marketable service offered to M2M service subscriber (organizations or individuals). Examples of services include Device Management, Location, Data Exchange, etc.

In each M2M Service, one or multiple M2M Service role(s) shall be defined by the M2M Service Provider. M2M Service role is defined as a set of privileges pertaining to a resource types which are associated with M2M Service. The M2M Subscriber subscribes one or multiple roles within the M2M Services, which M2M Subscribers are interested in.

The set of M2M Services and M2M Service roles supported in this specification is depicted in Annex X(the list of roles is provided as informative).

It shall also be possible for an M2M Service Provider to define his own services and roles.

An M2M Service Subscription governs for an M2M subscription, the M2M nodes where AEs can reside and execute. It also governs the M2M Service roles as well as subscriber defined groups used for Access Right.   An example of the Subscriber defined group is all node applications within this service subscription with app-ID set to a specific value. Access Right resource configuration shall be in line with M2M Service Subscription. For Authorization of accessing the resource, Access Right is applied. Details of configuring Access Right are FFS.

How to authorize the request operation based on M2M Service Subscription resource will be defined in section FFS of TS-0003 [TS-0003].

An M2M Service Subscription shall be used for the following purposes:

- Serve as a basis for authorization for resource operations

- Serve as the basis for charging.

- Identify which nodes are part of this M2M Service Subscription

-----------------------------------END FIRST CHANGE------------------------

---------------------------------------SECOND CHANGE----------------------------

### 7.1.8	M2M External Identifier (M2M-Ext-ID)

This is an identifier used by an M2M Service Provider (M2M SP) when services targeted to a CSE, identified by a CSE-ID, are requested from the Underlying Network.

The M2M External Identifier allows the Underlying Network to identify the M2M Device associated with the CSE-ID for the service request. To that effect, the Underlying Network maps the M2M-Ext-ID to the Underlying Network Identifier it allocated to the target M2M Device. In addition, the M2M SP shall maintain the association between the CSE-ID, the M2M-Ext-ID and the identity of the Underlying Network.

Both pre-provisioned and dynamic plug and play association between the CSE-ID with the M2M-Ext-ID should to be supported.

NOTE: There shall be 1:1:1 mapping between M2M-Ext-ID, the identity of the Underlying Network and the CSE-ID. Hence an M2M SP interworking with multiple Underlying Networks shall have a different M2M-Ext-IDs associated with the same CSE-ID, one per Underlying Network and  shall select the appropriate M2M-Ext-ID for any service request it initiates towards an Underlying Network.

NOTE: The mapping by the Underlying Network of the M2M-Ext-ID to the M2M Device is access network specific.

Editor's Note:  The method for dynamic plug-and-play association of M2M-Ext-ID and the 3GPP Underlying Network Identifier is FFS.

Editor's Note: Define "identity of the Underlying Network".

### 7.1.9	M2M Service Identifier (M2M-Serv-ID)

The M2M-Serv-ID is an identifier of a M2M Service offered by an M2M Service Provider. It is an essential part of the M2M Service Subscription which stores a set of M2M-Serv-ID pertaining to the set of subscribed services. Beyond the set of services depicted in this specification it shall be possible for an M2M Service Provider to offer other services. Those will be identified by means of Service Provider specific identifiers.

-----------------------------------END SECOND CHANGE-------------------------

--------------------------------------THIRD CHANGE----------------------------

### 9.6.20	Resource Type m2mServiceSubscription

This resource represents an M2M Service Subscription. It is used to represent all data pertaining to the M2M Service Subscription (the technical part of the contract between an M2M Application provider and an M2M Service Provider).

Editor’s Note: The link between the M2M Service Subscription resource and RBAC will be added once RBAC is included in the specification.

Figure 9.6.20-1: Structure of <m2mServiceSubscription> resource 
(only resource specific attributes are shown)

Editor’s Note: the M2M-Sub-ID storage is FFS

This resource shall contain the child resources according to their multiplicitly in Table 9.6.19-1 (0 indicates the optionality of the child resource).

Table 9.6.19-1: Child resources of <m2mServiceSubscription> resource

| Child Resource Name of <remoteCSE> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| nodeInfo | <nodeInfo> | 0..n | See section 9.6.18. |

The <m2mServiceSubscription> resource shall contain the attributes described in Table 9.6.20-1.

Table 9.6.20-1: Attributes of <m2mServiceSubscription> resource

| Attribute Name of <m2mServiceSubscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..1 | RW | See section 9.6.1 where this common attribute is described. If no accessRightID is given at the time of creation, the accessRightID of the parent resource is linked to this attribute |
| creationTime (cT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| subsSer&RoleList | 1 | WO | This attribute indicates the list of subscribed service and roles. |
| appID | 0..n | RW | The value of this attribute shall be set to an application identifier as defined in section 7.1.3 pertaining to applications in infrastructure domain (IN-AE) of this M2M service subscription. |
| subsGroup | 0..n | RW | This attribute contains a group created by the subscriber for the purpose of helping easy setting of Access Rights. An example of the subscriber defined group is all node applications within this service subscription with app-ID set to a specific value. |

### 9.6.20	Resource Type nodeInfo

This resource represents M2M node information that is needed as part of the M2M Service Subscription resource. It shall contain information about the node as well as application identifiers running on that node.

Figure 9.6.20-1: Structure of <nodeInfo> resource 
(only resource specific attributes are shown)

The <nodeInfo> resource shall contain the attributes described in Table 9.6.20-1.

Table 9.6.20-1: Attributes of <nodeInfo> resource

| Attribute Name of <m2mServiceSubscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..1 | RW | See section 9.6.1 where this common attribute is described. If no accessRightID is given at the time of creation, the accessRightID of the parent resource is linked to this attribute |
| creationTime (cT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| nodeID | 1 | RW | Node identifier indicating where the M2M Service Subscription applies. Wildcard may be used to allow all the Nodes within a M2M Service Provider. |
| AppID | 0..n | RW | See section 7.1.3. application ID pertaining to an application running on this node |
| CSEID | 0..1 | RW | cseID pertaining to this node (for nodes that have a CSE). The cseID becomes know once the pre CSE registration procedure is triggered. |

-----------------------------------END THIRD CHANGE-----------------------

----------------------------------------FOURTH CHANGE----------------------------

# Annex <C>: (Informative):	List of M2M Services

This annex provides the list of M2M Services supported in this specification as well as the list of associated roles mapped to each M2M Service.

| M2M Service (name) | M2M-Serv-ID | Roles |
| --- | --- | --- |
| Application and service management | 01 | 1-Configuration 2-Diagnostic and monitoring 3-Software management |
| Device management | 02 | 1-Device Configuration 2-Device Diagnostics and Monitoring 3-Device Firmware Management 4-Device Topology |
| Location | 03 | 1-Location |
| Data exchange | 04 | 1-Basic data |
| Device onboarding | 05 | 1-onboarding |
| Service Provider specific | 80 to 99 range |  |

Editor’s note: Each role must be mapped to a set of resource types and related primitives.

-----------------------------------END FOURTH CHANGE----------------------------

# Comments

Add wild card