| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Group procedure clarification |
| Source:* | LG Electronics |
| Contact: | Seungmyeong Jeong, seungmyeong.jeong@lge.com |
| Date:* | 2014-02-10 |
| Abstract:* |  |
| Agenda Item:* | Tbd |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

In group operations, when a request from Originator is fanned out to each member by group hosting CSE, each member does the following according to the current specification:

Member Hosting CSEs: For the CREATE procedure, the Member Hosting CSE shall:

- Treat the request received from the group hosting CSE as a normal CREATE request on the addressed resource as if it comes from the original Originator.

To do this, group hosting CSE who creates fan out request should also include information of original Originator. This contribution proposes to clarify this information is contained in fr parameter in fanned out requests created by group hosting CSE.

In R01:

- Corrected a typo in the title of Table 10.2.4.6-1.

- Added “fr parameter in the request is set to ID of the Originator.” In group hosting CSE procedure for clarity.

- Removed additional ID of original Originator in fan out requests, rather that ID information is contained as fr parameter in the fan out request.

- Removed “Treat the request received from the group hosting CSE as a normal UPDATE request on the addressed resource as if it comes from the original originator. “ in member hosting CSE procedure

- Instead, added “Perform the corresponding CREATE procedure for the resource type in the request. (clause 10.2 resource specific procedures)”

- Proposals

Start of changed text 1

#### 10.2.4.6	Create <Members>

This procedure shall be used for creating the content of all member resources belonging to an existing <group> resource.

Originator: The Originator shall request to create the content in all member resources belonging to an existing <group> resource by using a CREATE verb. The Request may address the virtual child resource members of the specific <group> resource of a group hosting CSE to create the same content under all member resources. The request may also address the URI that results from appending a relative URI to the members URI in order to create the same content (e.g. attribute or child resource) under the corresponding attributes or child resources represented by the relative URI with respect to all member resources. The Originator may be an AE or CSE.

Group Hosting CSE: For the CREATE procedure, the Group Hosting CSE shall:

- Check if the Originator has WRITE permission in the accessRight resource referenced by the membersAccessRightID in the <group> resource. In the case membersAccessRightID is not provided the access right defined for the <group> resource shall be used.

- Upon successful validation, obtain the URIs of all member resources from the attribute membersList of the addressed <group> resource.

- Generate fan out requests addressing the obtained URIs (appended with the relative URI if any) to the member hosting CSEs as indicated in Figure 10.2.4.6-1. fr parameter in the request is set to ID of the Originator.

- In the case that the member resources contain a sub-group resource, generate a unique group request identifier, include the group request identifier in all the requests to be fanned out and locally store the group request identifier.

- If the group hosting CSE determines that multiple member resources belong to one CSE according to the URIs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group hosting CSE creating a <group> resource on the member hosting CSE to collect all the members on that member hosting CSE.

- After receiving the responses from the member hosting CSEs, respond to the Originator with the aggregated results and the associated <memberId>s.

Member Hosting CSEs: For the CREATE procedure, the Member Hosting CSE shall:

- Perform the corresponding CREATE procedure for the resource type in the request. (clause 10.2 resource specific procedures)

- Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifiers stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the group request identifier.

- Check if the original Originator has the CREATE permission on the addressed resource. Upon successful validation, perform the create procedures for the corresponding type of addressed resource as described in other subclauses of section 10.2.

- Send the corresponding response to the Group Hosting CSE.

Editor’s Note: How to aggregate synchronous and asynchronous responses is to be considered in stage 3.

Editor’s Note: How to generate and maintain the gid is to be FFS is stage 3.

Figure 10.2.4.6-1: Group content management procedures

The procedures illustrated in Figure 10.2.4.6-1 apply to sections 10.2.4.6 to 10.2.4.9:

Table 10.2.4.6-1: <Members> CREATE

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | None |
| Information on Request message | op: C fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the members virtual resource. cn: The representation of the resource the Originator intends to create gid: The group request identifier |
| Local processing on Hosting CSE | Fan out requests to each member hosting CSE addressing the obtained URI from the attribute membersList of the group resource appended with relative URI if any. Generate group request identifier and include the identifier in the fanned out requests in the case of sub groups. |
| Information on Response message | Converged responses from member hosting CSEs. |
| Post-Conditions | None |
| Exceptions | Same request with identical group request identifier received. Originator does not have the access right to access the members resource. |

#### 10.2.4.7	Retrieve <Members>

This procedure shall be used for retrieving the content of all member resources belonging to an existing <group> resource.

Originator: The Originator shall request to obtain the content or specific information (e.g. attributes) of all member resources belonging an existing <group> resource by using a RETRIEVE verb. The request may address the virtual child resource members of the specific <group> resource of a group hosting CSE for retrieving the content of all member resources. The request may also address the URI that results from appending a relative URI to the members URI in order to retrieve the corresponding attributes or child resources represented by the relative URI with respect to all member resources. The originator may be an AE or CSE.

Group Hosting CSE: For the RETRIEVE procedure, the Group Hosting CSE shall:

- Check if the Originator has READ permission in the accessRight resource referenced by the membersAccessRightID in the addressed <group> resource. In the case membersAccessRightID is not provided the access right defined for the group resource shall be used.

- Upon successful validation, obtain the URIs of all member resources from the membersList attribute of the addressed <group> resource.

- Generate fan out requests addressing the obtained URIs (appended with the relative URI if any) to the member hosting CSEs as indicated in Figure 10.2.4.6-1. fr parameter in the request is set to ID of the Originator.

- In the case that the member resources contain a sub-group resource, generate a unique group request identifier, include the group request identifier in all the requests to be fanned out and locally store the group request identifier.

- If the group hosting CSE determines that multiple member resources belong to one CSE according to the URIs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group hosting CSE creating a <group> resource on the member hosting CSE to collect all the members on that member hosting CSE.

- After receiving the responses from the member hosting CSEs, respond to the originator with the aggregated results and the associated <memberId>s.

Member Hosting CSEs: For the RETRIEVE procedure, the Member Hosting CSE shall:

- Perform the corresponding CREATE procedure for the resource type in the request. (clause 10.2 resource specific procedures)

- Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the request identifier.

- Check if the original originator has the READ permission on the addressed resource. Upon successful validation, perform the retrieve procedures for the corresponding type of addressed resource as described in other subclauses of section 10.2.<??>

- Send the corresponding response to the group hosting CSE.

Table 10.2.4.7-1: <Members> RETRIEVE

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | None |
| Information on Request message | op: R fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the members resource. gid: The group request identifier. |
| Local processing on Hosting CSE | Fan out requests to each member hosting CSE addressing the obtained URI from the attribute membersList of the group resource appended with relative URI if any. Generate group request identifier and include the identifier in the fanned out requests in the case of sub groups. |
| Information on Response message | Converged responses from member hosting CSEs. |
| Post-Conditions | None |
| Exceptions | Same request with identical request identifier received. Originator does not have the access right to access the members resource. |

#### 10.2.4.8	Update <Members>

This procedure shall be used for updating the content of all member resources belonging to an existing <group> resource.

Originator: The Originator shall request to update the content of all member resources belonging to an existing <group> resource with the same new data by using a UPDATE verb. The request may address the virtual child resource members of the specific <group> resource of a group hosting CSE to update all member resources. The request may also address the URI that results from appending a relative URI to the members in order to update only the corresponding attributes or child resources represented by the relative URI with respect to all member resources. The originator may be an AE or CSE.

Group Hosting CSE: For the UPDATE procedure, the Group Hosting CSE shall:

- Check if the originator has WRITE permission in the accessRight resource referenced by the membersAccessRightID in the group resource. In the case membersAccessRightID is not provided the access right defined for the group resource shall be used.

- Upon successful validation, obtain the URIs of all member resources from the attribute membersList of the addressed <group> resource.

- Generate fan out requests addressing the obtained URIs (appended with the relative URI if any) to the member hosting CSEs as indicated in Figure 10.2.4.6-1. fr parameter in the request is set to ID of the Originator.

- In the case that the member resources contain a sub-group resource, generate a unique group request identifier, include it in all the requests to be fanned out and locally store the group request identifier.

- If the group hosting CSE determines that multiple member resources belong to one CSE according to the URIs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group hosting CSE creating a <group> resource on the member hosting CSE to collect all the members on that member hosting CSE.

- After receiving the responses from the member hosting CSEs, respond to the originator with the aggregated results and the associated <memberId>s.

Member Hosting CSEs: For the UPDATE procedure, the Member Hosting CSE shall:

- Perform the corresponding CREATE procedure for the resource type in the request. (clause 10.2 resource specific procedures)

- Check if the request has a group request identifier.Check if the request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the request identifier.

- Check if the original originator has the UPDATE permission on the addressed resource. Upon successful validation, perform the update procedures for the corresponding type of addressed resource as described in other subclauses of section 10.2 <??>

- Send the corresponding response to the group hosting CSE.

Table 10.2.4.8-1: <Members> UPDATE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | None |
| Information on Request message | op: U fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <group> resource. cn: The representation of the resource the Originator intend to Udpate. gid: The group request identifier. |
| Local processing on Hosting CSE | Fan out requests to each member hosting CSE addressing the obtained URI from the attribute membersList of the group resource appended with relative URI if any. Generate group request identifier and include the identifier in the fanned out requests in the case of sub groups. |
| Information on Response message | Converged responses from member hosting CSEs. |
| Post-Conditions | None |
| Exceptions | Same request with identical request identifier received. Originator does not have the access right to access the members resource. |

#### 10.2.4.9	Delete <Members>

This procedure shall be used for deleting the content of all member resources belonging to an existing <group> resource.

Originator: The Originator shall request to delete the content of all member resources belonging to an existing <group> resource by using a DELETE verb. The request may address the virtual child resource members of the specific <group> resource of a group hosting CSE to delete all member resources. The request may also address the URI that results from appending a relative URI to the members in order to delete only the corresponding attributes or child resources represented by the relative URI with respect to all member resources. The originator may be an AE or a CSE.

Group Hosting CSE: For the DELETE procedure, the Group Hosting CSE shall:

- Check if the Originator has WRITE permission in the accessRight resource referenced by the membersAccessRightID in the <group> resource. In the case membersAccessRightID is not provided the access right defined for the group resource shall be used.

- Upon successful validation, obtain the URIs of all member resources from the attribute membersList of the addressed <group> resource.

- Generate fan out requests addressing the obtained URIs (appended with the relative URI if any) to the member hosting CSEs as indicated in Figure 10.2.4.6-1. fr parameter in the request is set to ID of the Originator.

- In the case that the member resources contain a sub-group resource, generate a unique group request identifier, include the group request identifier in all the requests to be fanned out and locally store the group request identifier.

- If the group hosting CSE determines that multiple member resources belong to one CSE according to the URIs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group hosting CSE creating a <group> resource on the member hosting CSE to collect all the members on that member hosting CSE.

- After receiving the responses from the member hosting CSEs, respond to the originator with the aggregated results and the associated <memberId>s.

Member Hosting CSEs: For the DELETE procedure, the Member Hosting CSE shall:

- Perform the corresponding CREATE procedure for the resource type in the request. (clause 10.2 resource specific procedures)

- Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the group request identifier.

- Check if the original originator has the DELETE permission on the addressed resource. Upon successful validation, perform the delete procedures for the corresponding type of addressed resource as described in other subclauses of clause 10.2<??>

- Send the corresponding response to the Group Hosting CSE.

Table 10.2.4.9-1: <Members> DELETE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | None |
| Information on Request message | op: D fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <group> resource. gid: The group request identifier. |
| Local processing on Hosting CSE | Fan out requests to each member hosting CSE addressing the obtained URI from the attribute membersList of the group resource appended with relative URI if any. Generate group request identifier and include the identifier in the fanned out requests in the case of sub groups. |
| Information on Response message | Converged responses from member hosting CSEs. |
| Post-Conditions | None |
| Exceptions | Same request with identical request identifier received. Originator does not have the access right to access the members resource. |

End of changed text 1