| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Huawei, China Unicom |
| Format:* | TP#9 |
| Date:* | 2014-02-20 |
| Contact:* | Qi Yu (yuqi@huawei.com); Changwei Hu (hucw5@chinaunicom.cn ) |
| Reason for Change/s:* | This contribution proposes a new section to support delivery of device triggering messages over Tsms interface. |
| Clause/Sub Clause Affected* | B.6.1.2 |
| Agenda Item:* | ARC |
| Work item(s): | WI0002 |
| Document(s) Impacted* | oneM2M-TS 0001 Technical Architecture v 0.3.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Rationale

3GPP can support device triggering by Tsp and Tsms interfaces. The TS-0001 includes section B6.1.2 for Tsp. This contribution proposes a new section to support delivery of device triggering messages over Tsms interface.

======================== START 1ST CHANGE ===========================

#### B.6.1.2	Serving IN-CSE initiated connectivity establishment procedure

#### B6.1.2.1 Supporting connetivity establishement by Tsp

Figure B.6.1.2-1: IN-CSE initiated connectivity establishment

- The Serving IN-CSE receives a Request from Application Server with Terminated-CSE-ID which indicates the destination ASN-CSE.

- The Serving IN-CSE determines the need to trigger a particular ASN-CSE. Once Serving IN-CSE receives the Terminated-CSE ID, serving IN-CSE deduces 3GPP-External-ID which enables it to deliver data to the destination ASN-CSE in 3GPP Underlying Network via MTC functions.

If the serving IN-CSE has no connectivity details for an 3GPP MTC-IWF, it may determine the IP address(es)/port(s) of the MTC-IWF by performing a DNS query using the 3GPP External Identifier or using a locally configured MTC-IWF identifier.

Editor’s Note: Mechanisms other than DNS query could be used for determining the IP address(es)/port(s) of the MTC-IWF. These are FFS.

- The Serving IN-CSE sends the Trigger Request (includes 3GPP External Identifier or MSISDN, ASN-CSE Identifier, trigger reference number, validity period, priority, Application Port ID and trigger payload) message to the MTC-IWF. The IN-CSE includes a trigger payload that contains the information destined for the ASN-CSE (i.e., target device).

Once, 3GPP-MTC-IWF receives the Trigger Request, it deduces particular MSISDN from given 3GPP-External-ID which one-to-one mapping is obtained from a query to 3GPP-HSS.

- The MTC-IWF selects T4 trigger delivery procedure according to the 3GPP TS23.682, based on the information received from HSS/HLR and local policy.

- The MTC-IWF sends the Device Trigger Report (External Identifier or MSISDN and trigger reference number) message to the Serving IN-CSE with a cause value indicating whether the trigger delivery succeeded or failed and the reason for the failure.

- ASN-CSE establishes IP connection with Underlying Network.

After reception of domain name and IP address of the ASN-CSE the IN-CSE can initiate communication with the target device via the IP connection.

B6.1.2.2 Supporting connectivity establishment by Tsms

Tsms is defined by 3GPP and is the interface that encompasses all the various proprietary SMS-SC to SME interface standards (such as SMPP, see TR 23.039). Tsms can be used to send a device triggering message to an ASN/MN encapsulated in an MT-SMS by Serving IN-CSE acting as a SME. ASN/MN initiates immediate or later communication with the Serving IN-CSE according to the content of trigger.======================== END 1ST CHANGE =============================