| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC #9 |
| Title:* | Resource Type for CMDH Policy |
| Source:* | Nicolas Damour, Sierra Wireless, ndamour@sierrawireless.com Josef Blanz, Qualcomm Inc. (TIA), jblanz@qti.qualcomm.com |
| Contact: | Nicolas Damour |
| Date:* | 2014-02-18 |
| Abstract:* | This contribution introduces a new resource type to support provisioning of CMDH related policies |
| Agenda Item:* | Contributions |
| Work item(s): | WI-0002 Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To adopt the suggested modification for inclusion into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Below are samples of the styles to be used in this document

- Introduction

In its current version, the Architecture Technical Specification, section 8.1.2, introduces several request parameters that are meant to drive the CMDH Common Services Function present in a hosting CSE to take appropriate action pertaining to that request. For example, based on these parameters, the CMDH CSF may aggregate several requests into just one before forwarding it, or may take some time before forwarding a given request to its target CSE.

The relevant parameters are the following.

| Name | Description | Category |
| --- | --- | --- |
| ec | event category | Communication Categorization |
| rqet | request expiration timestamp | Communication Timing |
| rset | result expiration timestamp | Communication Timing |
| oet | operational execution time | Communication Timing |
| rp | response persistence | Communication Timing |
| rt | response type | Communication Scheme |
| rc | result content | Communication Scheme |
| rd | result destination | Communication Scheme |
| da | delivery aggregation | Communication Scheme |

All these parameters allow to finely tune the communication patterns in the M2M system, but requiring users (for example Application Entities) to set them all may impose an unnecessary burden on them.

This contribution introduces a new resource type called cmdhPolicy that allows users who prefer simplicity to use only the parameters ec (event category) to render to a set of predefined CMDH parameters associated with a CMDH policy. Users who want full control over CMDH management will remain able to use all parameters as they see fit.

- Proposal

# Start of proposed new text #

### 9.6.X		Resource Type cmdhPolicy

The <cmdhPolicy> resource type represents a set of rules defining which CMDH parameters will be used by default when a request issued by a local originator (eg. locally registered AE or another CSF inside the local CSE) contains the “ec” parameter but not all other CMDH parameters.

One or several resources of type <cmdhPolicy> may be linked as child resources of the local <CSEBase> resource, thus defining a set of CMDH policies applicable whenever this local hosting CSE receives requests.

In addition, one or several resources of type <cmdhPolicy> may be linked as child resources of other resources of type <application> or <remoteCSE>, thus overriding the default set of policies for the relevant locally registered Application Entities or remote CSEs.

Figure 9.6.X-.1: Structure of <cmdhPolicy> resource 
(only resource specific attributes are shown)

The resource <cmdhPolicy> shall contain child resources according to their multiplicity shown in Table 9.6.X-1. A value of "0" for multiplicity indicates the child resource is optional.

Table 9.6.X-1: Child resources of <cmdhPolicy> resource

| Child Resource Name of <cmdhPolicy> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <cmdhDefaults> | 1. | See section 9.6.W where the type of this child resource is described. |
| [variable] | <cmdhLimits> | 1..n | See section 9.6.X where the type of this child resource is described. |
| [variable] | <cmdhNetworkAccessRules> | 1..n | See section 9.6.Y where the type of this child resource is described. |
| [variable] | <cmdhBuffer> | 1..n | See section 9.6.Z where the type of this child resource is described. |

The resource <cmdhPolicy> shall contain attributes according to their multiplicity shown in Table 9.6.X-2.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.X-2: Attributes of <cmdhPolicy> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aR) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| name | 1 | RW | A name under which the CMDH policy will be referred. |
| status | 1 | RW | Either “active” or “inactive”, this attribute allows to provision policies without activating them immediately, thus sparing the need to completely erase policies and then reprovision them remotely when one only needs to deactivate them temporarily. Only one policy can be “active” at any given time. |

Note: in order to avoid race conditions, it may be better that the CSE refers to the currently active cmdhPolicy instead of using the “status” attribute.

Editor’s note: When the <CSEBase> resource is accepted, an attribute or link in the <CSEBase> resource could be used to point to the active <cmdhPolicy> resource.

# End of proposed text #