| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | deviceInfo, batteryMgmt, deviceCapability, capabilityInstance Resources |
| Source:* | LG Electronics |
| Contact: | Seungkyu Park, seungk.park@lge.com |
| Date:* | 2014-2-10 |
| Abstract:* | This contribution provides the resources; deviceInfo, batteryMgmt, deviceCapability, capabilityInstance. |
| Agenda Item:* | ARC 9.0 |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

This contribution is to propose the new resources for below purposes:

- Device Information

- Device Functional Capabilities

- Power (Battery) Characteristics

## Beginning of Change 1 ##

### X.y.1	Resource Type batteryMgmt

This resource is used to share information regarding the battery.

Figure X.y.z-1: Structure of <batteryMgmt> resource

This resource shall contain the child resources according to their multiplicitly in Table X.y.z-1 (0 indicates the optionality of the child resource).

Table X.y.1-1: Child resources of <batteryMgmt> resource

| Child Resource Name of <batteryMgmt> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See section 9.6.9 |

This resource shall contain the attributes according to their multiplicitly in Table X.y.z-2 (0 indicates the optionality of the attribute).

Table X.y.1-2: Attributes of <batteryMgmt> resource

| Attribute Name of <batteryMgmt> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| batteryLevel | 1 | RO | The current battery level. |
| batteryStatus | 1 | RO | Indicates the status of the battery. |

## End of Change 1 ##

## Beginning of Change 2 ##

### X.y.2	Resource Type deviceInfo

This resource is used to share information regarding the device.

Figure X.y.z-1: Structure of <deviceInfo> resource

This resource shall contain the child resources according to their multiplicitly in Table X.y.z-1 (0 indicates the optionality of the child resource).

Table X.y.2-1: Child resources of <deviceInfo> resource

| Child Resource Name of <batteryMgmt> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See section 9.6.9 |

This resource shall contain the attributes according to their multiplicitly in Table X.y.z-2 (0 indicates the optionality of the attribute).

Table X.y.2-2: Attributes of <deviceInfo> resource

| Attribute Name of <batteryMgmt> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| deviceLabel | 1 | RO | Unique device label assigned by the manufacturer. The uniqueness may be global or only valid within a certain domain (e.g. vendor-wise or for a certain deviceType). |
| Manufacturer | 1 | RO | The name/identifier of the device manufacturer. |
| Model | 1 | RO | The name/identifier of the device mode assigned by the manufacturer. |
| deviceType | 1 | RO | The type (e.g. cell phone, photo frame, smart meter) or product class (e.g. X-series) of the device. |
| fwVersion | 1 | RO | The firmware version of the device. NOTE: If the device only supports one kind of Software this is identical to softwareVersion. |
| swVersion | 1 | RO | The software version of the device. |
| hwVersion | 1 | RO | The hardware version of the device. |

## End of Change 2 ##

## Beginning of Change 3 ##

### X.y.3	Resource Type deviceCapability

This resource is used to manage the device capabilities.

Figure X.y.z-1: Structure of <deviceCapability> resource

This resource shall contain the child resources according to their multiplicitly in Table X.y.z-1 (0 indicates the optionality of the child resource).

Table X.y.3-1: Child resources of <deviceCapability> resource

| Child Resource Name of <batteryMgmt> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See section 9.6.9 |
| [variable] | <capabilityInstance> | 0..n | See section X.y.4 |

This resource shall contain the attributes according to their multiplicitly in Table X.y.z-2 (0 indicates the optionality of the attribute).

Table X.y.3-2: Attributes of <deviceCapability> resource

| Attribute Name of <batteryMgmt> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |

## End of Change 3 ##

## Beginning of Change 4 ##

### X.y.4	Resource Type capabilityInstance

This resource is the instance for representing each device capability.

Figure X.y.4-1: Structure of <capabilityInstance> resource

This resource shall contain the child resources according to their multiplicitly in Table X.y.z-1 (0 indicates the optionality of the child resource).

Table X.y.z-1: Child resources of <capabilityInstance> resource

| Child Resource Name of <batteryMgmt> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See section 9.6.9 |

This resource shall contain the attributes according to their multiplicitly in Table X.y.z-2 (0 indicates the optionality of the attribute).

Table X.y.4-2: Attributes of <capabilityInstance> resource

| Attribute Name of <batteryMgmt> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| capabilityName | 1 | WO | The name of the capability. |
| attached | 1 | RO | Indicates whether the capability is attached to the device or not. |
| capabilityActionStatus | 1 | RO | Indicates the status of the Action (including a progress indicator, a final state and a reminder of the requested action). |
| enable | 0..1 | WO | The action that allows enabling the device capability. UPDATE Request on this attribute will trigger the action. |
| disable | 0..1 | WO | The action that allows disabling the device capability. UPDATE Request on this attribute will trigger the action. |

## End of Change 4 ##