| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | deviceInfo, batteryMgmt, deviceCapability, capabilityInstance Resources |
| Source:* | LG Electronics |
| Contact: | Seungkyu Park, seungk.park@lge.com |
| Date:* | 2014-2-10 |
| Abstract:* | This contribution provides the resources; deviceInfo, batteryMgmt, deviceCapability, capabilityInstance. |
| Agenda Item:* | ARC 9.0 |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

This contribution is to propose the new resources for below purposes:

- Device Information

- Device Functional Capabilities

- Power (Battery) Characteristics

- Reboot

- eventLog

## Beginning of Change 1 (all new texts) ##

### C.x	Resource battery

This resource is used to share information regarding the battery. The resource type of the Resource battery is <mgmtObj>.

Editor's Note: Using [battery] notation needs more discussion with WG2.

Figure C.x-1: Structure of battery resource

This resource shall contain the attributes according to their multiplicitly in Table C.x-1 (0 indicates the optionality of the attribute).

Table C.x-2: Attributes of battery resource

| Attribute Name of battery | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | See section 9.6.10. This attribute shall have the fixed value “battery”. |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |
| batteryLevel | 1 | RO | The current battery level. |
| batteryStatus | 1 | RO | Indicates the status of the battery. |

## End of Change 1 ##

## Beginning of Change 2 (all new texts) ##

### C.y	Resource deviceInfo

This resource is used to share information regarding the device. The resource type of the Resource deviceInfo is <mgmtObj>.

Figure C.y-1: Structure of deviceInfo resource

This resource shall contain the attributes according to their multiplicitly in Table C.y-1 (0 indicates the optionality of the attribute).

Table C.y-2: Attributes of deviceInfo resource

| Attribute Name of deviceInfo | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | See section 9.6.10. This attribute shall have the fixed value “deviceInfo”. |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |
| deviceLabel | 1 | RO | Unique device label assigned by the manufacturer. The uniqueness may be global or only valid within a certain domain (e.g. vendor-wise or for a certain deviceType). |
| Manufacturer | 1 | RO | The name/identifier of the device manufacturer. |
| Model | 1 | RO | The name/identifier of the device mode assigned by the manufacturer. |
| deviceType | 1 | RO | The type (e.g. cell phone, photo frame, smart meter) or product class (e.g. X-series) of the device. |
| fwVersion | 1 | RO | The firmware version of the device. NOTE: If the device only supports one kind of Software this is identical to softwareVersion. |
| swVersion | 1 | RO | The software version of the device. |
| hwVersion | 1 | RO | The hardware version of the device. |

## End of Change 2 ##

## Beginning of Change 3 (all new texts) ##

### C.z	Resource deviceCapability

This resource is used to manage the device capabilities. The resource type of the Resource deviceCapability is <mgmtObj>.

Figure C.z-1: Structure of deviceCapability resource

This resource shall contain the child resources according to their multiplicitly in Table C.z-1 (0 indicates the optionality of the child resource).

Table C.z-2: Child resources of deviceCapability resource

| Child Resource Name of <batteryMgmt> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <parameter> | 0..n | See section C.a |

This resource shall contain the attributes according to their multiplicitly in Table C.z-2 (0 indicates the optionality of the attribute).

Table X.y.3-2: Attributes of deviceCapability resource

| Attribute Name of deviceCapability | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | See section 9.6.10. This attribute shall have the fixed value “deviceCapability”. |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |

## End of Change 3 ##

## Beginning of Change 4 (all new texts) ##

### C.za	Resource capabilityInstance

This resource is the instance for representing each device capability. The resource type of the Resource capabilityInstance is <parameter>.

Figure C.za-1: Structure of capabilityInstance resource

This resource shall contain the attributes according to their multiplicitly in Table C.za-2 (0 indicates the optionality of the attribute).

Table C.za-2: Attributes of capabilityInstance resource

| Attribute Name of capabilityInstance | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |
| capabilityName | 1 | WO | The name of the capability. |
| attached | 1 | RO | Indicates whether the capability is attached to the device or not. |
| capabilityActionStatus | 1 | RO | Indicates the status of the Action (including a progress indicator, a final state and a reminder of the requested action). |
| enable | 0..1 | WO | The action that allows enabling the device capability. |
| disable | 0..1 | WO | The action that allows disabling the device capability. |

## End of Change 4 ##

## Beginning of Change 5 (all new texts) ##

### C.zb	Resource reboot

This resource is used to reboot the device. The resource type of the Resource reboot is <mgmtObj>.

Figure C.zb-1: Structure of reboot resource

This resource shall contain the attributes according to their multiplicitly in Table C.zb-2 (0 indicates the optionality of the attribute).

Table C.zb-2: Attributes of reboot resource

| Attribute Name of reboot | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | See section 9.6.10. This attribute shall have the fixed value “reboot”. |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |
| reboot | 1 | RW | The action that allows rebooting the device. |
| factoryReset | 1 | RW | The action that allows making the device returning to the factory settings. |

## End of Change 5 ##

## Beginning of Change 6 ##

### C.zc	Resource eventLog

This resource is used to record the event log for the device. The resource type of the Resource eventLog is <mgmtObj>.

Figure C.zc-1: Structure of eventLog resource

This resource shall contain the attributes according to their multiplicitly in Table C.zc-2 (0 indicates the optionality of the attribute).

Table C.zc-2: Attributes of eventLog resource

| Attribute Name of eventLog | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | See section 9.6.10. This attribute shall have the fixed value “eventLog”. |
| objectID | 0..1 | WO | See section 9.6.10 |
| objectPath | 0..1 | WO | See section 9.6.10 |
| description | 0..1 | RW | See section 9.6.10 |
| logTypeId | 1 | RW | Identifies the types of log to be recorded. E.g., security log, system log. |
| logData | 1 | R | Diagnostic data logged upon event of interests defined by this diagnostic function. |
| logActionStatus | 1 | RO | Indicates the status of the Action. E.g., Started, Stopped. |
| logStart | 1 | RW | The action that allows starting the log corresponding to the mentioned logTypeId. |
| logStop | 1 | RW | The action that allows stopping the log corresponding to the mentioned logTypeId. |

## End of Change 6 ##