| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC #9 |
| Title:* | Access Right Link Type |
| Source:* | Nicolas Damour, Sierra Wireless, ndamour@sierrawireless.com |
| Contact: | Nicolas Damour |
| Date:* | 2014-02-10 |
| Abstract:* | This contribution completes the section 9.4 on links by reformulating how a resource is linked to an access right over a link of type accessRight, defined in an attribute “accessRightID” |
| Agenda Item:* | Contributions |
| Work item(s): | WI-0002 Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To adopt the suggested modification for inclusion into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Below are samples of the styles to be used in this document

- Introduction

In its current version, the Architecture Technical Specification, section 9.4, introduces the concept of links but remains vague about how they are actually implemented. A note also states that “a resource can also be linked using an attribute containing the linked resource ID”

This contribution intends to take the example of the already well-defined link between a resource and its access right over the attribute accessRightID to make more clear how a link defined over a resource attribute may look like.

- Proposal

# Proposed text change (changes compared to TS-0001 v3.0.2 are highlighted in yellow) #

9.4.2 Link Types

The following link types are defined:

- TBD.

| Link Type | Linking Resource Type (link origin) | Linked Resource Type (link destination) | Linking method | Description |
| --- | --- | --- | --- | --- |
| Access Right | Several (node, application, remoteCSE, container…) | accessright | Attribute named “accessRightID” | See section 9.6.1 |

Editor's Note: The types of links is FFS.

Editor’s Note: there are more link types to define in this table to reflect the current state of the TS.

# End of proposed text change #