| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC #9 |
| Title:* | Hosted CSE Link Type |
| Source:* | Nicolas Damour, Sierra Wireless, ndamour@sierrawireless.com |
| Contact: | Nicolas Damour |
| Date:* | 2014-02-20 |
| Abstract:* | This contribution proposes to add the relationship between a CSE and its hosting node, or between an application and its hosting node, by adding the relevant section into the Architecture TS. |
| Agenda Item:* | Contributions |
| Work item(s): | WI-0002 Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To adopt the suggested modification for inclusion into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Below are samples of the styles to be used in this document

- Introduction

In its current version, the Architecture Technical Specification, section 9.4, introduces the concept of nodes and CSEs, without establishing a clear link between them.

This contribution intends to make that link, and should be read in conjunction with ARC-2014-0032R03-baseRoot_Resource_Type.

- Proposal

# Proposed text change 1 (changes compared to TS-0001 v3.0.2 are highlighted in yellow) #

9.4.2 Links

The following links are defined:

- TBD.

| Linked Resource Type (link destination) | Linking Resource Type (link origin) | Linking method | Description |
| --- | --- | --- | --- |
| CSEBase or remoteCSE | node | Attribute named “hostedCSEID” OR parent resource of type CSEBase | See section 9.6.x |

Editor's Note: The types of links is FFS.

Editor’s Note: there are more links to define in this table to reflect the current state of the TS.

# End of proposed text change #

# Proposed text change 2 (changes compared to TS-0001 v3.0.2 are highlighted in yellow) #

Table 9.6.17-2: Attributes of <node> resource

| Attribute Name of <node> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID_[i] (aRI_[i]) | 1..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| nodeID | 1 | RW | The ID of the Node which is specified in the resource type. |
| hostedCSEID | 1 | RW | The ID of the CSEBase that is hosted on this node |

# End of proposed text change #