| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 (ARC) at TP#9 |
| Title:* | Briefing Resource and Procedures |
| Source:* | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Contact: | As above |
| Date:* | 2014-02-10 |
| Abstract:* | The purpose of the briefing resource is to allow deploying off-the-shelf Field Domain Nodes without directly configuring the Field Domain Nodes. This contribution provides specification text defining the <briefing> resource and associated procedures. |
| Agenda Item:* | Contributions impacting ARC TS-0001 |
| Work item(s): | ARC WI-0002 |
| Document(s) Impacted* | Architecture TS (TS-0001) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG4 member should discuss on this topic, and determines final forms to be included as part of Security TS and/or Architecture TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

The purpose of the <briefing> resource is to allow deploying off-the-shelf Field Domain Nodes without directly configuring the Field Domain Nodes before deployment in a manual manner.

In many cases it will either not be possible or very difficult for CSE/AE in Field Domain Nodes, to preconfigure the CSE/AE with the CSE_ID of the Registrar with which the Field Domain CSE/AE should register. The<briefing> resource contains such details. An Field Domain CSE/AE shall obtain the content of the <briefing> resource from a “Briefing” Registrar whose identity is pre-configured to the Field Domain CSE, and who can authenticate with the Field Domain CSE/AE; the Field Domain CSE/AE  subsequently authenticates and registers with the Registrar identified in the <briefing> resource.

================<Start Change 1>================

### 9.6.18	Resource Type application

The <application> resource represents information about an Application Entity known to a given Common Services Entity.

Figure 9.6.18-1: Structure of <application> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.18-1 (0 indicates the optionality of the child resource).

Table 9.6.18-1: Child resources of <application> resource

| Child Resource Name of <application> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See section 9.6.9. |
| [variable] | <container> | 0..n | See section 9.6.3. |
| [variable] | <group> | 0..n | See section 9.6.5. |
| [variable] | <accessRight> | 0..n | See section 9.6.2. |
| software_[i] | <mgmtObj> | 1..n | See section 9.6.10 for <mgmtObj>. This resource represents the software component (or components, if the multiplicity is greater than 1) that compose the application. This mgmtObj shall have at least the following <parameters> child resources of its “parameters” subresource: - name (multiplicity 1) - version (multiplicity 1) - state (multiplicity 1) |
| [variable] | <commCapabilities> | 1..n | Resource <commCapabilities> needs to be defined. This resource describes the communication capabilities (essentially the protocols) supported and used by the corresponding Application Entity over the Mca reference point to this CSE. |
| briefing | <briefing> | 0..1 | See section 9.6.23. |

================<End Change 1>================

================<Start Change 2>================

### 9.6.19	Resource Type remoteCSE

A <remoteCse> resource shall represent a remote CSE that is registered to the local CSE. CSE resources shall be located directly under the <baseRoot>.

Conversely each registered CSE shall also be represented as a sub-set of <remoteCse> resource in the registering CSE's <baseRoot>.

For example, when CSE1 registers with CSE2, there will be two <remoteCse> resources created: one in CSE1 <baseRoot1>/<remoteCse2> and one in CSE2 <baseRoot2>/<remoteCse1>.

Note that the creation of the two resources does not imply mutual registration. The <baseRoot1>/<remoteCse2> is only local to CSE1 and is for its internal use.

Figure 9.6.19-1: Structure of <remoteCSE> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicitly in Table 9.6.19-1 (0 indicates the optionality of the child resource).

Table 9.6.19-1: Child resources of <remoteCSE> resource

| Child Resource Name of <remoteCSE> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <Application> | 0..n | See section 9.6.18. |
| [variable] | <container> | 0..n | See section 9.6.3. |
| [variable] | <group> | 0..n | See section 9.6.5. |
| [variable] | <accessRight> | 0..n | See section 9.6.2. |
| [variable] | <subscription> | 0..n | See section 9.6.9. |
| [variable] | <mgmtObj> | 0..n | See section 9.6.10. |
| briefing | <briefing> | 0..1 | See section 9.6.23. |

================<End Change 2>================

================<Start Change 3>================

### 9.6.23	Resource Type briefing

#### 9.6.23.1		Motivation

For CSE/AE in Field Domain Nodes, it may not be possible to preconfigure the CSE/AE with the CSE_ID of the Registrar with which the Field Domain CSE/AE should register. The<briefing> resource contains such details. A Field Domain CSE/AE shall obtain the content of the <briefing> resource from a “Briefing” Registrar whose identity is pre-configured to the Field Domain CSE, and who can authenticate with the Field Domain CSE/AE; the Field Domain CSE/AE  subsequently authenticates and registers with the Registrar identified in the <briefing> resource. The <briefing> resource may also contain other parameters facilitating mutual authentication of the Field Domain CSE/AE with the identified Registrar.

Examples:

- A device manufacturer may provide a Briefing Registrar for the devices that it manufactures. Device owners can provide the M2M SP (owning the Briefing Registrar) with the Target Registrar CSE_ID and any other credentials (such as Target M2M SP root certificates). The CSE/AE in the device are pre-configured to contact the Briefing Registrar during the device-start-up process. The CSE/AE retrieves the Target Registrar CSE_ID and any other credentials. The CSE/AE then authenticates and registers with the Target Registrar, using the additional credentials (such as Target M2M SP root certificates) where applicable.

- An Underlying Network Service Provider (UN SP) may provide a Briefing Registrar for the its Underlying Network Service Subscribers. The UICC/UIM in the Field Domain Node are pre-configured with the Briefing Registrar CSE_ID. The Briefing Registrar CSE_ID is retrieved from the during the device-start-up process.  The CSE/AE retrieves the Target Registrar CSE_ID and any other credentials. The CSE/AE then authenticates and registers with the identified Target Registrar.

The Security Solutions TS [TS-0003] describes where briefing procedures occur during authentication and initial registration.

In some scenarios, the Registree will retrieve the <content of the <briefing> resource immediately after registering with the Briefing Registrar, and then immediately de-register from the Briefing Registrar and authenticate and register with the Target Registrar.

In other scenarios, the Registree may subscribe to the <briefing> resource, and retrieve the content when notifications indicate that the resource has been updated.

#### 9.6.23.2		Specification

The <briefing> resource represents information to be provided to a Registree (Common Service Entity or Application Entity) for directing the Registree to authentication and register with another Registrar. This is typically used when a Registree is initiated and needs to determine which Common Server Entity it needs to register with to obtain full service.

The <briefing> resource shall be a child resource of the <remoteCSE> or <application> resource of the Registree to which the information is intended.

Figure 9.6.23-1: Structure of <briefing> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.23-1 (0 indicates the optionality of the child resource).

Table 9.6.23-1: Child resources of <briefing> resource

| Child Resource Name of <application> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See section 9.6.9. |
| [variable] | <accessRight> | 0..n | See section 9.6.2. |

The <briefing> resource shall contain the attributes described in Table 9.6.23-2.

Table 9.6.23-2: Attributes of <briefing> resource

| Attribute Name of <briefing> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RO | See section 9.6.1 where this common attribute is described. |
| name | 0..1 | RO | A human readable name of the Target Registrar |
| Target-CSE-ID | 1 | RO | Identifier for the Target Registrar |
| Target-Root-Certificates | 0..n | RO | Root certificates that may be used for the Target Registrar’s certificate (if the Target Registrar is to be authenticated using certificates). |
| Target-Identity-Token | 0..1 | RO | A value provided by the Target Registrar (through out of scope means) obtained from the Target Registrar as a means for identifying the Registree. The Registree provides this value to the Target Registrar during registration and the Target Registrar cross references this value to identify which Registree just registered. |

================<End Change 3>================

================<Start Change 4>================

### 10.2.11	<briefing> Resource Procedures

#### 10.2.11.1		Introduction

The briefing information shall be represented by a <briefing> resource (see clause 9.6.23). This allows manipulation of the briefing information in a resource oriented manner.

The following clauses describe procedures for Creation, Retrieval, Update and Deletion of a <subscription> resource.

#### 10.2.11.2		Create <briefing>

This procedure is not used. The <briefing> resource shall be created when the parent <remoteCSE> or <application> resource is created.

#### 10.2.11.3	Retrieve <subscription>

This procedure shall be used to retrieve the briefing information such as name, Target-CSE-ID, Target-Root-Certificates, Target-Identity-Token.

Originator: The Originator can be an AE or a CSE. The Request shall address a <briefing> resource..

Hosting CSE: If the Hosting SCE validates the Originator has RETRIEVE permission referring accessRightID , it shall return the complete representation of the <briefing> resource.

Table 10.2.11.3-1: <briefing> RETRIEVE

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | The Originator has RETRIEVE permission to the briefing resource. |
| Information on Request message | fr: ?? to: ?? No change from the basic procedure. |
| Local processing on Hosting CSE | fr: ?? to: ?? No change from the basic procedure. |
| Information on Response message | No change from the generic procedure. |
| Post-Conditions | None |
| Exceptions | No change from the generic procedure. |

#### 10.2.11.4	Update <briefing>

This procedure shall be used to update existing briefing information, e.g. to provide new Target Registrar details to the Registree associate with the parent <remoteCSE> or <application> resource.

Originator: The Originator can be an AE or a CSE. The Originator may send new value(s) for read-write attribute(s) of a <subscription> resource.

Hosting CSE: After the Hosting CSE verifying the existence of the addressed resource, the validity of the attributes provided and the permissions to modify them referring accessRightID, shall update the attributes provided and shall send positive response to the Originator.

Table 10.2.11.4-1: <briefing> UPDATE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | The Originator has UPDATE permission to the briefing resource. |
| Information on Request message | No change from the basic procedure. |
| Local processing on Hosting CSE | No change from the basic procedure. |
| Information on Response message | No change from the generic procedure. |
| Post-Conditions | None |
| Exceptions | No change from the generic procedure. |

#### 10.2.9.5	Delete <briefing>

This resource cannot be deleted separately from the parent resource. This resource is deleted when the parent resource is deleted.

================<End Change 4>================