| CHANGE REQUEST |
| --- |
| Group Name:* | ARC #9 |
| Source:* | InterDigital Communications, NE C, Intel |
| Format:* |  |
| Date:* | 2014-01-24 |
| Contact:* | Catalina.Mladin@InterDigital.com Barbara.Pareglio@neclab.eu ? Jain, Puneet <puneet.jain@intel.com> |
| Reason for Change/s:* | Addition of Trigger Recipient Identifier |
| Clause/Sub Clause Affected* |  |
| Agenda Item:* | TBD |
| Work item(s): | WI-0002 |
| Document(s) Impacted* | TS-0001 v.0.3.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Modify TS-0001 Spec as proposed in this contribution. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

In the context of introducing Device Trigerring services, WG2 has been presented ARC-2014-078R06 .  The introduction of a new ID associated with a trigger and the execution environment port to which it is routed has been generally agreed upon,  pending definition clarifications.

This documents proposes a definition for this new ID, as well as a corresponding update tothe ID table in section 7.2 of the ARC TS-001 v.0.3.2.

- Proposal(s)

Start of New Text  (1)

7.1.x  Trigger Recipient Identifier (Trigger-Recipient-ID)

This is an identifier used when device triggering services are requested from the Underlying Network, to identify an instance of an ASN/MN-CSE on an execution environment, to which the trigger is routed. For example, when 3GPP device triggering is used, the Trigger-Recipient-ID maps to the Application-Port-Identifier [3GPP 23.682].

End of New Text (1)

Start of Change (2)

## 7.2	M2M Identifiers lifecycle and characteristics

Table 7.2-1: M2M Identifiers lifecycle and characteristics

| Identifier | Assigned by | Assigned to | Assigned during | Lifetime | Uniqueness | Used during | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| M2M Service Provider Identifier | Out of scope | AE, CSE | Out of scope | Out of scope | Global | FFS |  |
| Application Instance Identifier | FFS | AE | Note that the Application instance identifier is created when the executing AE registers to a local CSE | Application Instance Registration | Global | - Application instance Registration - Other operations FFS |  |
| CSE Identifier | M2M SP | CSE | During the first M2M service connection unless pre-provisioned | Life of the CSE | Global | Information flows (section 10) |  |
| M2M Node Identifier | M2M SP | M2M Node hosting CSE | Pre-provisioned | Life of the M2M Node | Global | Out of scope |  |
| M2M Subscription Identifier | M2M SP | Application Entities, and one or more CSEs belonging to the same M2M subscriber | At service signup | Life of the Subscription with the MM SP | Global | - Charging and Information Recorded - Other operations are FFS | Multiple CSEs can be allocated the same M2M Subscription Identifier |
| M2M-Request-ID | Mcc: CSE Mca: Application Instance | A request initiated by an AE or CSE | Mcc: When a request is initiated by a CSE, or handling of a request received by a CSE. Mca: When a request is initiated by an AE | Equal to the lifetime of the Request and its corresponding Response | Mcc: Global Mca: Local or global | Requests and corresponding responses |  |
| External Identifier | Manual mode: Jointly between the Underlying Network provider and M2M SP, where applicable. Plug-And- Play: FFS | M2M Node belonging to a CSE that wants to utilize services of the Underlying Network. | Manual Mode: Administrative Agreement. Plug-And- Play: FFS | Life time of the CSE. | FFS | Requests initiated by a CSE over the Interface, where applicable. |  |
| Trigger Recipient Identifier | Execution Environment | ASN/MN-CSE instantiation | ASN/MN-CSE start-up or wake-up | CSE instance lifetime | Execution Environment-wide | Device Trigerring procedures |  |

End of change (2)