| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Philip Jacobs, Cisco Systems, phjacobs@cisco.com |
| Format:* | teleconference |
| Date:* | 2014-03-06 |
| Contact:* |  |
| Reason for Change/s:* | Missing information in table 9.6-1 |
| CR against: | TS-0001 v-0.4.2 |
| Clauses/Sub Clauses Affected* | 9.6 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Decide to adopt proposed changes |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Do not conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The problem is, that Table 9.6-1 Resource Summary has many empty cells. Since the resource type clauses have been updated there have been changes to child and parent resources.

This CR proposes:

- New text to fill the empty cells.

- To make child/parent updates in the table (every resource type clause was re-checked)

- To update the existing editors note  to reflect the current baseline version.

- To add a new editor’s note to identify inconsistencies between resource type clauses

Since it is difficult to see Word tracked changes in a table, the changes have been highlighted. When agreed, the highlighting should be removed before integration into the TS.

### -----------------------Start of change 1-------------------------------------------

## 9.6	Specified Resource Types

Table 9.6-1 introduces the defined resource types and their related child or parent resource types. Details of each resource type follow in the remainder of this clause.

Table 9.6-1 Resource Summary

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Permissions for entities’ access modes | subscription | Application, remoteCSE, CSEBase | 9.6.2 |
| application | Represents information about an AE | subscription, container, group, accessControlPolicy, mgmtObj, commCapabilities, pollingChannel | remoteCSE, CSEBase | 9.6.5 |
| cmdhBuffer | Defines CMDH buffer usage limits | None documented | cmdhPolicy | 9.6.30 |
| cmdhDefaults | Defines CMDH default values | cmdhDefEcValue, cmdhEcDefParamValues | cmdhPolicy | 9.6.24 |
| cmdhEcDefParamValues | Represent a specific set of default values for the CMDH related parameters | None documented | cmdhDefaults | 9.6.26 |
| cmdhDefEcValue | Defines a value for the ec (event category) parameter of an incoming request when it is not defined. | None documented | cmdhDefaults | 9.6.25 |
| cmdhLimits | Defines limits for CMDH related parameter values | None documented | cmdhPolicy | 9.6.27 |
| cmdhNetworkAccessRules | Defines rules for the usage of underlying networks | cmdhNwAccessRule | cmdhPolicy | 9.6.28 |
| cmdhNwAccessRule | Defines a rule for the usage of underlying networks | schedule | cmdhNetworkAccessRules | 9.6.29 |
| cmdhPolicy | A set of rules defining which CMDH parameters will be used by default | cmdhDefaults, cmdhLimits, cmdhNetworkAccessRules, cmdhBuffer | None documented | 9.6.23 |
| container | Shares data instances among entities | container, instance, subscription, | application, container, remoteCSE, CSEBase | 9.6.6 |
| CSEBase | The root for all the resources that are residing on a CSE. | remoteCSE, node, application, container, group, accessControlPolicy, subscription, mgmtObj, mgmtCmd, locationPolicy, statsConfig | None | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | None documented | None documented | 9.6.11 |
| eventConfig | Defines events that trigger statistics collection | None documented | statsConfig | 9.6.32 |
| execInstance | Represents a successful instance of mgmtCmd | None documented | mgmtCmd | 9.6.18 |
| group | Represents a group of resources | members | Application, remoteCSE, CSEBase | 9.6.13 |
| instance | Data instance in a container | None documented | container | 9.6.7 |
| locationPolicy | Obtains/manages geographical location | None documented | CSEBase | 9.6.10 |
| members | Virtual resource target for group requests | None documented | group | 9.6.14 |
| mgmtCmd | Method to execute management procedures / model commands and RPCs for existing protocols | execInstance | CSEBase | 9.6.17 |
| mgmtObj | Represents individual management functions | parameters | remoteCSE, CSEBase | 9.6.15 |
| m2mServiceSubscription | Data pertaining to the M2M Service Subscription | nodeInfo | None documented | 9.6.20 |
| node | Represents specific Node information | schedule, mgmtObj | CSEBase, remoteCSE | 9.6.19 |
| nodeInfo | Node information | None documented | m2mServiceSubscription | 9.6.21 |
| parameters | Parameters/attributes for management purposes | parameters | mgmtObj, parameters | 9.6.16 |
| pollingChannel | Represent a channel that can be used for a request-unreachable entity | None documented | remoteCSE, application | 9.6.22 |
| remoteCSE | Represents a remote CSE registered to the local CSE | application, container, group, accessControlPolicy, subscription, mgmtObj, pollingChannel, node | CSEBase | 9.6.4 |
| request | Expresses/access context of an issued Request | None documented | None documented | 9.6.12 |
| schedule | Contains scheduling information for delivery of messages | None documented | node, subscription, cmdhNwAccessRule | 9.6.39 |
| statsCollect | Defines triggers for the IN-CSE to collect statistics for applications | None documented | CSEBase (in IN-CSE) | 9.6.33 |
| statsConfig | Stores configuration of statistics for applications | eventConfig | CSEBase (in IN-CSE) | 9.6.31 |
| subscription | Information of subscribed-to resources | schedule | accessControlPolicy, application, container, group, remoteCSE, CSEBase | 9.6.8 |

Editor’s Note: This Table was based upon revision 0.4.2 and may be missing information from subsequent agreed contributions. It is expected to be updated as we further define resources. Cells marked “None Documented” indicate the status of 0.3.2, if no addition is needed to these cells then they should be marked “None” when this Table is finalised.

Editor’s Note: There are inconsistencies between resource type clauses as follows:

- <Group> does not list <subscription> as a child, but <subscription> lists group as a parent

### 9.6.1	Common Attributes

### -----------------------End of change 1---------------------------------------------