| CHANGE REQUEST |
| --- |
| Group Name:* | ARC #9.2 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Teleconference |
| Date:* | 2014-3-14 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | This contribution is to clean up the announce-able resource including the open issues. |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0001, Functional Architecture |
| Clauses/Sub Clauses* | 9.6.4, 9.6.5, 9.6.6, 9.6.7, 9.6.9, 9.6.10, 9.6.13, 9.6.15, 9.6.19 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution cleans up the open issues as follows:

-	To delete the Editor's Note: "To update the picture to include "link", "announceTo" and "announcedAttribute" attribute" since those are listed as common attributes

-	To mark 'MP/OP/NP' for the newly added attributes

-	To mark the 'lastModifiedTime' attribute as 'NP'

-	To delete the <instanceAnnc>

### -----------------------Start of change 1-------------------------------------------

### 9.6.4	Resource Type remoteCSE

A <remoteCSE> resource shall represent a remote CSE that is registered to the local CSE. CSE resources shall be located directly under the <CSEBase>.

Conversely each registered CSE shall also be represented as a sub-set of <remoteCSE> resource in the registering CSE's <CSEBase>.

For example, when CSE1 registers with CSE2, there will be two <remoteCSE> resources created: one in CSE1 <CSEBase1>/<remoteCSE2> and one in CSE2 <CSEBase2>/<remoteCSE1>.

Note that the creation of the two resources does not imply mutual registration. The <CSEBase1>/<remoteCSE2> is only local to CSE1 and is for its internal use.

Figure 9.6.4-1: Structure of <remoteCSE> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.4-1 (0 indicates the optionality of the child resource).

# Table 9.6.4-1: Child resources of <remoteCSE> resource

| Child Resource Name of <remoteCSE> | Child Resource Type | Multiplicity | Description | <remoteCSEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <application> | 0..n | See clause 9.6.5 | <applicatoinAnnc> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicyAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <mgmtObj> | 0..n | See clause 9.6.15 | <mgmtObjAnnc> |
| [variable] | <pollingChannel> | 0..n | See section 9.6.22. If requestReachability is FALSE, the CSE that created this <remoteCSE> should create a <pollingChannel> resource and perform long polling. | none |
| [variable] | <node> | 0..1 | See section 9.6.19. This child resource contains the node specific information only when the information represented by this resource is from a node of type ASN or MN. | <nodeAnnc> |

The <remoteCSE> resource shall contain the attributes described in Table 9.6.4-2.

# Table 9.6.4-2: Attributes of <remoteCSE> resource

| Attribute Name of <remoteCSE> | Multiplicity | RW/ RO/ WO | Description | <remoteCSEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | NP |
| expirationTime (eT) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 0..n | RW | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <remoteCSEAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. | OP |
| pointOfAccess (poA) | 0..n | RW | For request-reachable remote CSE it represents the list of physical addresses to be used to connect to it (e.g. IP address, FQDN). The attribute is absent if the remote CSE is not request-reachable. | OP |
| CSEBase (bRt) | 1 | WO | The URI of the CSEBase of the original CSE represented by remote CSE. | OP |
| CSE-ID | 1 | WO | The globally unique CSE identifier. | OP |
| Trigger-Recipient-ID | 0..1 | RW | See section 7.1.10 where this attribute is described. | OP |
| requestReachability | 1 | RW | If the CSE that created this <remoteCSE> can receive a request from other AE/CSE(s), this attribute is set to “TRUE” otherwise “FALSE”. NOTE: Even if this attribute is set to “FALSE”, it does not mean it AE/CSE is always unreachable by all entities. E.g., the requesting AE/CSE is behind the same NAT, so it can communicate within the same NAT. | OP |

<remoteCSE> and announced <remoteCSE> shall have different resourceType coding.

Editor's Note on CSE-ID: an alignment between CSE-ID and CSEBase is needed.

Editor's Note on CSEBase: the alignment with naming convention proposed for inter-M2M service provider is needed.

Editor's Note on child resources: child resources of <remoteCse> resource can accommodate listed resources and their announced versions.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### 9.6.5	Resource Type application

The <application> resource represents information about an Application Entity known to a given Common Services Entity.

Figure 9.6.5-1: Structure of <application> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.5-1 (0 indicates the optionality of the child resource)

# Table 9.6.5-1: Child resources of <application> resource

| Child Resource Name of <application> | Child Resource Type | Multiplicity | Description | <applicationAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicyAnnc> |
| software | <mgmtObj> | 1..n | See clause 9.6.15 for <mgmtObj>. This resource represents the software component (or components, if the multiplicity is greater than 1) that compose the application. This mgmtObj shall have at least the following <parameters> child resources of its "parameters" subresource: name (multiplicity 1) version (multiplicity 1) state (multiplicity 1) | <mgmtObjAnnc> |
| [variable] | <commCapabilities> | 1..n | Resource <commCapabilities> needs to be defined. This resource describes the communication capabilities (essentially the protocols) supported and used by the corresponding Application Entity over the Mca reference point to this CSE. | <commCapabilitiesAnnc> |
| [variable] | <pollingChannel> | 0..n | See section 9.6.22. When the local CSE of this AE is request-unreachable, the AE should create this <pollingChannel> resource and perform long polling. | none |

The <application> resource shall contain the attributes described in Table 9.6.5-2.

# Table 9.6.5-2: Attributes of <application> resource

| Attribute Name of <application> | Multiplicity | RW/ RO/ WO | Description | <applicationAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | NP |
| labels (lBs) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <applicationAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (e.g. "HeatingMonitoring") | OP |
| App-ID | 1 | RO | Application Identifier | OP |
| App-Inst-ID | 1 | RO | When the application resource refers to an actual application instance in the executing environment. | OP |
| pointOfAccess | 0..n | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g., IP address, FQDN, URI). This attribute shall be accessible only by the Application and the hosting CSE. | OP |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is managed and understood by the application; to be passed to the application | OP |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information only if this <application> resource is about ADN-AE and the <node> resource is existed in the parent resource, <CSEBase>. | OP |

Editor's Note: Cardinality of pointOfAccess attribute (0..n) needs to be investigated for all its occurrences.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

### 9.6.6	Resource Type container

This resource represents a container for data instances. It is used to share information among other entities and potentially to track the data. A <container> resource has no associated content, only attributes and child resources.

Figure 9.6.6-1: Structure of <container> resource
(only child resources and resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.6-1 (0 indicates the optionality of the child resource).

Editor's Note: Susbscription relation with this resource is for FFS.

Editor's Note: location resource relation with containers is for FFS.

# Table 9.6.6-1: Child resources of <container> resource

| Child Resource Name of <container> | Child Resource Type | Multiplicity | Description | <containerAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <instance> | 0..n | See clause 9.6.7 | <instanceAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <containerAnnc> |

This resource shall contain the attributes according to their multiplicity in Table 9.6.6-2 (0 indicates the optionality of the attribute).

# Table 9.6.6-2: Attribute of <container> resource

| Attribute Name of <container> | Multiplicity | RW/ RO/ WO | Description | <containerAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. If no accessConytolPolicyID is given at the time of creation, the accessControlPolicyID of the parent resource is linked to this attribute | MP |
| labels (lBs) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (st) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creator (cr) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | NP |
| versionTag (vT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <containerAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| maxNrOfInstances (mi) | 0..1 | RW | Maximum number of instances of <instance> child resources. | OP |
| maxByteSize (mb) | 0..1 | RW | Maximum number of bytes that are allocated for a <container> resource for all instances in the <container> resource. | OP |
| maxInstanceAge (ma) | 0..1 | RW | Maximum age of the instances of <instance> resources within the <container>. The value is expressed in seconds. | OP |
| currentNrOfInstances (ni) | 1 | RO | Current number of instances in a <container> resource. It is limited by the maxNrOfInstances. | OP |
| currentByteSize (nb) | 1 | RO | Current size in bytes of data stored in a <container> resource. It is limited by the maxNrOfBytes. | OP |
| latest (lt) | 0..1 | RO | Reference to latest instance, when present. | OP |
| locationID (LID ) | 0..1 | RW | URI of the resource where the attributes/policies that define how location information are obtained and managed. This attribute is defined only when the <container> resource is used for containing location information. | OP |
| ontologyRef (oR) | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the instances of the container. (see note) NOTE: The access to this URI is out of scope of oneM2M. | OP |

Editor's Note: Mechanisms for announcing are FFS.

Editor's Note: The container type is FFS.

Editor's Note: The following attributes are FFS depending on resource structure discussions:

- child: resources with child relation with the considered resource

- parent: resources with paren relation with the considered resource

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4---------------------------------------------

### 9.6.7	Resource Type instance

The <instance> resource represents a data instance in the container. The content of the instance is opaque to the M2M platform and it might even be encrypted. However, there is meta-data associated with an instance which shall be accessible.

Contrary to other resources, the <instance> resource cannot be modified once created, regardless of the accessControlPolicyID associated with the parent resource. An instance may be deleted explicitly or it may be deleted by the platform based on policies. If the platform has policies for the instance retention these shall be represented by the attributes maxByteSize, maxNrOfInstances and/or maxInstanceAge on the <container> resource. If multiple policies are in effect, the strictest policy shall apply.

The <instance> resource inherits the same access rights of the parent <container> resource, and does not have its own <accessControlPolicy> attribute.

Figure 9.6.7-1: Structure of <instance> resource
(only child resources and resource specific attributes are shown)

This resource shall contain the attributes according to their multiplicity in Table 9.6.7-1 (0 indicates the optionality of the attribute).

# Table 9.6.7-1: Attributes of <instance> resource

| Attribute Name of <instance> | Multiplicity | RW/ RO/ WO | Description |  |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |  |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. |  |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |  |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |  |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |  |
| versionTag (vT) | 1 | RO | See clause 9.6.1 where this common attribute is described. The versionTag attribute of the parent resource should be incremented first and copied into this versionTag attribute when a new instance is added to the parent resource. |  |
| typeOfContent (tOC) | 0..1 | WO | Optional type of the content included in the content attribute. This is media-type as defined in <reference to stage 3 document>. |  |
| contentSize (cS) | 1 | WO | Size in bytes of the content attribute. |  |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the instances of the container. If this attribute is not present, the instance inherits the ontologyRef from the parent <container> resource if present (see note) NOTE: Access to this URI is out of scope of oneM2M. |  |
| content (c) | 1 | WO | Actual opaque content of an instance. This may for example be an image taken by a security camera, or a temperature measurement taken by a temperature sensor. |  |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5---------------------------------------------

### 9.6.9	Resource Type schedule

The <schedule> resource contains scheduling information for delivery of messages.

Editor's Note: It is expected that the reachability period will be extended by the duration of a transaction which is currently occurring, but the details need further study.

The list of resources, which use <schedule> resource, is as follows.

TBD

Editor's Note: This list will be revised as resources are further progressed

The <schedule> resource shall represent scheduling information in the context of its parent resource. An Originator shall have the same access rights to the <schedule> resource as it has to its parent resource.

Figure 9.6.9-1: Structure of <schedule> resource 
(only resource specific attributes are shown)

The <schedule> resource shall contain the attributes described in Table 9.6.9-1.

# Table 9.6.9-1: Attributes of <schedule> resource

| Attribute Name of <schedule> | Multiplicity | RW/ RO/ WO | Description | <scheduleAnnc> Attributes |
| --- | --- | --- | --- | --- |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | NP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <scheduleAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| scheduleElement | 1..n | RW | Expresses time periods defined by second, minute, hour day of month, month, and year. Supports repeating periods, and wildcards. | OP |

### -----------------------End of change 5---------------------------------------------

### -----------------------Start of change 6---------------------------------------------

### 9.6.10	Resource Type locationPolicy

The <locationPolicy> resource in LOC CSF represents the method for obtaining and managing geographical location information of an M2M Node.

The actual location information shall be stored in the <instance> resource, a child resource of <container> resource.  The <container> resource has the locationId attribute which holds the URI of this <locationPolicy> resource as a linkage. The LOC CSF can obtain location information based on the attributes defined under <locationPolicy> resource, and store the location information in the target <container> resource.

Based on the locationSource attribute, the way of obtaining location information of an M2M Node can be differentiated: Network-based where the CSE on behalf of the AE obtains the target M2M Node's location information from Underlying Network, Device-based where the ASN is equipped with any location capable  modules or technologies (e.g. GPS) and is able to position itself, and Sharing-based where the ADN has no GPS and Underlying Network connection capability, but its location information can be retrieved from either ASN or MN.

NOTE:	Geographical location information is more than longitude and latitude.

Figure 9.6.10-1: Structure of <locationPolicy> resource
(only resource specific attributes are shown)

This resource shall contain the attributes according to their multiplicity in Table 9.6.10-1 (0 indicates the optionality of the attribute).

# Table 9.6.10-1: Attributes of <locationPolicy> resource

| Attribute Name of <locationPolicy> | Multiplicity | RW/ RO/ WO | Description | <locationPolicyAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 1..n | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | NP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <locationPolicyAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| locationSource | 1 | RW | Indicates the source of location information Network Based GPS Based Sharing Based | OP |
| locationUpdatePeriod | 0..1 | RW | Indicates the period for updating location information. If the value is marked '0' or not defined, location information is updated only when a retrieval request is triggered. | OP |
| locationTargetId | 0..1 | RW | The identifier to be used for retrieving the location information of a remote Node and this attribute is only used in the case that location information is provided by a location server. | OP |
| locationServer | 0..1 | RW | Indicates the identity of the location server. This attribute is only used in that case location information is provided by a location server. | OP |
| locationContainerID | 0..1 | RO | A URI of the <container> resource where the actual location information of a M2M Node is stored. | OP |
| locationContainerName | 0..1 | RW | A Name of the <container> resource where the actual location information of a M2M Node is stored. If it is not assigned, the Hosting CSE automatically assigns a name of the resource. Note: The created <container> resource related to this policy shall be stored only in the Hosting CSE. | OP |

### -----------------------End of change 6---------------------------------------------

### -----------------------Start of change 7---------------------------------------------

### 9.6.13	Resource Type group

The <group> resource represents a group of resources of the same or mixed types. The <group> resource can be used to do bulk manipulations on the resources represented by the members. The <group> resource contains an attribute that represents the members of the group and a virtual resource (the members) that allows verbs to be applied to the resources represented by those members.

When used as one of the permission holders in an <accessControlPolicy> resource, the group can be used to grant a collection of applications (represented by <application> resources) or CSEs (represented by <Entity> resources) permissions for accessing (Creating children, Retrieving, etc.) a resource.

Figure 9.6.13-1: Structure of <group> resource
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.13-1.

# Table 9.6.13-1: Child resources of <group> resource

| Child Resource Name of <group> | Child Resource Type | Multiplicity | Description | <groupAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| members | <Members> | 1 | See clause 9.6.14 | n/a |

# The <group> resource shall contain the attributes with the indicated multiplicity in Table 9.6.13-2

# Table 9.6.13-2: Attributes of <group> resource

| Attribute Name of <group> | Multiplicity | RW/ RO/ WO | Description | <groupAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creator (cr) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | NP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <groupAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| memberType (mT) | 1 | WO | It is the resource type of the member resources of the group if all member resources (including the member resources in any sub-groups) are of the same type. Otherwise, it's a type of 'mixed'. | OP |
| currentNrOfMembers (nM) | 1 | RO | Current number of members in a group. It is limited by the maxNrOfMembers. | OP |
| maxNrOfMembers (mM) | 1 | RW | Maximum number of members in the group. | OP |
| membersList (mL) | 1 | RW | List of zero or more member URIs referred to in the remaining of this specification as memberID. Each URI (memberID) should refer to a member resource or a (sub-) group resource of the group. | OP |
| membersAccessRightID(mAR) | 0..1 | RW | URI of the accessControlPolicy resource defining who is allowed to access the members attribute. | OP |
| memberTypeValidated(mTV) | 1 | RO | Denotes if memberType of all member resources of the group has been validated. | OP |
| consistencyStrategy (cS) | 0..1 | WO | This attribute determines how to deal with the <group> resource if the memberType validation fails.Which means delete the inconsistent member if the attribute is ABANDON_MEMBER; delete the group if the attribute is ABANDON_GROUP; set the memberType to "mixed" if the attribute is SET_MIXED. | OP |
| groupName (gN) | 0..1 | RW | Human readable name of the group. | OP |

### -----------------------End of change 7---------------------------------------------

### -----------------------Start of change 8---------------------------------------------

### 9.6.15	Resource Type mgmtObj

The mgmtObj resource contains management data which represents individual M2M management functions. It represents a general structure to map to external management technology (e.g. OMA DM [i.2], BBF [ref] TR-0069 [i.12] and LWM2M [ref]) data models.

Editor's note - add references?

Figure 9.6.15-1: Structure of <mgmtObj> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.15-1 (0 indicates the optionality of the child resource).

# Table 9.6.15-1: Child resources of <mgmtObj> resource

| Child Resource Name of <mgmtObj> | Child Resource Type | Multiplicity | Description | <mgmtObjAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <parameters> | 0..n | See clause 9.6.16. Collects multiple parameters or attributes for management purpose. A <parameters> resource can have zero or more other <parameters> sub-resources so as to form hierarchical structure, i.e. the management data for this specific <mgmtObj>. Such structure helps to import existing management objects as defined in OMA DM, BBF TR-069, LWM2M, or any other technology. | none |

The <mgmtObj> resource shall contain the attributes described in Table 9.6.15-2.

# Table 9.6.15-2: Attributes of <mgmtObj> resource

| Attribute Name of <mgmtObj> | Multiplicity | RW/ RO/ WO | Description | <mgmtObjAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See clause 9.6.1 where this common attribute is described | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described | MP |
| accessControlID (aRI) | 1 | RW | See clause 9.6.1 where this common attribute is described | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described | NP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <mgmtObjAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| mgmtDefinition | 1 | WO | Specifies the type of mgmtObj resource e.g. software, firmware, memory. The list of the value of the attribute can be seen in Annex D. | MP |
| objectID | 0..1 | WO | Contains a URN that uniquely identifies the external management technology data model used for this <mgmtObj> resource as well as the managed function and version it represents. This attribute shall be provided during the creation of the <mgmtObj> resource and shall not be modifiable afterwards. This is mandatory for the <mgmtObj>, for which the data model is not specified by oneM2M but mapped from external management technology data model specified in other device management protocols (e.g. OMA-DM, BBF TR-069 and LWM2M). | OP |
| objectPath | 0..1 | WO | Contains the local path of the external management object instance on the managed entity which is represented by the <mgmtObj> resource in the hosting CSE. This attribute shall be provided during the creation of the <mgmtObj>, so that the hosting CSE can correlate the created <mgmtObj> with the external management object instance on the managed entity for further management operations. It shall not be modifiable after creation. The format of this attribute shall be a local external management object path in the form as specified by existing management protocols. (e.g. "./anyPath/Fw1" in OMA DM, "Device.USBHosts.Host.3." in BBF TR-069). | OP |
| [objectAttribute] | 0..n | RW | Each [objectAttribute] is mapped from a leaf node of a hierarchical structured management object (including oneM2M data model and the existing management data models) based on the mapping rules below the table. | OP |
| description | 0..1 | RW | Text format description of mgmtObj. | OP |

When mapping resources from management technologies to a corresponding <mgmtObj> resource, the following rules shall apply:

The root resource of external management objects maps to the <mgmtObj> resource

For child resource of the root resource of specific technology:

Rule1: If the child external management object cannot have a child external management object, the external management object maps to the  [objectAttribute] attribute of the <mgmtObj> resource with the same resource name;

Rule2: If the child external management object can have another child external management object, the external management object maps to the <parameters> resource with the same resource name.

For the external management object that is mapped to the <parameters> resource, the child external management object of the external management object are mapped to the  [objectAttribute] attribute or to the <parameter> resource according to the Rule1 and Rule2.

### -----------------------End of change 8---------------------------------------------

### -----------------------Start of change 9---------------------------------------------

### 9.6.19	Resource Type node

The <node> resource represents specific information of a M2M Node that can be utilized by other oneM2M operations. For example, the CMDH CSF can determine when the CSE sends a request message to the target CSE based on the target CSE's reachability schedule. This resource type mainly contains the properties of an M2M Node such as reachability schedule, context information (e.g. memory and storage) and network topology.

This node specific information stored in this resource type such as memory and storage can be obtained either by the existing device management technologies (OMA DM, BBF TR-069 [i.12]) or any other way (e.g. through JNI (Java Native Interface)). Since <mgmtObj> resource type represents the management functions including both ways, the types of sub-resources are <mgmtObj> resource type.

The location of <node> resource can be differentiated according to the type of node.

ASN: under <CSEBase> of the ASN-CSE.

ADN: under <CSEBase> resource of the local CSE. The <application> resource regarding the ADN shall have the proper link (URI) to the <node> resource that contain node specific information of the ADN.

MN: under <CSEBase> of the MN CSE.

Editor's Note: ADN case needs to be defined

Editor's Note: More specific information regarding a node can be added.

Figure 9.6.19-1: Structure of <node> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.19-1 (0 indicates the optionality of the child resource).

Table 9.6.19-1: Child resources of <node> resource

| Child Resource Name of <node> | Child Resource Type | Multiplicity | Description | <nodeAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| memory | <mgmtObj> | 0..1 | This resource provides the memory (typically RAM) information of the node. (e.g. the amount of total volatile memory), See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| storage | <mgmtObj> | 0..n | This resource provides the storage (typically flash or disk) information of the node. (e.g. the amount of total writable persistent storage). See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| power | <mgmtObj> | 0..1 | The resource provides the power information of the node. (e.g. remaining battery charge). See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| networkTopology | <mgmtObj> | 0..1 | This resource describes the list of Nodes attached behind the MN node and its underlying relation among the nodes in the M2M Area Network. This attribute is defined in case the Node is MN. See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| schedule | <schedule> | 0..1 | This resource defines the reachability schedule information of the node. See clause 9.6.9 for <schedule>. | <scheduleAnnc> |

The <node> resource shall contain the attributes described in Table 9.6.19-2.

# Table 9.6.19-2: Attributes of <node> resource

| Attribute Name of <node> | Multiplicity | RW/ RO/ WO | Description | <nodeAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 1..n | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | NP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <nodeAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | OP |
| nodeID | 1 | RW | The ID of the Node which is specified in the resource type. This attribute is identical to M2M-Node-ID. | OP |
| hostedCSEID | 1 | RW | The ID of the CSEBase that is hosted on this node. | OP |

### -----------------------End of change 9---------------------------------------------