| CHANGE REQUEST |
| --- |
| Group Name:* | <WG2 |
| Source:* | Rajesh Bhalla, ZTE, rabhalla@ztetx.com |
| Format:* | ARC #9.3 |
| Date:* | <2014-03-xx |
| Contact:* | Rajesh Bhalla, ZTE, rabhalla@ztetx.com |
| Reason for Change/s:* | Cleanup of section 10.1 |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.4.2 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes changes for the cleanup of section 10.1 in TS-0001 v0.4.2. Addresses some Editor's Notes as well.

### -----------------------Start of change 1-------------------------------------------

## 10.1	Basic Procedures

The procedures in the following sub-clauses assume blocking Requests as described in clause 8.2.2

### 10.1.1	CREATE (C)

The CREATE procedure shall be used by an Originator CSE or AE to create a resource on a Receiver CSE (also called the Hosting CSE). The CREATE procedure has been divided in two, since there is a need to distinguish between Registration related Create and Non-registration related Create procedures.

The Registration related Create procedure is applicable for the following resource types only:

<application>, and

<remoteCSE>

Whereas Non-registration related Create procedure is applicable for all other resource types described in section 9.6.

#### 10.1.1.1	 Non-registration related CREATE procedure

This procedure is valid for all resources which are not related to Registration.

As a pre-condition for this procedure, the Originator has been already successfully authenticated, with the procedure described in XXX <xref to security related procedures>. Therefore all exceptions that are related to authentication failure are not described in this section.

Originator requests to create a resource by using the CREATE method. See clause 8.1.2 for the information to be included in the Request message.

Receiver, once the Originator has been succcessfully authenticated and that the Request is allowed by the given privileges, shall validate Request and shall create the resource.

# Figure 10.1.1-1: Procedure for CREATEing a Resource

Step 001: The Originator shall send the following information in the CREATE Request message:

op: 	C (Create);

to: 	URI of the target resource where the new resource should be created (parent resource)

# fr: 	ID of the Originator (either the AE or CSE)

Editor's Note: AE or CSE may not have the ID upon its registration request. Alternative information for fr is FFS.

nm:  optional name of the resource to be provided by the Originator, where permitted by the resource type as specified in section 9.6.

NOTE: Some of the resources defined in section 9.6 have a predefined name. For these resources the parameter nm is not applicable.

cn: 	attributes of the resource to be provided by the Originator. Of particular importance for the CREATE Request message is the common attribute  resourceType (section 9.6.1) which identifies the type of the resource to be Created.

In additoin, if an attribute in resource definition is identified as Mandatory and is of type RW, then such attribtue shall also be provided in the Request message.

Editor's Note: references to elements defined in sect 8 have been added here. They may be removed if we decide to move sect 8.1.2-4 to stage 3 doc. In this case, these references will be removed and sect 1 of this document would replace sect 8.1.2-4 in the TS-0001.

Step 002: The Receiver shall:

- Check if the Originator has the appropriate privileges for performing the Request. Privileges are part of the attribute accessControlPolicyID of the targeted resource. In case that such an attribute does not exist, the Receiver shall check the accessControlPolicyID of the parent resource.

Editor’s Note: how far should the Receiver go back to a parent to look for an accessControlPolicyID is FFS

- Verify that the suggested nm, if provided by the Originator in the Create Request message, does not already exist in its resource structure.

Assign an identifier to the resource to be created if a nm is not provided by the Originator.

Assign/modify default values for certain mandatory attributes of the resource, where allowed by the resource itself. if not provided by the Originator.

The Receiver shall assign a value to the following common attributes specified in section 9.6.1:

parentID;

creationTime;

expirationTime: If not provided by the Originator, the Receiver shall assign the maximum value possible (within the restriction of the Receiver policies). If the value provided by the Originator cannot be supported, due to either policy or subscription restrictions, the Receiver will assign a new value.

lastModifiedTime; which is equals to the creationTime

Any other RO (Read Only) attribtue within the restriction of the Receiver policies.

On successful validation of the Create Request, the Receiver shall create the requested resource.

Step 003: The Receiver shall respond with a Response message that shall contain the following information:

to: Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

# fr: Optional. ID of the Receiver.

cn:	URI and optionally the content of the created resource. The Receiver shall provide the content if the created resource contains attributes which were modified by the Receiver in step 002.

See clauses 8.1.3 and 8.1.4 for the information to be included in the Response message.

# General Exceptions:

- The targeted resource in to information does not exist. The Receiver responds with an Error.

The Originator does not have the privileges to Create a resource on the Receiver. The Receiver responds with an Error.

The resource with the specified name (if provided) already exists at the Receiver. The Receiver responds with an Error.

The provided information in cn is not accepted by the Receiver (e.g. missing mandatory parameter). The Receiver responds with an Error.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 10.1.1.2	 Registration related CREATE procedure

This section describes the CREATE procedure for <remoteCSE> and <application> resource types.

##### 10.1.1.2.1	 CSE Registration procedure

The procedure for CSE Registration follows the procedure described in section 10.1.1.1, but with some exceptions. Below is the detailed description on how to perform the CSE Registration and which part of the procedure deviates from the one described in section 10.1.1.1.

The Registration procedure requires the creation of two resources (a <remoteCSE> on the Receiver CSE and a <remoteCSE> on the Originator CSE) rather than one resource. The Registration procedure is always initiated by a CSE in the field domain and follows the restrictions described in section 6.2.9.

Receiver: Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), the Receiver shall allow the creation of the <remoteCSE> resource since at registration time there are no appropriate privileges associated with the Application yet.

Figure 10.1.1.2.1-1: Procedure for CREATEing a <remoteCSE> Resource

All the parameters of the Request and steps that are not indicated below, do not deviate from section 10.1.1.1.

Step 001: The Originator shall send the following information in the CREATE Request message:

fr:	Credentials of the Originator, CSE-ID, as defined in section 7.1.4

cn: 	Attributes of the resource to be provided by the Originator. Of particular importance for the CREATE Request message is the common attribute "resourceType" from section 9.6.1, which identifies the type of resource; and the attributes "CSE-ID" and "CSEBase". The "CSEBase" shall contain the absolute URI of the <CSEBase> resource at the Receiver.

Step 002:  The Receiver shall:

- This step from 10.1.1.1 cannot be performed for the Creation of <remoteCSE> resource.

All the other steps: 2-6, from step 002 from section 10.1.1.1 are still applicable

NOTE:     Optionally, if the M2M Service Provider supports inter-domain communication, the Receiver shall perform this step if the attribute “CSEBase” (part of the cn parameter of the request) contains the public domain of the CSE. The Receiver shall construct the domain as described in section XXX. The Receiver shall add an AAA or AAAA record in DNS with the public domain name of the Originator CSE and the IP address of the IN-CSE associated with the Originator

Editor’s Note: The section that should refer to section 6.5 somewhere where the public domains of CSEs are defined.

Editor's Note: Is there agreement to support inter-domain communication in Release-1? If not, the Note above and the associated Editor;s Notes, including this one, should be removed.

Step 003: See section 10.1.1.1

Step 004: The Originator, upon receipt of the CREATE response message, shall create a <remoteCSE> resource locally under its <CSEBase> resource. This resource is representing the Receiver CSE. The Originator shall provide the appropriate values to all mandatory parameters as described in section 9.6.4.

Step 005: The Originator may issue a RETRIEVE request towards the Receiver (same to as for the CREATE request message) to obtain the optional parameters of the <remoteCSE> resource created at the Receiver as for step 004 (e.g. label, accessControlPolicyID attributes). The RETRIEVE procedure is described in 10.1.2.

See sections 8.1.2 for the information to be included in the Request message.

Step 006: The Receiver verifies that the Originator has the appropriate privileges to access the information.

Step 007: The Receiver sends a RETRIEVE response message, according to the procedure described in 10.1.2.

See sections 8.1.3 and 8.1.4 for the information to be included in the Response message.

Step 008: The Originator shall update the created <remoteCSE> resource for the Receiver with the information obtained in step 007.

General Exceptions:

All exceptions from 10.1.1.1 are applicable; in addition the following exception may occur:

- The Originator does not have the privileges to retrieve the attributes of the Receiver CSE. The Receiver responds with an Error.

##### 10.1.1.2.2	 Application Registration procedure

The procedure for Application registration follows the procedure described in section 10.1.1.1 with the following exceptions:

Receiver, once the Originator has been successfully authorized (as described in section XXX), the Receiver shall allow the creation of the <application> resource according to the Access Control Policyt. The Receiver shall use, if present, the suggested name from the information parameter nm in the request. If the suggested name of the resource cannot be use (i.e., a resource with that name already exists) the Receiver shall reject the CREATE request. If the Request does not provide the optional nm, then the Receiver shall create the resource and assign a name to it.

Editor’s Note: which accessControlPolicy needs to be used is FFS.

Step 001: The Originator shall send the following information in the CREATE Request message:

fr: credentials of the Originator, App-Inst-ID, as defined in section 7.1.2

Editor’s Note: more investigation is needed in WG4 for clarify what will be the value of fr and in which section it will be described.

Step 002: for the <application> resource the Receiver cannot perform the action described in the first bullet of 10.1.1.1:

All the other parameters of the request and the following steps do not deviate from section 10.1.1.1.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 10.1.2	RETRIEVE (R)

The RETRIEVE operation shall be used for retrieving the information stored for any of the attributes for a resource at the Receiver CSE. The Originator CSE or AE may request to retrieve specific attribute(s) by including the identity of such attribute(s) in the Request message.

Originator requests to retrieve all attributes or specific attribute(s) of the target resource by using RETRIEVE Request. See clause 8.1.2 for the information to be included in the Request message. If only specific attribute(s) needs to be retrieved, the address of such attribute(s) (e.g. the URI) shall also be included in the cn information of the Request message.

Receiver once the Originator has been successfully authenticated; the Receiver performs local processing to verify the existence of requested resource and checks privileges for retrieving the information related to the resource. After the successful verification, the Receiver shall return the requested information, otherwise an error indication shall be returned.

# Figure 10.1.2-1: Procedure for RETRIEVing a Resource

Step 001: The Originator shall request to RETRIEVE information stored for any of the attribute(s) of a resource at the Receiver.

op:	R (Retrieve)

to: 	URI of the target resource

# fr:	 ID of the Originator (either the AE or CSE)

# cn:	Optional. If specific attribtue(s) needs to be retrieved, the address of such attribtue(s) (e.g., URI) shall be included in the cn parameter.

Step 002: The Receiver shall verify the existence of the resource and check if the Originator has appropriate privileges to retrieve information stored in the resource.

Step 003: The Receiver shall respond with a Response message that shall contain the following information:

to:	Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

# fr:	Optional. ID of the Receiver.

cn:	content of resource/attribtue(s) retrieved.

# General Exceptions:

- The targeted resource in to information does not exist. The Receiver responds with an Error.

- The Originator does not have privileges to retrieve information stored in the resource on the Receiver. The Receiver responds with an Error.

### 10.1.3	UPDATE (U)

The UPDATE operation shall be used for updating the information stored for any of the attributes at a target resource. Especially important is the "expirationTime", since a failure in refreshing this attribute may result in the deletion of the resource. The Originator CSE or AE can request to update  specific attribute(s) at the target resource by including the address (e.g., URI) of such attribute(s) in the Request message.

Originator requests to update any of the attributes at the target resource by using UPDATE Request message. The Originator shall send new (proposed) values for the attribute(s) that need to be updated. The UPDATE operation allows to modify the attributes (defined in section 9.6) that are indicated as “RW” (Read Write) for the specific resource type. See clause 8.1.2 for the information to be included in the Request message.

Receiver once the Originator has been successfully authenticated, the Receiver verifies the existence of the addressed resource, the validity of the attributes provided and the privileges to modify them, shall update the attributes provided and shall return a Response message to the Originator with the operation results as specified in clause 8.1.3.

# Figure 10.1.3-1: Procedure for UPDATing a Resource

Step 001: The Originator shall send the following information in the UPDATE Request message:

op:	U (Update)

to: 	URI to the target resource

# fr: 	ID of the Originator (either the AE or CSE)

cn: 	Information related to the attribute(s) to be updated at the target resource. The address of such attribute(s) (e.g. URI) and associated updated values in the cn parameter. Step 002: The Receiver shall validate if the Originator has appropriate privileges to perform the modification to the target resource. On successful validation, the Receiver shall update the resource as requested.

Step 003: The Receiver shall respond with a Response message that shall contain the following information:

to:	Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

# fr:	Optional. ID of the Receiver.

rs:	Operation result

# General Exceptions:

- The targeted resource in to information does not exist. The Receiver responds with an Error.

- The Originator does not have the privilege to modify the resource on the Receiver. The Receiver responds with Error.

- The provided information in the cn is not accepted by the Receiver. The Receiver responds with Error.

### 10.1.4	DELETE (D)

The DELETE operation shall be used by an Originator CSE or AE to delete a resource at a Receiver CSE. The DETETE procedure shall consist of the deletion of all related information of the target resource.

Originator requests to delete a resource by using a DELETE Request message. See clause 8.1.2 for the information to be included in the Request message.

Receiver once the Originator has been successfully authenticated, the Receiver verifies the existence of the requested resource, and the privileges for deleting the resource.

# Figure 10.1.4-1: Procedure for DELETING a Resource

Step 001: The Originator shall send a DELETE Request message to the Receiver.

op:	D (Delete)

to: 	URI of the target resource

# fr: 	ID of the Originator (either the AE or CSE)

Step 002: The Receiver shall verify the existence of the requested resource and if the Originator has the appropriate privilege to delete the resource. On successful validation, the Receiver shall check for children resources and delete all children resources and the associated references in parent resources and it shall remove the resource itself.

Step 003: The Receiver shall respond with a Response message that shall contain the following information:

to:	Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

# fr:	Optional. ID of the Receiver.

rs:	Operation result

# General Exceptions:

- The targeted resource in to information do not exist. The Receiver responds with an Error.

- The Originator does not have the privileges to delete the resource on the Receiver. The Receiver responds with an Error.

### 10.1.5	NOTIFY (N)

The NOTIFY operation shall be used for notifying information.

Originator: The Originator requests to notify information by using NOTIFY method. See clause 8.1.2 for the information to be included in a Request message.

Receiver: The Receiver responds to the Originator with the operation results as specified in clause 8.1.3.

# Figure 10.1.5-1: Procedure for NOTIFYing Information

Editor’s Note: not sure how to align this procedure with the other ones. The Receiver should also have a local processing, but if the addresse of the resource in the to is not one of the defined resource types what the receiver does is out of scope. However if the NOTIFY will correspons to a create instance then the procedures described in the create should apply. This operation needs more refining.

Step 001: A notification to be sent to the Receiver is triggered in the Originator.

Step 002: The Originator shall send the following information in the NOTIFY Request message:

op:	N (Notify)

to: 	URI where the notification should be sent to

# fr:	ID of the Originator (only a CSE)

cn:	Notification data and/or Notification reference

Step 003: The Receiver responds with a Response message that shall contain the following information:

rs: 	operation result

# General Exceptions:

- None identified.

Editor's note: General exceptions are FFS in particular for notification failures.

### -----------------------End of change 3---------------------------------------------