| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | FUJITSU |
| Format:* | Teleconference |
| Date:* | 2014-03-20 |
| Contact:* | Shingo Fujimoto,FUJITSU,shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | Resolving Editor’s Note regarding provisioning or discover Receiver’s address. |
| CR against: Release* | 1.0 |
| CR against: TS/TR* | oneM2M-TS 0001 Technical Architecture v 0.4.2 |
| Clauses/Sub Clauses* | 8.1.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Resolving Editor’s Note at 8.1.2 regarding provisioning or discover Receiver’s address.

### -----------------------Start of change 1-------------------------------------------

### 8.1.2	Request

Request from an Originator to a Receiver includes the following information:

- op: operation to be executed: Create (C), Retrieve (R), Update (U), Delete (D).

- to: URI of the target resource or the parent of the target resoruce, e.g. /m2m.provider1.com/netBase/temp1.

Editor's Note: This is made under the assumption that the CSE-ID is incorporated in the  URI of the target resource or the parent of the target resoruce.

- fr: ID of the Originator.

NOTE 1:	fr is used for access control of the target resource.

- mi: meta-information about the Request.

Editor's Note: Defaults for meta-information are FFS.

- cn: resource content to be transferred.

NOTE 2:	The to target resource needs to be known by the Originator. It can be known either by M2M Initial Provisioning Procedure (see 11.2), or by M2M Resource Discovery Procedure (see 10.2.5).

The op information shall indicate the operation to be executed at the Receiver:

- Create (C): a new resource addressable with to parameter is created.

- Retrieve (R): an existing to addressable resource is read and provided back to the Originator.

- Update (U): the content of an existing to addressable resource is replaced with cn new content.

- Delete (D): an existing to addressable resource and all its sub-resources are deleted from the Resource Storage.

- Notify (N):  information to the Receiver, processing on the Receiver is not indicated by the Originator.

Editor's Note: This is an initial list of the verbs. The need for more verbs is anticipated to cover all use cases, configuration and functions.

The to information shall address the target resource in the Receiver. The to information shall conform to section 9.3.1.The fr information shall be used by the Receiver to check the Originator identity for access permission verification.

The ty information shall be present in Request for the following operations:

- Create: ty is the type of the resource to be created.

The cn information shall be present in Request for the following operations:

- Create: cn is the content of the new resource with the resource type tag as in Table 9.2-1.

- Update: cn is the content to be replaced in an existing resource.

- Retrieve: cn is the filter to be applied for discovery purposes.

- Notify: cn is the notification information.

Note that the cn information can also be empty.

The mi information shall be as follows:

- ot: optional originating timestamp of when the message was built.

Example usage of the originating timestamp includes: to measure and enable operation (e.g. message logging, correlation, message prioritisation/scheduling, accept performance requests, charging, etc.) and to measure performance (distribution and processing latency, closed loop latency, SLAs, analytics, etc.)

- rqet: optional request expiration timestamp.

Example usage of the request expiration timestamp includes to indicate when request messages (including delay-tolerant) should expire due to their staleness being no longer of value, and to inform message scheduling/prioritisation. When a request has set request expiration timestamp to a specific time and the Request demands an operation on a Hosting CSE that is not the CSE currently processing the request, then the current CSE shall keep on trying to deliver the Request to the Hosting CSE until the request expiration timestamp time, in line with provisioned policies.

- rset: optional result expiration timestamp.

Example usage of the result expiration timestamp includes to indicate when result messages (including delay-tolerant) should expire due to expected staleness of the result, being no longer of value, and to inform message scheduling/prioritisation. It can be used to set the maximum allowed total request/result message sequence round trip deadline.

- rt: optional response type: indicates  what the response to the issued request shall contain and when the response is sent to the Originator:

- Acknowledgement: In case the request is accepted by the Local CSE, the Local CSE responds after acceptance with an Acknowledgement confirming that the Local CSE will further process the request.

- Result: In case the request is accepted by the Local CSE, the Local CSE responds with the result of the requested operation  after completion of the requested operation.

Example usage of the response type set to Acknowledgment: An Originator that is optimized to minimize communication time and energy consumption wants to express a Request to the local CSE and get an acknowledgement on whether the Request got accepted. After that the Originator may switch into a less power consuming mode and retrieve a Result of the requested Operation at a later time.

- rd: optional result destination:

- Local CSE: The Local CSE includes in the response to an accepted request a reference that can be used to access the status of the request and the result of the requested operation at a later time.

- Originator: The result of the requested operation needs to be sent as a notification to the Originator.

Example usage of the result destination set to Local CSE includes when the result content is extremely large, or when the result consists of multiple content parts from a target group which are to be aggregated asynchronously over time.

- rc: optional result content: Indicates what are the expected components of the result of the requested operation. The Originator of a request may not need to get back a result of an operation at all. This shall be indicated in the rc information. Which exact settings of rc are possible depends on the requested operation specified in op. Possible values of rc are:

- "resource": Only a representation of the requested resources will be returned as content, without any mention of the links of the requested resources to other resources. This is the default value.

- "resource;links-of-types:A,B,C": A representation of the requested resources, along with links of types A, B and C to other resources (possibly limited by a maximum number of retrieved links), will be returned as content.

Editor's Note: Link types A, B, C are examples and are FFS. Or should it be converted to a NOTE.

- "resource;links": A representation of the requested resources, along with all links to other resources (possibly limited by a maximum number of retrieved links), will be returned as content.

- "links": Only the links of the requested resources to other resources (possibly limited by a maximum number of retrieved links), without any representation of the actual resources requested, will be returned as content.

- "nothing": Nothing will be returned as content of the Response.

- "result-notification": A notification will be returned when the operation is completed.

Editor's Note: Details on what settings for rc are possible can be added at a later when the specific operations that can be requested are defined (e.g. register an AE, modify content of a container, etc.)

- rp: optional response persistence: indicates the duration for which the address containing the responses is to persist.

Example usage of response persistence includes requesting sufficient persistence for analytics to process the response content aggregated asynchronously over time. If a result expiration timestamp is specified then the response persistence should last beyond the  result expiration time.

- ri: Request Identifier mandatory over the Mca, Mcc, and Mcn reference points.

Example usage of request identifier includes enabling the correlation between a Request and one of the many received Responses.

- oet: optional operational execution time: indicates the time when the specified operation op is to be executed by the target CSE. A target CSE shall execute the specified operation of a Request having its operational execution time indicator set, starting at the operational execution time. If the execution time has already passed or if the indicator is not set, then the specified operation shall be immediately executed, unless the request expiration time, if set, has been reached.

Example usage of operational execution time includes asynchronous distribution of flows, which are to be executed synchronously at the operational execution time.

NOTE 3:	Time-based flows may not be able to be supported depending upon time services available at CSEs.

- ec: optional event category: Indicates the event category that should be used to handle this request. Event categories are impacting how Requests to access remotely hosted resources are processed in the CMDH CSF. Selection and scheduling of connections via CMDH are driven by policies that can differentiate event categories.

Editor's Note: Details on how to limit use of ec by AEs and relationship to provisioned policies are FFS.

Example usage of "event category" set to specific value X: When the request is demanding an operation to be executed on a Hosting CSE that is different from the Local CSE, the request may be stored in the CSE that is currently processing the request on the way to the Hosting CSE until it is allowed by provisioned policies for that event category X to use a communication link to reach the next CSE on a path to the Hosting CSE or until the request expiration timestamp is expired.

- da: optional delivery aggregation on/off: Use CRUD operations of <delivery> resources to express forwarding of one or more original requests to the same target CSE(s).

NOTE 4:	Since da is optional, there could be a default value to be used when not present in the Request. This parameter 	may not be exposed to AEs via Mca.

Example usage of delivery aggregation set on: The CSE processing a request shall use aggregation of requests to the same target CSE by requesting CREATE of a <delivery> resource on the next CSE on the path to the target CSE.

- gid: optional group request identifier: Identifier added to the group request that is to be fanned out to each member of the group.

- fc:  optional filter criteria: conditions for filtered retrieve operation are described in Table 8.1.2-1.

Table 8.1.2-1: Filter criteria conditions

| Condition tag | Multiplicity | Matching condition |
| --- | --- | --- |
| createdBefore | 0..1 | The creationTime attribute of the resource is chronologically before the specified value. |
| createdAfter | 0..1 | The creationTime attribute of the resource is chronologically after the specified value. |
| modifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically after the specified value. |
| unmodifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically before the specified value. |
| expireBefore | 0..1 | The expirationTime attribute of the resource is chronologically before the specified value. |
| expireAfter | 0..1 | The expirationTime attribute of the resource is chronologically after the specified value. |
| labels | 0..n | The labels attributes of the resource matches the specified value. |
| resourceType | 0..n | The resourceType attribute of the resource is the same as the specified value. It also allows discriminating between normal and announced resources. |
| sizeAbove | 0..1 | The contentSize attribute of the <instance> resource is equal to or greater than the specified value. |
| sizeBelow | 0..1 | The contentSize attribute of the <instance> resource is smaller than the specified value. |
| contentType | 0..n | The typeOfContent attribute of the <instance> resource matches the specified value |
| limit | 0..1 | Limitation the number of matching resources to the specified value. |
| attribute | 0..n | Attribute token name to be provided to reduce the scope of filtering to resource attributes. |

Example usage of filter criteria conditions in a HTTP query: an HTTP GET operation can be requested applying also a filter in the query part of the request itself:

GET /root?label=one&label=two&createdBefore=2014-01-01T00:00:00&limit=128

The example discovers a maximum of 128 resources matching the following logical condition: createdBefore < 2014-01-01T00:00:00 AND (label = one OR label = two).

Once the Request is delivered, the Receiver shall analyze the Request to determine the target resource.

If the target resource is addressing another M2M node, the Receiver shall route the request appropriately.

If the target resource is addressing the Receiver, it shall:

- Check the existence of to addressed resource.

- Identify the resource type with the tag value as in Table 9.2-1.

- Check the permission for fr Originator to perform the requested operation.

- Perform the requested operation (using cn content when provided).

- Perform the requested operation (using cn content when provided) according to the operational execution time.

- Depending on the request result content, respond to the Originator with indication of successful or unsuccessful operation results. In some specific cases (e.g. limitation in the binding protocol or based on application indications), the Response could be avoided.

The message flow procedure started with an Originator Request shall be considered closed when either:

- A Request is received with an expired rqet (request expiration timestamp).

- A Response is delivered to the Originator.

The requested operation at the Receiver is successfully completed and no Response is needed.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?