| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 ARC9.3 |
| Source:* | Huawei |
| Format:* | Teleconference |
| Date:* | <2014-03-23> |
| Contact:* | Qi Yu, Huawei Technologies, yuqi@huawei.com |
| Reason for Change/s:* | This CR is proposed to correct the attribute “hostedCSEID” of <node> resource. There is no CSE hosted on the node in case of ADN. |
| CR against: Release* | Release 1.0.0 |
| CR against: TS/TR* | TS-0001-Functional_Architecture-V0_4_2 |
| Clauses/Sub Clauses* | Section 9.6.19 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

# This CR intends to modify the attribute “hostedCSEID” of < node> resource. An Application Dedicated Node does not contain a Common Services Entity. Therefore, there is no related CSE hosted on this type of node.

### -----------------------Start of change 1-------------------------------------------

### 9.6.19	Resource Type node

The <node> resource represents specific information of a M2M Node that can be utilized by other oneM2M operations. For example, the CMDH CSF can determine when the CSE sends a request message to the target CSE based on the target CSE's reachability schedule. This resource type mainly contains the properties of an M2M Node such as reachability schedule, context information (e.g. memory and storage) and network topology.

This node specific information stored in this resource type such as memory and storage can be obtained either by the existing device management technologies (OMA DM, BBF TR-069 [i.12]) or any other way (e.g. through JNI (Java Native Interface)). Since <mgmtObj> resource type represents the management functions including both ways, the types of sub-resources are <mgmtObj> resource type.

The location of <node> resource can be differentiated according to the type of node.

ASN: under <CSEBase> of the ASN-CSE.

ADN: under <CSEBase> resource of the local CSE. The <application> resource regarding the ADN shall have the proper link (URI) to the <node> resource that contain node specific information of the ADN.

MN: under <CSEBase> of the MN CSE.

Editor's Note: ADN case needs to be defined

Editor's Note: More specific information regarding a node can be added.

Figure 9.6.19-1: Structure of <node> resource 
(only resource specific attributes are shown)

Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the child resources according to their multiplicity in Table 9.6.19-1 (0 indicates the optionality of the child resource).

Table 9.6.19-1: Child resources of <node> resource

| Child Resource Name of <node> | Child Resource Type | Multiplicity | Description | <nodeAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| memory | <mgmtObj> | 0..1 | This resource provides the memory (typically RAM) information of the node. (e.g. the amount of total volatile memory), See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| storage | <mgmtObj> | 0..n | This resource provides the storage (typically flash or disk) information of the node. (e.g. the amount of total writable persistent storage). See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| power | <mgmtObj> | 0..1 | The resource provides the power information of the node. (e.g. remaining battery charge). See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| networkTopology | <mgmtObj> | 0..1 | This resource describes the list of Nodes attached behind the MN node and its underlying relation among the nodes in the M2M Area Network. This attribute is defined in case the Node is MN. See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| schedule | <schedule> | 0..1 | This resource defines the reachability schedule information of the node. See clause 9.6.9 for <schedule>. | <scheduleAnnc> |

The <node> resource shall contain the attributes described in Table 9.6.19-2.

# Table 9.6.19-2: Attributes of <node> resource

| Attribute Name of <node> | Multiplicity | RW/ RO/ WO | Description | <nodeAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 1..n | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <nodeAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | OP |
| nodeID | 1 | RW | The ID of the Node which is specified in the resource type. This attribute is identical to M2M-Node-ID. | OP |
| hostedCSEID | 0..1 | RW | The ID of the CSEBase that is hosted on this node if the type of node is ASN or MN. | ?? |

### -----------------------End of change 1---------------------------------------------