| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | NEC |
| Format:* | TP9 |
| Date:* | 2014-01-13 |
| Contact:* | Barbara Pareglio (barbara.pareglio@neclab.eu); |
| Reason for Change/s:* | Cleaning up the section 5.2. |
| Clause/Sub Clause Affected* | 5.2 |
| Agenda Item:* | Contribution |
| Work item(s): |  |
| Document(s) Impacted* | oneM2M-TS 0001 Technical Architecture v 0 3 2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Proposal

This contribution proposes some editorial changes to section 5.2 Architecture Reference Model.

- The following “NOTE: The Mcc reference point between two CSEs may be supported between different M2M nodes.” Does not make too much sense since by definition the Mcc reference point is between different nodes. Probably the intention was to think about different types of node, but in that case the reference point cannot be the same.

- For consistency reason the term Infrastructure Domain is used instead of Network Domain

======================== START 1ST CHANGE ===========================

## 5.2	Architecture Reference Model

### 5.2.1	Functional Architecture

Figure 5.2.1-1illustrates oneM2M functional architecture.

Figure 5.2.1-1: oneM2M Functional Architecture

The oneM2M functional architecture in Figure 5.2.1-1 comprises of the following functions:

1.	Application Entity (AE): Application Entity provides Application logic for the end-to-end M2M solutions. Examples of the Application Entities can be fleet tracking application, remote blood sugar monitoring application, or remote power metering and controlling application.

2.	Common Services Entity (CSE):  A Common Services Entity comprises the set of "service functions" that are common to the M2M environments and specified by oneM2M. Such service functions are exposed to other entities through Reference Points Mca and Mcc. Reference point Mcn is used for accessing Underlying Network Service Entities.

Examples of service functions offered by CSE are: Data Management, Device Management, M2M Subscription Management, Location Services etc. Such "subfunctions" offered by a CSE may be logically apprehended as Common Services Functions (CSFs). Inside a Common Services Entity (CSE), some of the CSFs can be mandatory and others can be optional. Also, inside a CSF, some subfunctions can be mandatory or optional (e.g., inside a "Device Management" CSF, some of the subfunctions like "Application Software Installation", "Firmware Updates", "Logging", "Monitoring", etc. can be mandatory or optional).

3.	Underlying Network Services Entity (NSE):  An Underlying Network Services Entity provides services to the CSEs. Examples of such services include device management, location services and device triggering. No particular organization of the NSEs is assumed.

NOTE: Underlying Networks provide data transport services between entities in the oneM2M System. Such data transport services are not included in the NSE.

### 5.2.2	Reference Points

The following reference points are supported by the Common Service Entity (CSE). The "Mc(-) nomenclature is based on the mnemonic "M2M communications".

#### 5.2.2.1	Mca Reference Point

The Mca reference point designates communication flows between an Application Entity (AE) and a Common Services Entity (CSE). The Mca reference point shall allow an AE to use the services provided by the CSE, and for the CSE to communicate with the AE.

The services offered via the Mca reference point are dependent on the functionality supported by the CSE.

NOTE:  The AE and the CSE it invokes may or may not be co-located within the same physical entity.

#### 5.2.2.2	Mcc Reference Point

The Mcc reference point designates communication flows between two Common Service Entities (CSEs). The Mcc reference point shall allow a CSE to use the services of another CSE in order to provide needed functionality. The services offered via the Mcc reference point are dependent on the functionality supported by the CSEs.

Editor’s Note: In the event oneM2M develops specifications for more than one CSE implementation, the use of the Mcc reference point between them (for both intra-domain and inter-domain instances) would need elaboration, and is FFS. This requires coordination between the ARC and PRO working groups.

#### 5.2.2.3	Mcn Reference Point

The Mcn reference point designates communication flows between a Common Service Entity (CSE) and the Underlying Network Services Entity (NSE). The Mcn reference point shall allow a CSE to use the services (other than transport and connectivity services) provided by the Underlying NSE in order to provide the needed functionality.

The services offered via the Mcn reference point are dependent on the services provided by the Underlying NSE.

Editor's Note: The following NOTE should be moved into section 6.x.

NOTE: Information exchange between two M2M nodes assumes the usage of the transport and connectivity services of the Underlying Network Services Entity, which are considered to be the basic services.

Editor's Note: While allowing for different instantiations of the CS Function into different functional Entities, this specification follows the following guidelines/principles while specifying the interfaces on Mca, Mcc and Mcn reference points:

•	Specification of the interfaces on reference points Mca and Mcc are dependent on the functionality provided by the CSE.

•	Specification of the interfaces on reference point Mcn are dependent on the services provided by NSE, but it may take into account the functionality provided by the CSE.

#### 5.2.2.4	Mcc' Reference Point

The Mcc’ reference point designates communication flows between two Common Service Entities (CSEs) in infrastructure nodes that are oneM2M compliant and that resides in different M2M SP domains. Hence, it allows a CSE of an infrastructure node residing in the Infrastructure Domain of an M2M Service Provider to communicate with a CSE of another infrastructure node residing in the Infrastructure Domain of another M2M Service Provider to use its services,  and vice versa.

The actual trigger for this communication could be initiated elsewhere in the oneM2M network. Hence, Mcc’ extends the reachability of services offered over the Mcc reference point, or a subset thereof.

Note that the services offered via the Mcc’ reference point are dependent on the functionality supported by the CSEs.

======================== END 1ST CHANGE =============================