| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Barbara Pareglio, NEC, Barbara.pareglio@neclab.eu |
| Format:* | ARC#9.4 |
| Date:* | 2014-03-20 |
| Contact:* | Barbara Pareglio, NEC, Barbara.pareglio@neclab.eu |
| Reason for Change/s:* | Inconsistent usage of common attribute expirationTime |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.4.2 |
| Clauses/Sub Clauses* | 9.6.4, 9.6.5 and 9.6.16 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR proposes to change the expirationTime from Optional to Mandatory in 2 occoruncies in the resources, one for <application> and the other for <remoteCSE> and added the missing attribute in <paramters>.

### -----------------------Start of change 1-------------------------------------------

### 9.6.4	Resource Type remoteCSE

A <remoteCSE> resource shall represent a remote CSE that is registered to the local CSE. CSE resources shall be located directly under the <CSEBase>.

Conversely each registered CSE shall also be represented as a sub-set of <remoteCSE> resource in the registering CSE's <CSEBase>.

For example, when CSE1 registers with CSE2, there will be two <remoteCSE> resources created: one in CSE1 <CSEBase1>/<remoteCSE2> and one in CSE2 <CSEBase2>/<remoteCSE1>.

Note that the creation of the two resources does not imply mutual registration. The <CSEBase1>/<remoteCSE2> is only local to CSE1 and is for its internal use.

Figure 9.6.4-1: Structure of <remoteCSE> resource 
(only resource specific attributes are shown)

Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the child resources according to their multiplicity in Table 9.6.4-1 (0 indicates the optionality of the child resource).

# Table 9.6.4-1: Child resources of <remoteCSE> resource

| Child Resource Name of <remoteCSE> | Child Resource Type | Multiplicity | Description | <remoteCSEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <application> | 0..n | See clause 9.6.5 | <applicatoinAnnc> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicyAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <mgmtObj> | 0..n | See clause 9.6.15 | <mgmtObjAnnc> |
| [variable] | <pollingChannel> | 0..n | See section 9.6.22. If requestReachability is FALSE, the CSE that created this <remoteCSE> should create a <pollingChannel> resource and perform long polling. | ?? |
| [variable] | <node> | 0..1 | See section 9.6.19. This child resource contains the node specific information only when the information represented by this resource is from a node of type ASN or MN. | ?? |

The <remoteCSE> resource shall contain the attributes described in Table 9.6.4-2.

# Table 9.6.4-2: Attributes of <remoteCSE> resource

| Attribute Name of <remoteCSE> | Multiplicity | RW/ RO/ WO | Description | <remoteCSEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 0..n | RW | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <remoteCSEAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. | OP |
| pointOfAccess (poA) | 0..n | RW | For request-reachable remote CSE it represents the list of physical addresses to be used to connect to it (e.g. IP address, FQDN). The attribute is absent if the remote CSE is not request-reachable. | OP |
| CSEBase (bRt) | 1 | WO | The URI of the CSEBase of the original CSE represented by remote CSE. | OP |
| CSE-ID | 1 | WO | The globally unique CSE identifier. | OP |
| Trigger-Recipient-ID | 0..1 | RW | See section 7.1.10 where this attribute is described. | ?? |
| requestReachability | 1 | RW | If the CSE that created this <remoteCSE> can receive a request from other AE/CSE(s), this attribute is set to “TRUE” otherwise “FALSE”. NOTE: Even if this attribute is set to “FALSE”, it does not mean it AE/CSE is always unreachable by all entities. E.g., the requesting AE/CSE is behind the same NAT, so it can communicate within the same NAT. | ?? |

<remoteCSE> and announced <remoteCSE> shall have different resourceType coding.

Editor's Note on CSE-ID: an alignment between CSE-ID and CSEBase is needed.

Editor's Note on CSEBase: the alignment with naming convention proposed for inter-M2M service provider is needed.

Editor's Note on child resources: child resources of <remoteCse> resource can accommodate listed resources and their announced versions.

### 9.6.5	Resource Type application

The <application> resource represents information about an Application Entity known to a given Common Services Entity.

Figure 9.6.5-1: Structure of <application> resource 
(only resource specific attributes are shown)

Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the child resources according to their multiplicity in Table 9.6.5-1 (0 indicates the optionality of the child resource)T

# Table 9.6.5-1: Child resources of <application> resource

| Child Resource Name of <application> | Child Resource Type | Multiplicity | Description | <applicationAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicyAnnc> |
| software | <mgmtObj> | 1..n | See clause 9.6.15 for <mgmtObj>. This resource represents the software component (or components, if the multiplicity is greater than 1) that compose the application. This mgmtObj shall have at least the following <parameters> child resources of its "parameters" subresource: name (multiplicity 1) version (multiplicity 1) state (multiplicity 1) | <mgmtObjAnnc> |
| [variable] | <commCapabilities> | 1..n | Resource <commCapabilities> needs to be defined. This resource describes the communication capabilities (essentially the protocols) supported and used by the corresponding Application Entity over the Mca reference point to this CSE. | <commCapabilitiesAnnc> |
| [variable] | <pollingChannel> | 0..n | See section 9.6.22. When the local CSE of this AE is request-unreachable, the AE should create this <pollingChannel> resource and perform long polling. | ?? |

The <application> resource shall contain the attributes described in Table 9.6.5-2.

# Table 9.6.5-2: Attributes of <application> resource

| Attribute Name of <application> | Multiplicity | RW/ RO/ WO | Description | <applicationAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <applicationAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (e.g. "HeatingMonitoring") | OP |
| App-ID | 1 | RO | Application Identifier | OP |
| App-Inst-ID | 1 | RO | When the application resource refers to an actual application instance in the executing environment. | OP |
| pointOfAccess | 0..n | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g., IP address, FQDN, URI). This attribute shall be accessible only by the Application and the hosting CSE. | ?? |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is managed and understood by the application; to be passed to the application | OP |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information only if this <application> resource is about ADN-AE and the <node> resource is existed in the parent resource, <CSEBase>. | ?? |

Editor's Note: Cardinality of pointOfAccess attribute (0..n) needs to be investigated for all its occurrences.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?