| CHANGE REQUEST |
| --- |
| Group Name:* | ARC9.4 |
| Source:* | Yali Guo, Haier, Yali.guo@haierubic.com |
| Format:* | Teleconference |
| Date:* | 2014-03-21 |
| Contact:* | Yali Guo, Haier, Yali.guo@haierubic.com |
| Reason for Change/s:* | To make clarification on the M2M identifiers used for the triggering request message over Mcn interface |
| CR against: Release* | Rel-1 |
| CR against: TS/TR* | oneM2M-TS 0001 Technical Architecture v 0.4.2 |
| Clauses/Sub Clauses* | 7.1.7, 7.2, 8.4.2.1, Annex B.6.1.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution makes clarification on the M2M identifiers used for the triggering request message over Mcn interface.

Refers to the Annex B.6.1.2 of the Device Triggering procedure defined by 3GPP, the IN-CSE ID and the M2M-Request-ID are expected by the underlying network, they should be added  in the device triggering request message over Mcn interface.

For the M2M-Request-ID over Mcn, if there’s an 1:1 mapping or 1:N mapping between a Mca request and the Mcn requests, the IN-CSE could include the same received M2M Request Identifier in the Mcn requests. But for the N:1 mapping between Mca requests and a Mcn request, i.e. several requests from AE to the target ASN/MN-CSE mapping to the same trigger request over Mcn, the IN-CSE should create a M2M-Request-ID over Mcn and maintain a binding between the created M2M-Request-ID and the multiple M2M Request Identifiers received from the AEs.

There’s still a FFS exist for the uniqueness of M2M-Ext-ID, as this M2M-Ext-ID has been defined in 3GPP to be globally unique, see following copied for 3GPP TS 23.003. This contribution remove the FFS to clarify this.

“The combination of Local Identifier and Domain Identifier makes the External Identifier globally unique.”

## Proposal

- The M2M-Request-ID may be created by the CSE for the requests over Mcn.

- Clarify the M2M-Ext-ID is globally unique.

- Add M2M-Request-ID and M2M-Ext-ID in the triggering request over Mcn

- Fix a small editorial error.

### -----------------------Start of the 1st change -------------------------------------------

### 7.1.7	M2M Request Identifier (M2M-Request-ID)

This is an identifier that tracks a Request initiated by an application over the Mca reference point, and by a CSE over the Mcc and Mcn reference points, if applicable, end to end. It is also included in the Response to the Request over all the above reference points.

To enable applications to track Requests and corresponding Responses over the Mca reference point, applications shall include a distinct M2M Request Identifier per request over the Mca Reference point to the CSE for any initiated request.

'The CSE shall make such M2M Request Identifier recived from the AE globally unique by appending its CSE-ID to it.

If the CSE creates an M2M Request Identifier, then the CSE shall maintain a binding between the M2M Request Identifier received from the AE and the CSE M2M Request Identifier it created in its interactions towards other peer CSEs or NSEs. The CSE shall include the M2M Request Identifier received from the AE in its Response to the application. This binding shall be maintained by the CSE until the Request is deposed off. Note that the Request initiated by the CSE could be the result of an application request, or a request initiated autonomously by the CSE to fulfil a service.

A CSE receiving a Request from a peer CSE shall include the received M2M Request Identifier in all additional Requests unspanned (i.e.1:1) it has to generate (including propagation of the incoming Request) and that are associated with the incoming Request, where applicable.

The CSE may include the same received M2M Request Identifier from AE/a peer CSE or create an M2M Request Identifier in its interactions with the Underlying Network Service Entity, over the Mcn reference point where applicable.

Note that the M2M Request Identifier can be made globally unique by including the CSE-ID in combination with any random number.

Editor's Note:  Bring in a contribution to indicate where this information will carried.

Editor's Note:  In order to allow interworking, how the platform understands whether the Request Identifier is globally unique or not needs to be specified.

### -----------------------Start of the 2nd change -------------------------------------------

## 7.2	M2M Identifiers lifecycle and characteristics

# Table 7.2-1: M2M Identifiers lifecycle and characteristics

| Identifier | Assigned by | Assigned to | Assigned during | Lifetime | Uniqueness | Used during | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| M2M Service Provider Identifier | Out of scope | AE, CSE | Out of scope | Out of scope | Global | FFS |  |
| Application Instance Identifier | FFS | AE | AE instantiation | Application Instance Registration | Global | - Application instance Registration - Security Context Establishment - Other operations FFS | Security requirements apply for Security Context Establishment |
| CSE Identifier | M2M SP | CSE | Security Provisioning | Life of the CSE | Global | - Information flows (clause 10) - Security Context Establishment | Secuirty requirements apply for Secuirty Context Establishment |
| M2M Node Identifier | Out of Scope | M2M Node hosting CSE | Pre-provisioned | Life of the M2M Node | Global | Security provisioning (FFS) | Needs to be Read Only |
| M2M Subscription Identifier | M2M SP | Application Entities, and one or more CSEs belonging to the same M2M subscriber | At service signup | Life of the Subscription with the MM SP | Global | - Charging and Information Recorded - Other operations are FFS | Multiple CSEs can be allocated the same M2M Subscription Identifier |
| M2M-Request-ID | Mcc: CSE Mca: Application Instance Mcn: CSE | A request initiated by an AE or CSE | Mcc: When a request is initiated by a CSE, or handling of a request received by a CSE. Mca: When a request is initiated by an AE Mcn: When a request is initiated by a CSE, or handling of a request received by a CSE. | Equal to the lifetime of the Request and its corresponding Response | Mcc: Global Mca: Local or global Mcn: Global | Requests and corresponding responses |  |
| External Identifier | Manual mode: Jointly between the Underlying Network provider and M2M SP, where applicable. Plug-And- Play: FFS | M2M Node belonging to a CSE that wants to utilize services of the Underlying Network. | Manual Mode: Administrative Agreement. Plug-And- Play: FFS | Life time of the CSE. | Global | Requests initiated by a CSE over the Interface, where applicable. |  |
| Underlying Network Identifier | M2M SP | Underlying Networks | Pre-provisioned | Life of the Underlying Network | Local to M2M SP domain | UL Network selection |  |
| Trigger Recipient Identifier | Execution Environment | ASN/MN-CSE instantiation | ASN/MN-CSE start-up or wake-up | CSE instance lifetime | Execution Environment-wide | Device Trigerring procedures |  |

### -----------------------Start of the 3rd change -------------------------------------------

#### 8.4.2.1	Triggering procedure for targeting ASN/MN-CSE

This case describes the scenario where IN-CSE targets an ASN/MN-CSE (which is register with the IN-CSE) for the Device Triggering request.

The Figure 8.4.2 1-1 shows the general procedure for Device Triggering and, if required, for establishment of connectivity between IN-CSE and the Field Node.

Figure 8.4.2 1-1: Device Triggering general procedure for CSE

NOTE:     IN and ASN/MN are assumed to be connected through the same Underlying Network.

NOTE:     The Device Triggering Handler is a functional entity that receives the device triggering request, and it is dependent on the Underlying Network. The Device Triggering Handler is not part of the specification is left to implementors.

Pre-condition

The CSE which is the target of the device triggering has to be registered with the IN-CSE.

The CSE-PoA for the ASN/MN-CSE already contains either an IP address or none.

[optional] Step-1: Request to targeted ASN/MN-CSE

The IN-AE requests to perform one of the CRUD operation on a resource residing on the ASN/MN-CSE, the request is sent via the Mca reference point to the IN-CSE.

Step-2: Underlying network selection

The IN-CSE selects the Underlying Network and the mechanism to deliver the triggering request to the Underlying Network according to the configuration for connected Underlying Networks.

For example for 3GPP access network IN-CSE might be allowed to use Tsp, Tsms and GSMA OneAPI, but the preferred mechanism could be Tsp.

Step-3: Device Triggering request

IN-CSE issues the device triggering request to the selected Underlying Network.

The Underlying Network dependent Device Triggering procedure is executed as described in Annexes.

Some information that needs to be provided to the selected Underlying Network for performing device triggering is:

M2M-Ext-ID associated with the ASN/MN-CSE as the target of the triggering request (see 7.1.8).

Trigger-Recipient-ID associated with the ASN/MN-CSE (see section 7.1.10). For example when 3GPP Underlying Network is used this identifier could map to Application-Port-ID.

IN-CSE ID which could be used by the underlying network to authorize the IN-CSE for device triggering.

M2M-Request-ID used to track the trigger request.

NOTE: The above Trigger-Recipient-ID is sent at registration.

Editor’s Note: M2M-Ext-ID is set on registration, how the IN-CSE gets it is FFS.

Editor’s Note: The above list with information to be sent over Device Triggering request on the underlying network is not complete and/or limiting. What is needed is for FFS.

Step-4: Underlying Network Specific Device Triggering procedure

Device Triggering processing procedure is performed between the Underlying Network and the target Node which hosts the ASN/MN-CSE.

Step-5: Device Triggering response

The IN-CSE receives a response for the Device Triggering request via Mcn reference point.

The Underlying Network dependant Device Triggering response procedure is described in Annexes.

Step-6: ASN/MN-CSE Receives Device Trigger

[optional] Step-7 Connection establishment

In case that it is required by the Device Triggering request, connectivity is established between the ASN/MN-CSE and the IN-CSE and the renewal of the PoA might be needed.

### -----------------------Start of the 4th change -------------------------------------------

#### B.6.1.2	IN-CSE initiated connectivity establishment procedure over Tsp

Connection Establishement between IN-CSE and ASN/MN-CSE

Whenever the IN-CSE requires to establish a connection towards another entity (i.e. ASN-CSE), the Device Triggering procedure over the Tsp interface as described in [TS 23.682] shall be used.

# Figure B.6.1.2-1: IN-CSE initiated connectivity establishment

Pre-condition

The CSE which is the target of the device triggering has to be registered with the IN-CSE. The IN-CSE checks the state information of the target device, which some of this information is the result of previous connection establishment or triggering requests, such as the case of power-off, dormant and/or connected state. The IN-CSE decides its next action, i.e., if it needs to start Triggering or report to IN-AE about the unavailability to perform the request.

The PoA for the ASN/MN-CSE either already contain an IP address which is not valid anymore or no address at all, or FQDN does not resolve to a valid IP address. This is a pre-requisite for performing the device triggering procedure.

Editor’s Note:  How the M2M-Ext-ID is obtained is FFS. The ID should at least be available somewhere in the ASN/MN-CSE resource or the IN-CSE should keep a map between M2M-Ext-ID and CSE-ID, so that the IN-CSE can access the information when needed.

[optional] Step 1: Request targeted to ASN/MN-CSE

The IN-AE requests to perform one of the CRUD operation on a resource residing on the ASN/MN-CSE, the request is sent via the Mca reference point to the IN-CSE.

Editor’s Note: In case of any request as described in section 8.1 for resource manipulation over Mca reference point, the request indicates by the address of the target resource URI. In order to reach the specified resource a Device Triggering may be required.

Step 2: DNS Query / Response

The IN-CSE determines the need to trigger the ASN-CSE.

If the IN-CSE has no contact details for a contact MTC-IWF, it may determine the IP address(es)/port(s) of the MTC-IWF by performing a DNS query using the M2M-Ext-ID (M2M External Identifier) or using a locally configured MTC-IWF identifier.

Editor's Note: Mechanisms other than DNS query could be used for determining the IP address(es)/port(s) of the MTC-IWF. These are FFS.

Step-3: Device Triggering Request

The IN-CSE buffers the original request informaiton and sends the Trigger Request message that contains information as specified in [3GPP TS23.682]:

M2M-Ext-ID or MSISDN,

SCS-Identifier, (is set to the IN-CSE ID)

Trigger reference number, (used to correlate the request with the response, is set to the M2M-Request-ID)

Validity period, (which indicated how long the request is valid)

Priority, (this field only allows to set the priority on or off)

Application Port ID, (is set to the ASN-CSE Trigger-Recipient-ID since it is the triggering application addressed in the device from 3GPP point of view)

Trigger payload, (optional information can be set to the payload)

NOTE:     In case that the Device Triggering request is for M2M Service Connection setup request as the present flow, it is assumed that the target CSE (i.e. ASN-CSE) when it is woken upreceived the trigger it shall connect automatically to the IN-CSE where it is registered. The information of the IN-CSE may be pre-stored in the target CSE (i.e. ASN-CSE). Therefore it is assumed that the trigger payload does not include optional information and the target CSE is registered to only one IN-CSE. How to use the optional part of the trigger payload is described as below.

Acknowledge

Once, 3GPP-MTC-IWF receives the Trigger Request, it will ask the HSS to determine if the IN-CSE is authorized to perform the triggering to the target CSE (i.e., ASN-CSE) and the HSS will resolve the M2M-Ext-ID to IMSI (or MSISDN). Then the 3GPP-MTC-IWF acknowledges to the IN-CSE with the confirmation of the received Device Triggering Request.

Step-4: Device Triggering delivery procedure

The MTC-IWF will initiate the  T4 trigger delivery procedure according to the 3GPP TS 23.682 [i.11], based on the information received from HSS and local policy.

NOTE:     3GPP Network Entities (e.g. SMS-SC) may select appropriate device triggering mechanism (e.g. SMS based or SIP based via IP-SM-GW) according to the device capabilities.

Step 5: ASN-CSE receives the trigger

As a result of the device triggering procedure the addressed ASN/MN-CSE is initiated, in this case of the flow the ASN-CSE will be started according to the received Application Port ID by the UE.

NOTE:     In case that the UE received optional part of the trigger payload, it is assumed that the information would be transmitted to the started application inside the UE.

Step 6: Device Triggering report

Request:

The MTC-IWF sends the Device Trigger Report message (containing the M2M-Ext-ID or MSISDN and trigger reference number)  to the  IN-CSE with a cause value indicating whether the trigger delivery succeeded or failed and the reason for the failure.

Acknowledge:

IN-CSE acknowledges to the MTC-IWF with the conformation of the received Device Triggering Report

[optional] Step 7: Connection establishment procedure

The ASN-CSE will perform the Connection establishment procedure as described in B.6.1.1 and oneM2M TS-0003 [i.xx] for Secure Connection establishment.

As a result of this procedure now the initial request over the reference point Mcc can be executed.

[optional] Step 8: PoA/Reachability state updated

Once the connection over Mcc is established, in the IN-CSE the PoA of the ASN-CSE shall be updated with the new established IP address and the IN-CSE holds the reachability state of the ASN/MN-CSE.

[optional] Step 9: Re-sending of original request

As a result of step 7, the communication is established and now the initial request with the information stored in the buffer of the IN-CSE at Step 3 can be re-issued over the reference point Mcc.

In the flow presented above not all parameters allowed in the Device Triggering Request message from 3GPP Tsp interface are used. Optionally the following cases are allowed:

By providing a payload which may contain:

Either actual content information (as permitted by the limitation of the payload parameter). For example;

It could contain a resource (or attribute) identifier (as expressed inside the ASN-CSE) and an actual content for the resource (or attribute) of any of the resources stored in the ASN-CSE.

Or any other instructions, like to initiate a specific procedure. For example, execute a command.

Or it could contain of the URI of an entity outside the oneM2M domain where the target ASN-CSE should connect to. If a URI is provided, in this case the steps 7, 8 and 9 of the previous flow cannot be performed since the connection establishment is not performed between two oneM2M entities, therefore how the actual setup is performed it is outside the scope of this specification.

Editor’s Note: What information could be transported in the payload is FFS.

### -----------------------End of changes ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?