| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Heedong Choi, LG Electronics, heedong.choi@lge.com Barbara Pareglio, NEC, Barbara.pareglio@neclab.eu |
| Format:* | ARC#10 |
| Date:* | 2014-04-08 |
| Contact:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Reason for Change/s:* | Cleanup clause 10.2.11 |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001 v0.4.2 |
| Clauses/Sub Clauses* | 10.2.11 <subscription> Resource Procedures |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes a cleanup of  clause 10.2.11 <subscription> Resource Procedures. The detailed changes are follows:

- Removed “Editor’s Note” and added some sentences

- Filled in and modified tables related CRUD for the <subscription> resource

- Changed “access right” into “access privilege” and “permission” into “privilege” due to links with the consensus term

- Corrected minor mistakes such as section maker, typo

- Aligned terminology and table template with other procedures

## -----------------------Start of change 1-------------------------------------------

### 10.2.11	<subscription> Resource Procedures

#### 10.2.11.1	Introduction

An Originator can create a <subscription> resource on a subscribed-to resource Hosting CSE to be notified when the resource is modified. After successful <subscription> resource creation, the Hosting CSE shall notify the Originator of a subscribed-to resource modification that meets conditions configured in the <subscription> resource.

A subscription shall be represented by a <subscription> resource (see clause 9.6.8). This allows manipulation of the subscription in a resource oriented manner, e.g. the conditions of a subscription may be modified by modifying a <subscription> resource, or a resource subscriber may unsubscribe by deleting the <subscription> resource.

The following clauses describe procedures for Creation, Retrieval, Update and Deletion of a <subscription> resource.

#### 10.2.11.2	Create <subscription>

This procedure shall be used to request a new subscription to be notified for the modifications of a subscribable resource. Generic create procedure is described in clause 10.1.1.1.

Originator: The Originator can be an AE or a CSE. The Originator shall request to create a <subscription> resource. The Request shall address a subscribable resource.

The Request shall include notificationURI(s).

Receiver: (which is also the Hosting CSE) shall validate the followings:

- if the subscribed-to resource, addressed in the to parameter in the Request, is a subscribable resource;

- if the Originator has privileges for retrieving to the subscribed-to resource;

- if the Originator has privileges to send notifications to the entity(ies) hosting notificationURI(s) when the Originator is not a hosting notificationURI;

- if the hosting CSE has privileges to send notifications to the entity(ies) that hosting notificationURI(s).

Editor's Note: The validation process described in the last two bullet points above needs to be investigated further, This is FFS.

If all those checks are successfully done, the Hosting CSE shall send positive Response to the Originator.

Table 10.2.11.2-1: <subscription> CREATE

| CREATE Description |
| --- |
| Pre-Conditions | The Originator configures proper permissions and access rights described above |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: The representation of the <subscription> resource for which the attributes are described in clause 9.6.8 The following attributes from clause 9.6.8 are mandatory for the request: “resourceType” which shall be set to the appropriate tag that identify the subscription resource as defined in 9.6.1 “notificationURI” “notificationStructure” All attributes indicated as optional in clause 9.6.18 are optional for the request. |
| Local processing on Hosting CSE | Check access privileges regarding creation of the <subscription> resource and sending notification to the notificationURI. |
| Information on Response message | No change from the basic procedure in clause 10.1.1.1 |
| Post-Conditions | None |
| Exceptions | All exception described in the basic procedure (clause 10.1.1.1) are applicable. |

#### 10.2.11.3	Retrieve <subscription>

This procedure shall be used to retrieve information of a subscription such as notificationURI, filterCriteria, expirationTime, etc. Generic retrieve procedure is described in clause 10.1.2.

Originator: The Originator can be an AE or a CSE. The Request shall address a <subscription> resource or one of its attributes.

Receiver: once the Originator has been successfully authenticate and access to resource has been granted by the Receiver (which is also the Hosting CSE), the Receiver shall create the <subscription> resource.

Table 10.2.11.3-1: <subscription> RETRIEVE

| RETRIEVE Description |
| --- |
| Pre-Conditions | The Originator has RETRIEVE permission to the subscription resource |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table. |
| Local processing on Hosting CSE | No change from the generic procedure. |
| Information on Response message | No change from the generic procedure |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedure (section 10.1.2) are applicable. |

#### 10.2.11.4	Update <subscription>

This procedure shall be used to update an existing subscription, e.g. extension of its lifetime or the modification of the notificationURI. Generic update procedure is described in clause 10.1.3.

Originator: The Originator can be an AE or a CSE. The Originator may send new value(s) for read-write attribute(s) of a <subscription> resource.

Receiver: once the Originator has been successfully authenticated and access to the resource is granted by the Receiver (which is also the Hosting CSE), the Receiver shall update the <subscription> resource.

Table 10.2.11.4-1: <subscription> UPDATE

| UPDATE Description |
| --- |
| Pre-Conditions | The Originator has UPDATE permission to the subscription resource |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table. |
| Local processing on Hosting CSE | No change from the generic procedure |
| Information on Response message | No change from the generic procedure |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedure (section10.1.3) are applicable. |

#### 10.2.11.5	Delete <subscription>

This procedure shall be used to unsubscribe an existing subscription. Generic delete procedure is described in clause 10.1.4.

Originator: The Originator can be an AE or a CSE.

Receiver: once the Originator has been successfully authenticated and access to the resource has been granted by the Receiver (which is also the Hosting CSE), the Receiver shall delete the <subscription> resource.

Table 10.2.11.4-1: <subscription> DELETE

| DELETE Description |
| --- |
| Pre-Conditions | The Originator has DELETE permission to the <subscription> resource |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table. |
| Local processing on Hosting CSE | No change from the generic procedure |
| Information on Response message | No change from the generic procedure |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedure (section 10.1.4) are applicable. |

## -----------------------End of change 1-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?