| CHANGE REQUEST |
| --- |
| Group Name:* | TP#10 |
| Source:* | LG Electronics |
| Format:* | Plenary |
| Date:* | 2014-03-28 |
| Contact:* | Hongbeom Ahn, LG Electronics, Hongbeom.ahn@lge.com |
| Reason for Change/s:* | This CR proposes to change some description to point out that the <node> resource type contains physical information or virtual representation of a oneM2M Node. |
| CR against: Release* | Release 1.0.0 |
| CR against: TS/TR* | TS-0001-Functional_Architecture-V0_4_2 |
| Clauses/Sub Clauses* | Section 9.6.19 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

# It was discussed that the description of <node> resource has been mis-used in the email discussion.

# Nodes are considered as functional objects and mapping to either physical objects or virtual object, case-by-case. This CR proposes to change some description to point out that the <node> resource type contains physical information or virtual representation of a oneM2M Node.

# The representation of logical information(schedule) will be taken out. This will be handled by another CR.

# The remained editor’s Note is no longer valid so it is removed.

### -----------------------Start of change 1-------------------------------------------

### 9.6.19	Resource Type node

The <node> resource represents specific information that provides characteristics of a oneM2M Node that can be utilized by other oneM2M operations. This resource type mainly contains the properties of a oneM2M Node such as context information (e.g. memory and storage) and network topology.

NOTE: It is assumed that <node> resource type is used when a oneM2M Node is mapped to physical object or its virtual representation.

This specific information stored in this resource type such as memory and storage can be obtained either by the existing device management technologies (OMA DM, BBF TR-069 [i.12]) or any other way (e.g. through JNI (Java Native Interface)). Since <mgmtObj> resource type represents the management functions including both ways, the types of sub-resources are <mgmtObj> resource type.

The location of <node> resource can be differentiated according to the type of node.

ASN: under <CSEBase> of the ASN-CSE.

ADN: under <CSEBase> resource of the local CSE. The <application> resource regarding the ADN shall have the proper link (URI) to the <node> resource that contain node specific information of the ADN.

MN: under <CSEBase> of the MN CSE.

Figure 9.6.19-1: Structure of <node> resource 
(only resource specific attributes are shown)

Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the child resources according to their multiplicity in Table 9.6.19-1 (0 indicates the optionality of the child resource).

Table 9.6.19-1: Child resources of <node> resource

| Child Resource Name of <node> | Child Resource Type | Multiplicity | Description | <nodeAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| memory | <mgmtObj> | 0..1 | This resource provides the memory (typically RAM) information of the node. (e.g. the amount of total volatile memory), See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| storage | <mgmtObj> | 0..n | This resource provides the storage (typically flash or disk) information of the node. (e.g. the amount of total writable persistent storage). See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| power | <mgmtObj> | 0..1 | The resource provides the power information of the node. (e.g. remaining battery charge). See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| networkTopology | <mgmtObj> | 0..1 | This resource describes the list of Nodes attached behind the MN node and its underlying relation among the nodes in the M2M Area Network. This attribute is defined in case the Node is MN. See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| schedule | <schedule> | 0..1 | This resource defines the reachability schedule information of the node. See clause 9.6.9 for <schedule>. | <scheduleAnnc> |

The <node> resource shall contain the attributes described in Table 9.6.19-2.

# Table 9.6.19-2: Attributes of <node> resource

| Attribute Name of <node> | Multiplicity | RW/ RO/ WO | Description | <nodeAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 1..n | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <nodeAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | OP |
| nodeID | 1 | RW | The ID of the Node which is specified in the resource type. This attribute is identical to M2M-Node-ID. | OP |
| hostedCSEID | 1 | RW | The ID of the CSEBase that is hosted on this node. | ?? |

### -----------------------End of change 1---------------------------------------------