| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0007 Mca Request Services |
| Source:* | Tim Carey, ALU, timothy.carey@alcatel-lucent.com |
| Contact: | Tim Carey, ALU, timothy.carey@alcatel-lucent.com |
| Date:* | 2014-03-10 |
| Abstract:* | Add a set of common services for requests across the Mca R01: Editorial Updates from LGE R02: Updates from TP#10 |
| Agenda Item:* |  |
| Work item(s): | TS-0007 WI |
| Document(s) Impacted* | TS-0007 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 6	M2M Services

This clause describes the M2M Services provided by the M2M Services Platform.

Editors Note: Signatures need to utilize the same names as attributes in TS-0001 where the attributes mean the same thing.

## 6.1	Introduction

The M2M Services defined in this clause are utilized by the Supporting Services described in the Annexes of this specification.

Figure 6.1-1: oneM2M Services

## 6.2	Service Subscription

The Service Subscription service provides the ability to:

- Validate that service capabilities (e.g., requests, notifications) that transpire across the Mca reference point

- Assist in authorization of a service capability by returning a role for the requested service capability

### 6.2.1	Service Capabilities

#### 6.2.1.1	validateSupportingService

This service capability ensures that a valid M2M Service Subscription exists for  a service capability that is either received by the M2M Service Platform from an AE or is transmitted to the AE from the M2M Service Platform.

##### 6.2.1.1.1	Pre-conditions

##### A correlation between the serviceId that defines the Supporting Service and the subscriptionId has been defined in order to obtain the serviceId.

##### 6.2.1.1.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| subscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Sub-ID) |
| serviceId | IN | NO | The M2M Service Identifier (M2M-Serv-ID) |
| returnCode | OUT | NO | Return codes: Service exists for Service Subscription does not exist for Service |

Table 6.2.1.1.2-1 validateSupportingService Signature

##### 6.2.1.1.3	Post-Conditions

Not Applicable

##### 6.2.1.1.4	Exceptions

Not Applicable

##### 6.2.1.1.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

### 6.2.1.1.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

- TBD

Editors note: The oneM2M Resource Interworking will be identified if a M2M Service Subscription operation is identified

### 6.2.1.1.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

#### 6.2.1.2	retrieveAuthorization

This service capabilities determines the Role associated with the Service Capability and the M2M Subscription.

##### 6.2.1.2.1	Pre-conditions

A correlation between the subscriptionId, serviceId and serviceCapId to a Role.

##### 6.2.1.2.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| subscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Sub-ID) |
| serviceId | IN | NO | The M2M Service Identifier (M2M-Serv-ID) |
| serviceCapId | IN | NO | The M2M Service Capability Identifier (M2M-Srv-ID) |
| rolePolicies | OUT | Yes | The Attribute Based Control Role policies that are valid for this subscription, service and service capability. |
| returnCode | OUT | NO | Return codes Roles exist Roles do not exist |

Table 6.2.1.1.2-1 retrieveAuthorization Signature

##### 6.2.1.2.3	Post-Conditions

Not Applicable

##### 6.2.1.2.4	Exceptions

Not Applicable

##### 6.2.1.2.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.2.1.2.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

- TBD

Editors note: The oneM2M Resource Interworking will be identified if a M2M Service Subscription operation is identified from the Security TS.

##### 6.2.1.2.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Service.

## 6.3	Authorization

The Authorization service provides the ability to:

- Authorize the issuer for the Service Capability

### 6.3.1	Service Capabilities

#### 6.3.1.1	authorizeServiceCapability

This service capability authenticates an issuer as a valid originator for the fromApp and then authorizes the service capability within the context of a M2M Service Subscription between the fromApp and toApp.

##### 6.3.1.1.1	Pre-conditions

The M2M Identifiers for th e request  issuer, subscriptionId, fromApp and toApp are assigned to the Service Subscription.

A correlation between the service capability and the M2M authorization event has been defined in order to authorize the service capability.

##### 6.3.1.1.2	Common Service Capability Parameters for Request Authentication and Authorization

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | The identifier of the originator that is issuing the request. |
| subscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-SUB-ID) |
| fromApp | IN | NO | The identifier of the AE that is originated the request (M2M-AppInst-ID) |
| toApp | IN | NO | The identifier of the AE that is to target of the request (M2M-AppInst-ID) |
| returnCode | OUT | YES | Return codes that are relevant to the Authentication and Authorizations of requests from AEs across the Mca reference point. Issuer is not authenticated Issuer does not have a Service Subscription Issuer not authorized for the Service Capability |

Table A.2.1.1.2-1 Common Service Capability Parameters for Request Authentication and Authorization

##### 6.3.1.1.3	Service Interactions

This service capability will consume the ServiceSubscription:retrieveAuthorization service capability:

##### 6.3.1.1.4	Post-Conditions

Not Applicable

##### 6.3.1.1.5	Exceptions

Not Applicable

##### 6.3.1.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.3.1.1.6	oneM2M Resource/CSF Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

- TBD

Editors note: The oneM2M Resource/Sevice Interworking will be identified once the Security TS-0003 is frozen.

##### 6.3.1.1.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Service.

# 7	M2M Service Components

This clause describes the M2M Service Components provided by the M2M Services Platform.

## 7.1	Introduction

An M2M Service Component defines the set of M2M Services that are related in the sense that the M2M Services that comprise the M2M Service Component are typically deployed together in order to support one or more Supporting Services.

The M2M Service Architecture augments the oneM2M Functional Architecture by specifying M2M Services provided to M2M Service Providers. These M2M Services are exposed to the AE across the Mca reference point as well as other Service Components across the Msc reference point.

## 7.1.1	Service Component Interaction Cross Reference

Table 7.1-1 Service Component Cross Reference

## 7.3	Infrastructure Component (INF)

The INF Component provides Services that are exposed to other  M2M Service Components across the Msc reference point.  The Services within the INF Component are common and utility type Services needed to enable other M2M Services.

## 7.3.1	INF to Service Cross Reference

Authorization: All Service Capabilities

ServiceSubscription: retrieveAuthorization

## 7.4	Service Subscription Component (SSUB)

The SSUB Component provides Services that are necessary to maintain M2M  Service Subscriptions, the associations (e.g., AE, devices) to the M2M Service Subscription and any External Identifiers associated with AE and devices. In addition the services used to manage devices and AEs are part of this component.

## 7.4.1	SSUB to Service Cross Reference

ServiceSubscription: All Service Capabilities

# Annex A (Informative): Common Services: Mca Received Requests

## A.1	Overview

This annex illustrates the usage of the common services described in this technical specification for implementation requests received from AEs across the Mca Reference Point.

Editors Note: Signatures need to utilize the same names as attributes in TS-0001 where the attributes mean the same thing.

### A.2	Supporting Services

### A.2.1	Authentication and Authorization of Requests

Upon reception of requests across the Mca reference, the request issuer is authenticated and the  request service capabilty is authorized when the:

- Request issuer has a service subscription for the request service capability.

- Request issuer is authorized  for the request service capability.

A.2.1.1	receiveRequest

###### A.2.1.1.1	Pre-conditions

The external identifiers for th e request  issuer, subscriptionId, fromApp and toApp are assigned to the Service Subscription.

A correlation between the service capability and the M2M authorization event has been defined in order to obtain the authorize the service capability.

A.2.1.1.2	Common Service Capability Parameters for Request Authentication and Authorization

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | The identifier of the originator that is issuing the request. |
| subscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-SUB-ID) |
| fromApp | IN | NO | The identifier of the AE that is originated the request (M2M-AppInst-ID) |
| toApp | IN | NO | The identifier of the AE that is to target of the request (M2M-AppInst-ID) |
| returnCode | OUT | YES | Return codes that are relevant to the Authentication and Authorizations of requests from AEs across the Mca reference point. Issuer is not authenticated Issuer does not have a Service Subscription Issuer not authorized for the Service Capability |

Table A.2.1.1.2-1 Common Service Capability Parameters for Request Authentication and Authorization

A.2.1.1.3	Service Interactions

The interactions of  service capabilities required to authenticate and authorize a request:

- Validate the Service Subscription using the Issuer, toApp and fromApp parameters received from the issuer.

- Authorized the use of the service capability within the Service Subscription

Figure A.2.1.1.3-1 receiveRequest Interaction Diagram

A.2.1.1.4	Post-Conditions

Success case: The request  is permitted.

Failure case: The request  is not permitted and an optional return code is transmitted back the request issuer.

A.2.1.1.5	Exceptions

Not Applicable

A.2.1.1.6	Policies for Use

Message Exchange Patterns: In-Out, In-Only, Robust In-Only, In-Optional-Out

Transaction Pattern: Participation allowed

A.2.1.2	getServiceCapability

The getServiceCapabilitycapability inspects the request to determine the M2M Service Capability associated with the request. Each request that is received has a service capability defined in the request header.

###### A.2.1.2.1	Pre-conditions

###### Not Applicable

A.2.1.2.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| operation | IN | NO | Request operation – Common to all requests |
| serviceCapId | OUT | NO | The M2M Service Capability Identifier (M2M-Srv-ID) |
| returnCode | OUT | YES | Return codes: Unable to determine Service Capability from Operation |

Table A.2.1.2.2-1 getServiceCapability Signature

A.2.1.1.3	Post-Conditions

Success case: The M2M-Srv-ID is returned

Failure case: An error code is returned

A.2.1.1.4	Exceptions

Not Applicable

A.2.1.1.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

A.2.1.3	getSupportingService

The getSupportingService capability inspects the request to determine the Supporting Service for the Service Capabilty. This service capability is assigned to M2M Service.

###### A.2.1.3.1	Pre-conditions

A correlation between the M2M-Srv-ID that defines the request operation and the M2M-Serv-ID that defines the Supporting Service has been defined in order to obtain the serviceId.

A.2.1.3.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| serviceCapId | IN | NO | The M2M Service Capability Identifier (M2M-Srv-ID) |
| serviceId | OUT | NO | The M2M Service Identifier (M2M-Serv-ID) of the Supporting Service |
| returnCode | OUT | YES | Return codes that are relevant to the Authentication and Authorizations of requests from AEs across the Mca reference point. M2M Services doesn’t exist for this Service Capability |

Table A.2.1.3.2-1 getSupportingService Signature

A.2.1.3.3	Post-Conditions

Success case: The M2M-Serv-ID is returned

Failure case: An error code is returned

A.2.1.3.4	Exceptions

Not Applicable

A.2.1.3.5	Policies for Use

Message Exchange Patterns: In-Out

### Transaction Pattern: Participation allowed