| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Barbara Pareglio, NEC barara.pareglio@neclab.eu |
| Format:* | ARC#10 |
| Date:* | 2014-03-28 |
| Contact:* | Barbara Pareglio, NEC |
| Reason for Change/s:* | Cleaned up the description of versionTag and changed the name to non-confuse it with the API version |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.4.3 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

As presented by contribution ARC-2014-1204 there are some inconsistencies with the attribute “versionTag”. The current CR proposed the following changes:

- Changed name from versionTag to requestNr: the reason is that versionTag could be confused to the possible API version or the other version attributes in the TS, even if there is no relation amongst these attributes. The architecture does not talk about versioning, but for WG3 there might be the need to think about versioning and these tag might become confusing.

- Change the multiplicity from 1 to 0..1, this attribute introduce an optimization that is not required for a lot of the deployments. The usage of such attribute is now dependent on M2M subscription and/or policies.

### -----------------------Start of change 1-------------------------------------------

### 9.6.1	Common Attributes

Many of the attributes of the resources described in the present document are common. Such attributes are described here once in order to avoid duplicating the description for every resource that contains it.

Attributes that are only used in one or two resource types are described only in the clause for that resource type.

In all tables representing resource attributes, each attribute name is followed by its "short name" in brackets that shall be used in resource representations to be transferred across reference points.

# Table 9.6.1-1: Common Attributes

| Common Attribute | Description |
| --- | --- |
| resourceType (rT) | Resource Type. This WO resourceType attribute stores <in a two capital letters token> the information useful for procedure processing, e.g. CO for <container>, CI for <instance>. |
| parentID (pID) | The identifier identifies the parent resource. {9.6.1.a} Editor's Note: The adoption of a URI format is still to be confirmed. |
| accessControlPolicyID (aRI) | The URI of an <accessControlPolicy> resource. The permissions defined in the <accessControlPolicy> resource that are referenced determine who is allowed to access the resource containing this attribute for a specific purpose (e.g. Retrieve, Update, Delete, etc.). If a resource type does not have an accessControlPolicyID attribute definition, then the accessControlPolicy for resources of that type are governed in a different way, for example, the accessControlPolicy associated with the parent may apply to a child resource that does not have an accessControlPolicyID attribute definition, or the permissions for access are fixed. Refer to the corresponding procedures to see how permissions are handled in such cases. If a resource type does have an accessControlPolicyID attribute definition, but the (optional) accessControlPolicyID attribute is not set, or it is set to a value that does not correspond to a valid, existing <accessControlPolicy> resource, or it refers to an <accessControlPolicy> resource that is not reachable (e.g. because it is located on a remote CSE that is offline or not reachable), then the system default access permissions shall apply. The system default access permissions grant all permissions (i.e. the full set of permissionsFlags) to the following permission holders depending on the prefix of URI of the resource.: {9.6.1.b} Editor's Note: what is the list of permission holders |
| creationTime (cT) | Time/date of creation of the resource. |
| expirationTime (eT) | Time/date after which the resource will be deleted by the hosting CSE. This attribute can be provided by the Originator, and in such a case it will be regarded as a hint to the hosting CSE on the lifetime of the resource. The hosting CSE can however decide on the real expirationTime. If the hosting CSE decides to change the expirationTime attribute value, this is communicated back to the Originator. The lifetime of the resource can be extended by providing a new value for this attribute in an UPDATE verb. Or by deleting the attribute value, e.g. by not providing the attribute when doing a full UPDATE, in which case the hosting CSE can decide on a new value. |
| lastModifiedTime (lMT) | Last modification time/date of the resource. |
| requestNrg (vT) | An incremental counter of modification on the resource. When a resource is created, this counter is set to 0, and it will be incremented on every modification of the resource. NOTE: In order to enable detection of overflow, the counter needs to be capable of expressing sufficiently long numbers. NOTE: this attribute has the scope to allow identifying changes in resources within a time interval that has is lower than the one supported by the attribute lastModifiedTime (e.g. less than a second or millisecond). NOTE:The support of this attribute is considered a feature based on the M2M Service Subscription and/or policies. |
| labels(lBs) | Tokens used as keys for discovering resources. |
| creator (cr) | The App-inst-ID or CSE-ID of the entity which created the resource |
| link (ln) | This attribute shall be present only for the announced resource. This attribute shall provide the URI to the original resource. |
| announceTo (aT) | This attributes shall be present for the announceable original resource only. This attribute maintains the list of URIs to the announced resources. Updates on this attribute will trigger new resource announcement or de-announcement. In case of new resource announcement, either the exact URI to the announced resource that is to be created can be provided, or the CSE-ID of the remote CSE can be provided. This means the original resource-hosting CSE will decide the exact location of the announced resource in the remote CSE identified by the CSE-ID. |
| announcedAttribute (aA) | This attributes shall be present for the announceable original resource only. This attribute maintains the list of the announced attributes in the original resource. Updates on this attribute will trigger new attribute announcement if a new attribute is added or de-announcement if the existing attribute is removed. |

{9.6.1.c} Editor's Note:  The usage of creator (cr) attribute is FFS.

{9.6.1.d} Editor's Note: The following attributes are FFS depending on resource structure discussions:

- child: resources with child relation with the considered resource

parent: resources with parent relation with the considered resource

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.6	Resource Type container

This resource represents a container for data instances. It is used to share information among other entities and potentially to track the data. A <container> resource has no associated content, only attributes and child resources.

Figure 9.6.6-1: Structure of <container> resource
(only child resources and resource specific attributes are shown)

{9.6.6.a} Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the child resources according to their multiplicity in Table 9.6.6-1 (0 indicates the optionality of the child resource).

{9.6.6.b} Editor's Note: Susbscription relation with this resource is for FFS.

{9.6.6.c} Editor's Note: location resource relation with containers is for FFS.

# Table 9.6.6-1: Child resources of <container> resource

| Child Resource Name of <container> | Child Resource Type | Multiplicity | Description | <containerAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <instance> | 0..n | See clause 9.6.7 | <instanceAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscriptionAnnc> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <containerAnnc> |

This resource shall contain the attributes according to their multiplicity in Table 9.6.6-2 (0 indicates the optionality of the attribute).

# Table 9.6.6-2: Attribute of <container> resource

| Attribute Name of <container> | Multiplicity | RW/ RO/ WO | Description | <containerAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. If no accessConytolPolicyID is given at the time of creation, the accessControlPolicyID of the parent resource is linked to this attribute | MP |
| labels (lBs) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (st) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creator (cr) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| requestNr (vT) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | ?? |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <containerAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| maxNrOfInstances (mi) | 0..1 | RW | Maximum number of instances of <instance> child resources. | OP |
| maxByteSize (mb) | 0..1 | RW | Maximum number of bytes that are allocated for a <container> resource for all instances in the <container> resource. | OP |
| maxInstanceAge (ma) | 0..1 | RW | Maximum age of the instances of <instance> resources within the <container>. The value is expressed in seconds. | OP |
| currentNrOfInstances (ni) | 1 | RO | Current number of instances in a <container> resource. It is limited by the maxNrOfInstances. | OP |
| currentByteSize (nb) | 1 | RO | Current size in bytes of data stored in a <container> resource. It is limited by the maxNrOfBytes. | OP |
| latest (lt) | 0..1 | RO | Reference to latest instance, when present. | OP |
| locationID (LID ) | 0..1 | RW | URI of the resource where the attributes/policies that define how location information are obtained and managed. This attribute is defined only when the <container> resource is used for containing location information. | OP |
| ontologyRef (oR) | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the instances of the container. (see note) NOTE: The access to this URI is out of scope of oneM2M. | OP |

{9.6.6.d} Editor's Note: Mechanisms for announcing are FFS.

{9.6.6.e} Editor's Note: The container type is FFS.

{9.6.6.f} Editor's Note: The following attributes are FFS depending on resource structure discussions:

- child: resources with child relation with the considered resource

- parent: resources with paren relation with the considered resource

### 9.6.7	Resource Type instance

The <instance> resource represents a data instance in the container. The content of the instance is opaque to the M2M platform and it might even be encrypted. However, there is meta-data associated with an instance which shall be accessible.

Contrary to other resources, the <instance> resource cannot be modified once created, regardless of the accessControlPolicyID associated with the parent resource. An instance may be deleted explicitly or it may be deleted by the platform based on policies. If the platform has policies for the instance retention these shall be represented by the attributes maxByteSize, maxNrOfInstances and/or maxInstanceAge on the <container> resource. If multiple policies are in effect, the strictest policy shall apply.

The <instance> resource inherits the same access rights of the parent <container> resource, and does not have its own <accessControlPolicy> attribute.

Figure 9.6.7-1: Structure of <instance> resource
(only child resources and resource specific attributes are shown)

{9.6.7.a} Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the attributes according to their multiplicity in Table 9.6.7-1 (0 indicates the optionality of the attribute).

# Table 9.6.7-1: Attributes of <instance> resource

| Attribute Name of <instance> | Multiplicity | RW/ RO/ WO | Description | <instanceAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| requestNr (vT) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. The requestNr attribute of the parent resource should be incremented first and copied into this requestNr attribute when a new instance is added to the parent resource. | ?? |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <instanceAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| typeOfContent (tOC) | 0..1 | WO | Optional type of the content included in the content attribute. This is media-type as defined in <reference to stage 3 document>. | OP |
| contentSize (cS) | 1 | WO | Size in bytes of the content attribute. | OP |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the instances of the container. If this attribute is not present, the instance inherits the ontologyRef from the parent <container> resource if present (see note) NOTE: Access to this URI is out of scope of oneM2M. | OP |
| content (c) | 1 | WO | Actual opaque content of an instance. This may for example be an image taken by a security camera, or a temperature measurement taken by a temperature sensor. | OP |

{9.6.7.b} Editor’s Note:  Clairify forward reference to Stage 3

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 9.6.11	Resource Type delivery

When a CSE is requested to initiate an operation (CRUD) targeting resources on another CSE, then it needs to involve the CMDH CSF in order to do proper scheduling and execution of delivery of data from the source CSE to the target CSE in line with provisioned policies. It is possible to do that in two different ways: Using delivery aggregation ("da" information set to on) or by forwarding the original request as a separate request on the Mcc reference point without changes.

In order to be able to initiate and manage the execution of data delivery in a resource-based manner, the resource type delivery is defined. This resource type needs to be used for forwarding requests from one CSE to another CSE when "da" information in the request is set to ON. If the "da" information is set to OFF, the original request shall be forwarded without change  to the next CSE.

Operations to Retrieve, Update or Delete a <delivery> resource will allow authorized entities to inquire the status of a delivery, change delivery attributes or cancel a delivery.

{9.6.11.a} Editor's Note: Further details on mechanisms how to do delivery handling are FFS.

{9.6.11.b} Editor's Note: The particular position in the addressable space of resources id FFS.

Figure 9.6.11-1: Structure of resource <delivery>
(only resource specific attributes are shown)

The resource <delivery> shall contain the attributes according to their multiplicity shown in Table 9.6.11-1.

# Table 9.6.11-1: Attributes of <delivery> resource

| Attribute Name of <delivery> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| requestNr (vT) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. |
| Source | 1 | WO | The CSE-ID of the CSE that initiated the delivery process represented by this <delivery> resource. |
| Target | 1 | WO | A list of CSE-IDs that defines one or more target CSEs for delivering the data contained in the data attribute |
| Lifespan | 1 | RW | Defines the time limit when the delivery of the information in the data attribute needs to complete. If the lifespan expires before successful delivery, no further attempts to deliver the information in the data attribute need to be executed. If the delivery fails, a feedback may be expected by the source CSE depending on options reflected in the deliveryMetaData attribute. The lifespan attribute of a <delivery> resource shall be set consistent with the rqet parameters of the set of original requests contained in the Data attribute, i.e. lifespan shall not extend beyond the earliest expiring rqet parameter in the set of the original requests contained in the Data attribute. |
| eventCat | 1 | RW | Defines the category of the event that triggered the delivery request represented by this <delivery> resource |
| deliveryMetaData | 1 | RW | Contains meta information on the delivery process represented by this <delivery> resource, such as delivery status, delivery options, tracing information, etc |
| data | 1 | WO | Attribute containing the data to be delivered to the target CSE(s). This data represents one or more original requests that were targeting the same CSE(s). |

### 9.6.12	Resource Type request

The use of this resource type is optional depending on the configuration.

When a CSE is requested to initiate an operation for which the result should be available to the Originator by reference ('rt' information of the request set to 'Acknowledgement'), the local CSE which received the Request directly from the Originator may need to provide a reference back to the Originator so that the Originator can access attributes of the Request at a later time - for instance in order to retrieve the result of an operation that was taking a longer time. The Originator (or any other authorized entity depending on access rights) can access the request status and the requested operation result through it.

The <request> resource may get deleted by the CSE that is hosting it:

- when the result of the requested operation (if any result was requested at all) has been sent back to the Originator (either by notification to the Originator or by retrieval initiated by the Originator);

- when the expiration time of the <request> resource is reached;

- at any other time -  depending on local settings in the CSE that hosts the <request> resource.

{9.6.12.a} Editor's Note: The exact way how to define that setting (e.g. via DM) is FFS.

For the purpose of providing a standardized structure for expressing and accessing the context of a previously issued Request, the resource type request is defined.

Figure 9.6.12-1: Structure of <request> resource
(only resource specific attributes are shown)

The resource <request> shall contain the attributes according to their multiplicity shown in Table 9.6.12-1.

# Table 9.6.12-1: Attributes of <request> resource

| Attribute Name of <request> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| expirationTime (et) | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| requestNr (vT) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. |
| operation | 1 | RO | The operation requested by the Originator, e.g. modifying the content of a container, registering an Application. |
| target | 1 | RO | The address or the target resource for the requested operation. |
| originator | 1 | RO | The originating entity for the request. |
| metaInformation | 1 | RO | Meta information about the request. The content of this attribute is equivalent to the "mi" information in clause 8.1. |
| content | 1 | RO | Contains the content that is supposed to be sent to the target resource. |
| requestStatus | 1 | RO | Contains information on the current status of the Request, e.g. "accepted and pending". |
| operationResult | 1 | RO | Contains information on the result of the requested action, e.g. "Resource created with URI: XXX". |

Creation of a <request> resource can only be done on a local CSE implicitly by an AE issuing a generic CRUD request for any other resource type to the Local CSE. A Local CSE cannot accept requests to create a <request> resource directly.

Retrieving of <request> resources or attributes of a <request> resource is allowed for authorized entities.

Update of a <request> resource can only be done by the CSE that hosts the <request> resource or by CSEs that provide operation results pertaining to the request (for instance when the result of an operation requested for a remote CSE becomes available).

Deletion of a <request> resource is possible by authorized entities. If the execution of the request was still pending at the time of deletion, the hosting CSE should to stop any further attempts to execute the request.

### -----------------------End of change 3 ---------------------------------------------