| CHANGE REQUEST |
| --- |
| Group Name:* | TP#10 |
| Source:* | Huawei Technologies Co., Ltd. |
| Format:* | Plenary |
| Date:* | <2014-3-24> |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* | The resource type parameters is not really necessary in the current release of TS. The CR proposes to delete it. |
| CR against: Release* | <Release One> |
| CR against: TS/TR* | TS0001 v0.4.2 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The only place <parameters> used in the current TS is deviceCapability which can be handled in a flattened way without parameters. So the CR proposes to remove resource type <parameters>.

### -----------------------Start of change 1-------------------------------------------

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.13	Resource Type mgmtObj

The mgmtObj resource contains management data which represents individual M2M management functions. It represents a general structure to map to external management technology (e.g. OMA DM [i.2], BBF [ref] TR-0069 [i.12] and LWM2M [ref]) data models.

Editor's note - add references?

Figure 9.6.13-1: Structure of <mgmtObj> resource 
(only resource specific attributes are shown)

Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

The <mgmtObj> resource shall contain the attributes described in table 9.6.13-2.

# Table 9.6.13-2: Attributes of <mgmtObj> resource

| Attribute Name of <mgmtObj> | Multiplicity | RW/ RO/ WO | Description | <mgmtObjAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See clause 9.6.1 where this common attribute is described | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described | MP |
| accessControlID (aRI) | 1 | RW | See clause 9.6.1 where this common attribute is described | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <mgmtObjAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| mgmtDefinition | 1 | WO | Specifies the type of mgmtObj resource e.g. software, firmware, memory. The list of the value of the attribute can be seen in Annex D. | MP |
| objectID | 0..1 | WO | Contains a URN that uniquely identifies the external management technology data model used for this <mgmtObj> resource as well as the managed function and version it represents. This attribute shall be provided during the creation of the <mgmtObj> resource and shall not be modifiable afterwards. This is mandatory for the <mgmtObj>, for which the data model is not specified by oneM2M but mapped from external management technology data model specified in other device management protocols (e.g. OMA-DM, BBF TR-069 and LWM2M). | OP |
| objectPath | 0..1 | WO | Contains the local path of the external management object instance on the managed entity which is represented by the <mgmtObj> resource in the hosting CSE. This attribute shall be provided during the creation of the <mgmtObj>, so that the hosting CSE can correlate the created <mgmtObj> with the external management object instance on the managed entity for further management operations. It shall not be modifiable after creation. The format of this attribute shall be a local external management object path in the form as specified by existing management protocols. (e.g. "./anyPath/Fw1" in OMA DM, "Device.USBHosts.Host.3." in BBF TR-069). | OP |
| mgmtLink | 0..n | RW | The attribute contains references to another <mgmtObj> resource in case a hierarchy of the <mgmtObj> is needed. | OP |
| [objectAttribute] | 0..n | RW | Each [objectAttribute] is mapped from a leaf node of a hierarchical structured management object (including oneM2M data model and the existing management data models) based on the mapping rules below the table. | OP |
| description | 0..1 | RW | Text format description of mgmtObj. | OP |

When mapping resources from management technologies to a corresponding <mgmtObj> resource, the following rules shall apply:

- The root resource of external management objects maps to the <mgmtObj> resource

- For child resource of the root resource of specific technology:

- Rule1: If the child external management object cannot have a child external management object, the external management object maps to the  [objectAttribute] attribute of the <mgmtObj> resource with the same resource name;

- Rule2: If the child external management object can have another child external management object, the external management object maps to a new <mgmtObj> resource. And the URI of the new <mgmtObj> is stored as one mgmtLink attribute of the <mgmtObj> resource which is mapped from the parent external management object.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 10.2.7	mgmtObj Management Procedures

#### 10.2.7.1	Introduction

This clause describes the management procedures over Mca and Mcc reference points. Different RESTful requests addressing a <mgmtObj> resource (or its attributes or child resources) shall be translated into existing management commands and procedures performed on the mapped external management object on the managed entity. The Receiver in the following procedures is IN-CSE.

#### 10.2.7.2	Create <mgmtObj>

This procedure is used to create a specific <mgmtObj> resource in the hosting CSE to expose the corresponding management function of a managed entity (i.e. M2M Device/Gateway) over Mca reference point. Depending on the data model being used, the created <mgmtObj> resource may be a partial or complete mapping from the external management object on the managed entity. If such external management object is missing from the managed entity, it shall be added to the managed entity. Further RESTful operations performed on the created <mgmtObj> resource shall be converted by the hosting CSE into a corresponding device management action performed on the mapped external management object on the managed entity using existing device management protocols (e.g. OMA-DM[ref] or BBF[ref] TR-069 [i.12]).

Originator: The Originator shall request to create a new <mgmtObj> resource to be named as "mgmtObj" by using a CREATE verb. The request shall address <CSEBase> resource of the hosting CSE.

The Originator may be:

- The CSE on the managed entity: In this case, the CSE first collects the original external management object (the management tree structure or also the value of the tree nodes if needed) of the local device and transforms the data into the <mgmtObj> resource representation, then requests the hosting CSE to create the corresponding <mgmtObj> resource.

- An AE: In this case, the AE requests the hosting CSE to add the corresponding external management object to the managed entity by creating an <mgmtObj> resource in the hosting CSE.

NOTE 1:	The IN-CSE may also create the <mgmtObj> resource locally by itself. The details are out of scope. In this case, the hosting CSE first collects the original external management object on the managed entity via existing device management protocols (e.g. OMA DM[ref], BBF TR-069 [i.12] or LWM2M), then transforms the object into the <mgmtObj> resource representation and create the <mgmtObj> resource locally in the IN-CSE.

NOTE 2:	The <mgmtObj> resource may also be created in the hosting CSE by other provisioning means which are out of scope.

Receiver: For the CREATE procedure, the Receiver shall:

- Check if the Originator has the CREATE permission on the addressed <CSEBase> resource. Check the validity of provided attributes.

- Upon successful validation, create a new <mgmtObj> resource with name "mgmtObj" in the hosting CSE with the provided attributes.

- If the originator is an AE: Check if there is existing management session between the management server and the managed entity. If not, request the management server to establish management session towards the managed entity. Send the management request to the managed entity or to the management server to add the corresponding external management object to the managed entity based on existing management protocol.

- Maintain the mapping relationship between the created <mgmtObj> resource and the external management object on the managed entity.

- Respond to the originator with the appropriate generic responses. It shall also provide in the response the URI of the created new resource.

# Table 10.2.7.2-1: <mgmtObj> CREATE

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | None |
| Information on Request message | op: C fr: Identifier of the AE or the CSE that initiates the Request to: Th eURI of the <CSEBase> where the <mgmtObj> resource is intended to be Created cn: The representation of the <mgmtObj> resource for which the attributes are described in clause 9.13 |
| Local processing on Hosting CSE | New external management object created on the managed entity using external management technologies in case the originator is IN-AE |
| Information on Response message | Proper error code if the new external management object is not created |
| Post-Conditions | None |
| Exceptions | The creation of the external management object is not allowed The created external management object already exists Corresponding external management object cannot be added to the managed entity for some reason (e.g. not reachable, memory shortage) |

#### 10.2.7.3	Retrieve <mgmtObj>

This procedure is used to retrieve information from an existing <mgmtObj> resource or its <parameters> child resources.

Originator: The Originator shall request to retrieve an existing <mgmtObj> resource by using a RETRIEVE verb. The request shall address a specific "mgmtObj" resource of a CSE or a specific <parameters> child resource of the <mgmtObj> resource to retrieve all attributes of the <mgmtObj> resource or the <parameters> child resource.

The originator may be:

- An IN-AE.

- An ASN/MN-CSE on the managed entity.

Receiver: For the RETRIEVE procedure, the Receiver shall:

- Check if the originator has the READ permission on the addressed <mgmtObj> resource.

- Upon successful validation, retrieve the corresponding <mgmtObj> resource or the <parameters> child resource including all attributes and references to all its child resources from its repository.

- Respond to the originator with the appropriate generic responses.

- If the Originator is an IN-AE and if the requested information of the <mgmtObj> resource is not available, identify the corresponding external management object on the managed entity according to the mapping relationship it maintains. Check if there is existing management session between the management server and the managed entity. If not, request the management server to establish management session towards the managed entity. Send the management request to get the corresponding external management object from the managed entity based on existing device management protocol (e.g. OMA-DM[ref], BBF[ref] TR-069 [i.12]), then return the result to the originator.

# Table 10.2.7.3-1: <mgmtObj> RETRIEVE

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | None |
| Information on Request message | op: R fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <mgmtObj> resource |
| Local processing on Hosting CSE | Get corresponding external management object from managed entity by existing management procedures in case the addressed <mgmtObj> is not available |
| Information on Response message | Proper error code if the external management object can not be retrieved |
| Post-Conditions | None |
| Exceptions | Corresponding external management object data cannot be retrieved from managed entity due to some reason (e.g. external management object not found) |

#### 10.2.7.4	Update <mgmtObj>

This procedure is used to update information of an existing <mgmtObj> resource or its <parameters>child resource.

Originator: The Originator shall request to update information of an existing <mgmtObj> resource by using an UPDATE verb. The Request shall address a specific <mgmtObj> resource on the hosting CSE to update the all attributes of the <mgmtObj> resource with new values when using UPDATE verb;

The Originator may be:

- IN-AE.

- CSE on the managed entity.

Receiver: For the UPDATE procedure, the Receiver shall:

- Check if the Originator has the WRITE permission on the address <mgmtObj> resource. Check the validity of provided attributes if any.

- Upon successful validation, update the corresponding attribute(s) of the <mgmtObj> resource accordingly.

- If the originator is an IN-AE, identify the corresponding external management object on the managed entity according to the mapping relationship it maintains. Check if there is existing management session between the management server and the managed entity. If not, request the management server to establish management session towards the managed entity. Send the management request to update the corresponding external management object in the managed entity accordingly based on existing device management protocol (e.g. OMA DM[ref], BBF[ref] TR-069 [i.12] or LWM2M[ref]).

- Respond to the Originator with the appropriate generic responses.

# Table 10.2.7.4-1: <mgmtObj> UPDATE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | None |
| Information on Request message | op: U fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <mgmtObj> resource cn: The representation of the <mgmtObj> resource for which the attributes are described in clause 9.13 |
| Local processing on Hosting CSE | Override corresponding external management object in managed entity by existing management procedures |
| Information on Response message | Proper error code if the external management object can not be updated |
| Post-Conditions | None |
| Exceptions | Corresponding external management object cannot be updated to managed entity due to some reason (e.g. not reachable, external management object not found) |

#### 10.2.7.5	Delete <mgmtObj>

This procedure is used to delete an existing <mgmtObj> resource so as to hide the management function of a managed entity (i.e. M2M Device/Gateway) from being exposed via Mca reference point. An IN-AE uses this procedure to remove the corresponding external management object (e.g. an obsolete software package) from the managed entity.

Originator: The Originator shall request to delete an existing <mgmtObj> resource by using a DELETE verb. The request shall address the specific <mgmtObj> resource on the hosting CSE.

The originator may be:

- The CSE on the managed entity: In this case, the CSE issues the request to the hosting CSE to hide the corresponding management function from being exposed by the <mgmtObj> resource.

- An IN-AE: In this case, the IN-AE requests the hosting CSE to delete the <mgmtObj> resource from the hosting CSE and to remove the corresponding external management object from the managed entity.

NOTE 1:	The hosting CSE in the network domain may also delete the <mgmtObj> resource locally by itself. This internal procedure is out of scope.

NOTE 2:	The <mgmtObj> resource may also be deleted in the hosting CSE by other provisioning means which are out of scope.

Receiver: For the DELETE procedure, the Receiver shall:

- Check if the Originator has the DELETE permission on the addressed <mgmtObj> resource.

- Upon successful validation, remove the addressed resource from its repository.

- If the Originator is an IN-AE, identify the corresponding external management object on the managed entity according to the mapping relationship it maintains. Check if there is existing management session between the management server and the managed entity. If not, request the management server to establish management session towards the managed entity. Send the management request to remove the corresponding external management object from the managed entity based on existing management protocol.

- Respond to the Originator with the appropriate generic responses.

# Table 10.2.7.5-1: <mgmtObj> DELETE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | None |
| Information on Request message | op: D fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <mgmtObj> resource. |
| Local processing on Hosting CSE | Trigger existing (OMA-DM[ref], BBF[ref] TR-0069 [i.12] or LWM2M[ref]) management procedures to delete the corresponding external management object from the managed entity. |
| Information on Response message | Proper error code if the external management object can not be deleted. |
| Post-Conditions | None |
| Exceptions | Corresponding external management object cannot be deleted from managed entity due to some reason (e.g. not reachable, external management object not found). |

#### 10.2.7.6	Execute <mgmtObj>

This procedure is used for executing a specific management command on a managed entity through an existing <mgmtObj> resource on the hosting CSE.

Originator: The Originator shall request to execute a specific management command which is represented by an existing <mgmtObj> resource or its attribute by using an UPDATE verb. The request shall address the specific executable <mgmtObj> resource or its attribute and shall contain an empty body. In the case that the management command is represented by an attribute of a <mgmtObj> resource, such attribute shall contain a URI that the request may also address to trigger the command execution alternatively.

After the execution request, the originator may request to retrieve the execution result or status from the executable <mgmtObj> resource or its attribute/child resource by using a RETRIEVE method as described in clause 10.3.4.3.

The Originator shall be:

- IN-AE.

Receiver: For the EXECUTE procedure, the Receiver shall:

- Check if the Originator has the WRITE permission on the addressed <mgmtObj> resource or its attribute.

- Upon successful validation, check if there is existing management session between the management server and the managed entity. If not, request the management server to establish management session towards the managed entity. Send the management request to execute the corresponding management command (e.g. "Exec" in OMA DM [ref]) on the managed entity based on existing device management protocol.

- Respond to the Originator with the appropriate generic responses. The Response may also contain execution results.

- Upon receiving a RETRIEVE request to retrieve the execution result or status from the executable <mgmtObj> resource or its attribute, perform the procedures as described in clause 10.2.5.3.

- Upon receiving from managed entity a management notification (e.g. OMA-DM [ref] "Generic Alert" message or BBF[ref] TR-0069 [i.12] "Inform" message) regarding the execution result or status, the receiver may actively send the management request to retrieve the execution result or status external management object information from the managed entity and update the corresponding <mgmtObj> resource or its attribute locally.

Editor's note: The definition of Execute is to be for FFS in clause 10.1.

# Table 10.2.7.6-1: <mgmtObj> EXECUTE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | None |
| Information on Request message | op: U fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <mgmtObj> resource cn: None |
| Local processing on Hosting CSE | Trigger existing (OMA DM, BBF TR-069, LWM2M[refs]) device management procedures to execute the corresponding management command on the managed entity |
| Information on Response message | Proper error code if the external management object can not be executed |
| Post-Conditions | None |
| Exceptions | Corresponding external management object operation cannot be executed in managed entity due to some reason (e.g. not reachable, external management object not found) |

### -----------------------End of change 3---------------------------------------------

# Comments

child resource <parameters> removed.