| CHANGE REQUEST |
| --- |
| Group Name:* | ARC#10 |
| Source:* | Catalina Mladin, InterDigital Communications |
| Format:* | TP#10 |
| Date:* | 2014-07-08 |
| Contact:* | Catalina Mladin, InterDigital, Catalina.Mladin@InterDigital.com |
| Reason for Change/s:* | Corrections to mgmtcmd related text |
| CR against: Release* | Release 1 |
| CR against: TS/TR* | TS-001 v0.3.2 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

Corrections for mgmtCmd and execInstance:

- Change 1: Updated Table 9.6-1 ( Resource Summary) with the child and parent resource types.

- Change 2: Updated mgmtCmd resource with paramenters/ information for announcing

- Change 3: Added mgmtCmd to node resource .

### -----------------------Start of change 1-------------------------------------------

## 9.6	Specified Resource Types

Table 9.6-1 introduces the defined resource types and their related child or parent resource types. Details of each resource type follow in the remainder of this clause.

Table 9.6-1 Resource Summary

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Permissions for entities’ access modes | subscription | Application, remoteCSE | 9.6.2 |
| application | Represents information about an AE | subscription, container, group, accessControlPolicy, software, commCapabilities | remoteCSE | 9.6.5 |
| cmdhBuffer |  |  |  | 9.6.30 |
| cmdhDefaults |  |  |  | 9.6.24 |
| cmdhEcDefParamValues |  |  |  | 9.6.26 |
| cmdhDefEcValue |  |  |  | 9.6.25 |
| cmdhLimits |  |  |  | 9.6.27 |
| cmdhNetworkAccessRules |  |  |  | 9.6.28 |
| cmdhNwAccessRule |  |  |  | 9.6.29 |
| cmdhPolicy |  |  |  | 9.6.23 |
| container | Shares data instances among entities | container, instance, subscription, | application, container, remoteCSE | 9.6.6 |
| CSEBase |  |  |  | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | None documented | None documented | 9.6.11 |
| eventConfig |  |  |  | 9.6.32 |
| execInstance | Represents a successful instance of mgmtCmd | None | ?? | 9.6.18 |
| group | Represents a group of resources | members | Application, remoteCSE | 9.6.13 |
| instance | Data instance in a container | None documented | container | 9.6.7 |
| locationPolicy | Obtains/manages geographical location | None documented | None documented | 9.6.10 |
| members | Virtual resource target for group requests | None documented | group | 9.6.14 |
| mgmtCmd | Method to execute management procedures / model commands and RPCs for existing protocols | execInstance | node, CSEbase | 9.6.17 |
| mgmtObj | Represents individual management functions | parameters | remoteCSE | 9.6.15 |
| m2mServiceSubscription | Data pertaining to the M2M Service Subscription | None documented | None documented | 9.6.20 |
| node | Represents specific Node information | schedule, others | application (in ADN) | 9.6.19 |
| nodeInfo |  |  |  | 9.6.21 |
| parameters | Parameters/attributes for management purposes | parameters | mgmtObj, parameters | 9.6.16 |
| pollingChannel |  |  |  | 9.6.22 |
| remoteCSE | Represents a remote CSE registered to the local CSE | application, container, group, accessControlPolicy, subscription, mgmtObj | None documented | 9.6.4 |
| request | Expresses/access context of an issued Request | None documented | None documented | 9.6.12 |
| schedule | Contains scheduling information for delivery of messages | None documented | node, subscription | 9.6.39 |
| statsCollect |  |  |  | 9.6.33 |
| statsConfig |  |  |  | 9.6.31 |
| subscription | Information of subscribed-to resources | schedule | accessControlPolicy, application, container, group, remoteCSE | 9.6.8 |

{9.6.a} Editor’s Note: This Table was based upon revision 0.3.2 and may be missing information from subsequent agreed contributions. It is expected to be updated as we further define resources. Cells marked “None Documented” indicate the status of 0.3.2, if no addition is needed to these cells then they should be marked “None” when this Table is finalised.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.17	Resource Type mgmtCmd

The <mgmtCmd> resource represents a method to execute management procedures or to model commands and remote procedure calls (RPC) required by existing management protocols (e.g. BBF TR-069 [i.12]), and enables AEs to request management procedures to be executed on a remote entity. It also enables cancellation of cancellable and initiated yet unfinished management procedures or commands.

Figure 9.6.17-1: Structure of <mgmtCmd> resource 
(only resource specific attributes are shown)

Each <mgmtCmd> corresponds to a specific type of management command, as defined by its attribute cmdType. For multiple requests of the same management command, <mgmtCmd> may use the child-resource (i.e. <execInstance>) to contain all execution instances. The execution of the management procedure represented by <mgmtCmd> shall be triggered using the UPDATE method to its attribute "execEnable".

This resource shall contain the child resources according to their multiplicity in Table 9.6.17-1 (0 indicates the optionality of the child resource).

# Table 9.6.17-1: Child resources of <mgmtCmd> resource

| Child Resource Name of <mgmtCmd> | Child Resource Type | Multiplicity | Description | <mgmtCmdAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <execInstance> | 1 | See clause 9.6.18 | none |

The <mgmtCmd> resource shall contain the attributes described in Table 9.6.17-2.

# Table 9.6.17-2: Attributes of <mgmtCmd> resource

| Attribute Name of <mgmtCmd> | Multiplicity | RW/ RO/ WO | Description | <mgmtCmdAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | WO | See clause 9.6.1 where this common attribute is described | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described | MP |
| accessControlPolicyID (aRI) | 1 | RW | See clause 9.6.1 where this common attribute is described | MP |
| labels (lBs) | 1 | RW | See clause 9.6.1 where this common attribute is described | OP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <mgmtCmdAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| description | 0..1 | RW | The text-format description of this resource | OP |
| cmdType | 1 | WO | The type to identify the management operation (e.g. download). | MP |
| execReqArgs | 0..1 | RW | Structured attribute (e.g. abstract type) to contain any command-specific arguments of the request. | OP |
| execEnable | 1 | RO | The attribute can be blank without any value or it can contain a URI that can be used to trigger execution of <mgmtCmd> using UPDATE method. | MP |

### 9.6.18	Resource Type execInstance

The <execInstance> resource represents a successful instance of <mgmtCmd> execution request, which had been triggered by a M2M network application using the UPDATE method to the attribute "execEnable" of <mgmtCmd>.

Figure 9.6.18-1: Structure of <execInstance> resource 
(only resource specific attributes are shown)

The <execInstance> resource shall contain the attributes described in Table 9.6.18-1.

# Table 9.6.18-1: Attributes of <execInstance> resource

| Attribute Name of <execInstance> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| expirationTime (eT) | 1 | RO | See clause 9.6.1 where this common attribute is described |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aRI) | 1 | RW | See clause 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described |
| execStatus | 1 | RO | The status of <execInstance>. It can be Initiated, Started, Finished, Cancelled, or Deleted. |
| execResult | 1 | RO | The execution result of <execInstance>. |
| execDisable | 0..1 | RW | The attribute is used to cancel <execInstance> using UPDATE method. |
| execTarget | 1 | RW | M2M-Node-ID of the target. |
| execMode | 0..1 | RW | Modes used to specify how the command will be executed (e.g. Immediate Once, Immediate and Repeatedly, Random Once, Random and Repeatedly). May be used together with execFrequency, execDelay and execNumber to provide the scheduling information. |
| execFrequency | 0..1 | RW | The minimum interval between two executions, to be used in conjunction with execMode.Modes involving random execution can be used to add random values between individual executions. |
| execDelay | 0..1 | RW | The minimum delay before the instance should be executed. Modes involving random execution can be used to increase this delay randomly. |
| execNumber | 0..1 | RW | The number of times the instance should be executed, to be used when execMode indicates a repetition indicates repetition pattern.. |
| execReqArgs | 0..n | RW | Structured attribute (e.g. abstract type) to contain any command-specific arguments used to trigger this <execInstance>. |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 9.6.19	Resource Type node

The <node> resource represents specific information of a M2M Node that can be utilized by other oneM2M operations. For example, the CMDH CSF can determine when the CSE sends a request message to the target CSE based on the target CSE's reachability schedule. This resource type mainly contains the properties of an M2M Node such as reachability schedule, context information (e.g. memory and storage) and network topology.

This node specific information stored in this resource type such as memory and storage can be obtained either by the existing device management technologies (OMA DM, BBF TR-069 [i.12]) or any other way (e.g. through JNI (Java Native Interface)). Since <mgmtObj> and <mgmtCmd>  resource types represent the management functions including both ways, the types of sub-resources are <mgmtObj> and <mgmtCmd>  resource types.

The location of <node> resource can be differentiated according to the type of node.

ASN: under <CSEBase> of the ASN-CSE.

ADN: under <CSEBase> resource of the local CSE. The <application> resource regarding the ADN shall have the proper link (URI) to the <node> resource that contain node specific information of the ADN.

MN: under <CSEBase> of the MN CSE.

{9.6.19.a} Editor's Note: ADN case needs to be defined

{9.6.19.b} Editor's Note: More specific information regarding a node can be added.

Figure 9.6.19-1: Structure of <node> resource 
(only resource specific attributes are shown)

{9.6.19.c} Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the child resources according to their multiplicity in Table 9.6.19-1 (0 indicates the optionality of the child resource).

Table 9.6.19-1: Child resources of <node> resource

| Child Resource Name of <node> | Child Resource Type | Multiplicity | Description | <nodeAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| memory | <mgmtObj> | 0..1 | This resource provides the memory (typically RAM) information of the node. (e.g. the amount of total volatile memory), See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| storage | <mgmtObj> | 0..n | This resource provides the storage (typically flash or disk) information of the node. (e.g. the amount of total writable persistent storage). See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| power | <mgmtObj> | 0..1 | The resource provides the power information of the node. (e.g. remaining battery charge). See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| networkTopology | <mgmtObj> | 0..1 | This resource describes the list of Nodes attached behind the MN node and its underlying relation among the nodes in the M2M Area Network. This attribute is defined in case the Node is MN. See clause 9.6.15 for <mgmtObj>. | <mgmtObjAnnc> |
| schedule | <schedule> | 0..1 | This resource defines the reachability schedule information of the node. See clause 9.6.9 for <schedule>. | <scheduleAnnc> |
| mgmtCmd | <mgmtCmd> | 0..n | This resource provides the means to execute magement commands. See clause 9.6.16 for <mgmtcmd>. | <mgmtCmdAnnc> |

The <node> resource shall contain the attributes described in Table 9.6.19-2.

# Table 9.6.19-2: Attributes of <node> resource

| Attribute Name of <node> | Multiplicity | RW/ RO/ WO | Description | <nodeAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 1..n | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <nodeAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | OP |
| nodeID | 1 | RW | The ID of the Node which is specified in the resource type. This attribute is identical to M2M-Node-ID. | OP |
| hostedCSEID | 1 | RW | The ID of the CSEBase that is hosted on this node. | ?? |

### -----------------------End of change 3---------------------------------------------