| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC 10 |
| Title:* | Clarification for Routing Requests within the oneM2M System |
| Source:* | Ericsson |
| Contact: | George Foti |
| Date:* | 2014-03-30 |
| Abstract:* | Proposal to include the following in the TS |
| Agenda Item:* | To be defined |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to discuss the definitions for inclusion in the TS architecture |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution proposes some clarification to enable CSEs to handle routing in a clear fashion

* * * Start of 1st Change * * *

Table 8.2.2-1 Accessing Resources in different CSEs

| Traversals across X/Y Reference Points | Description | Reference |
| --- | --- | --- |
| No Hops | The Originator of the Request accesses a resource. The Originator of the Request can be an Application or a CSE. Local CSE and Hosting CSE are the same entity. The CSE shall check the Access Rights for accessing the resource. Depending on the expected result content, the CSE shall respond to the Originator of the Request, either with a Success or Failure Response, or not at all. | Figure 8.2.2-1 |
| 1 Hop | The Originator of the Request accesses a resource. The Originator of the Request may only be an Application. Local CSE and Hosting CSEs are different entities. Local CSE shall forward the Request to the Hosting CSE if it is registered with the local CSE, after an optional checking of the Access Rights for accessing the resource and the syntax of the Request message. Hosting CSE shall check the Access Rights for accessing the resource and depending on the expected result content respond with a Success or Failure Response, or not at all. | Figure 8.2.2-2 (Editor's Note-1) |
| Multi Hops | The Originator of the Request accesses a resource. The Originator of the Request may be an Application or a CSE. Local CSE, middle CSE(s) and the Hosting CSE are different entities. Local CSE has some options: Forward the Request to middle CSE (e.g. MN-CSE) that the Local CSE is registered with if configured through policies to do so. Forward the request to an IN if the local CSE is registered with the IN and if configured through policies to do so. An optional checking of the Access Rights for accessing the resource and the syntax of the Request message may be performed prior to forwarding the Request. Middle CSE has some options: Forward the request to the hosting CSE if it is registered with the middle CSE node. Forward the Request to another middle CSE (e.g. another MN-CSE) that the middle CSE is registered with if configured to do so via policies. Forward the request to an IN if the middle CSE is registered with the IN and is configured through policies to do so. An optional checking of the Access Rights for accessing the resource and the syntax of the Request message can be performed prior to forwarding the Request. The IN node has some options: Forward a request to another IN node if the resource belongs to another M2M SP. Forward the request to the hosting CSE if the later is registered with the IN An optional checking of the Access Rights and the syntax of the Request message can be performed prior to forwarding the Request .Hosting CSE shall check the Access Rights for accessing the resource and depending on the expected result content respond with a Success or Failure Response, or not at all. | Figure 8.2.2-3 Figure 8.2.2-4 (Editor's Note-2) |
| Editor's Note-1: One-Hop case could potentially include the CSE-to-CSE communication also. The need for such procedures is FFS. Editor's Note-2: The multi-hop procedures address the scenario when the target is on a specific remote CSE. How a flow will work when the target is distributed on multiple remote CSEs is FFS. |

Figure 8.2.2-4

* * * End of 1st Change * * *

* * * Start of 2nd Change * * *

8.2.2.1 M2M Requests Routing Policies

Policies can be downloaded in various M2M nodes to govern routing of M2M requests to the next hop towards its target. Routing, through these policies, can be based, for example, on the target CSE, target M2M domain, specific types of resources if applicable, priority of a request, etc.

These policies are however out scope. It is the responsibility of M2M SP and the M2M node administrator to ensure the appropriateness of these policies for routing purposes. M2M responses shall follow the same route as their corresponding M2M requests.

It is also important to note that the IN node is typically the node that is capable of routing any request to its target and as such it can always be a default next hop for any request.

* * * End of 1nd Change * * *