| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC10 at |
| Title:* | Additional Specification for Creating of DNS Entries for Inter-M2M Service Provider Communications |
| Source:* | Ericsson |
| Contact: | George Foti |
| Date:* | 2014-03-30 |
| Abstract:* | Proposal to include the following in the TS |
| Agenda Item:* | To be defined |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to discuss the definitions for inclusion in the TS architecture |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution proposes additional text that describes related to when the DNS entries are created for Inter-M2M Service Provider Communications.

* * * Start of 1st Change * * *

### 6.5.3. DNS Provisioning for Inter-M2M SP Communication

As mentioned previously, any M2M SP supporting inter-M2M SP communication shall ensure that the public domain names for the CSEs whose functionality is available across domains are held in its DNS and shall always point to the IP address associated with the Infrastructure Node for the domain (being the entry point) for accessibility purposes.

This implies that the IN shall be responsible for creating the appropriate entry in its DNS for a successfully registered CSE in the IN if the M2M SP policies do allow access to the CSE across multiple M2M domains. Similarly the IN shall be responsible for deleting the appropriate entry in its DNS for a successfully de-registered CSE in the IN if the M2M SP policies do allow access to the CSE across multiple M2M domains

### 6.5.3.1 Inter-M2M SP Communication Access Control Policies

DNS entries may be complemented with additional M2M SP policies that further restrict access to CSE resources to requests originating from configured M2M SPs only.  These policies are out of scope

* * * End of 1st Change * * *

* * * Start of 2nd Change * * *

#### 10.2.2.1	Create <RemoteCSE>, aka CSE Registration

This flow is used for creating a <RemoteCSE> resource. It is part of the registration procedure for remote CSEs on the local CSE (which is also the hosting CSE), as described in section 10.1.1.2.1

Originator:  A CSE.

Receiver : Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), the Receiver shall grant the request after successful verification of the request.

If the IN is the receiver and if the M2M SP policies do allow access to the CSE across multiple M2M domains, then the IN shall create the appropriate entry in its DNS for a successfully registered CSE.

Table 10.2.2.1-1 <remoteCSE> CREATE flow

| CREATE: Description |
| --- |
| Pre-Conditions | The Originating CSE is successfully authorized. The Originating CSE has an assigned CSE-ID.. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable plus specifically: fr: CSE-ID. nm: the name of the <remoteCSE> resource is optionalcn: the resource content shall provide the information as defined in section 9.6.19. The following attributes from section 9.6.19 are mandatory for the request: “resourceType” which shall be set to the appropriate tag that identify the <remoteCSE> resource as defined in 9.6.1 “CSE-ID”: which contains the CSE-ID “CSEType” The following attributes from section 9.6.19 are optional for the request: “expirationTime” “accessControlPolicyID” “labels” “pointOfAccess” |
| Local processing on Hosting CSE | No change from the basic CREATE procedure (section 10.1.1) |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the table with the specific details for: cn: URI of the created <remoteCSE> resource, according to section 10.1.1 |
| Post-Conditions | Two new <remoteCSE> resources are created, one on the targeted CSE (Receiver) and one under the <CSEBase> of the Originator that correspond to the CSE of the Receiver. If the IN is the receiver and if the M2M SP policies do allow access to the CSE across multiple M2M domains, then the IN shall create the appropriate entry in its DNS for a successfully registered CSE. |
| Exceptions | All exception described in the basic CREATE procedure (section 10.1.1) are applicable. |

#### 10.2.2.4	Delete <remoteCSE>, aka CSE De-Registration

This flow is used for de-registering and deleting the <remoteCSE> resource with all related information.

Originator: An AE or a CSE.

Receiver: Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), the Receiver shall delete the <remoteCSE>.

If the IN is the receiver and it has created an entry in the DNS to allow access to the CSE across multiple M2M domains, then it shall delete the entry from the DNS.

Table 10.2.2.4-1 <remoteCSE> DELETE flow

| DELETE: Description |
| --- |
| Pre-Conditions | The targeted <remoteCSE> has been created (as part of the registration) |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable |
| Local processing on Hosting CSE | No change from the basic DELETE procedure (section 10.1.4). For <remoteCSE>, if the resource is deleted then the Hosting CSE should also delete the correspondent DNS entry, if it exists. |
| Information on Response message | No change from the basic DELETE procedure (section 10.1.4) |
| Post-Conditions | The targeted resource and all the children resources shall not exist anymore. Also all the related credential are deleted. If the IN is the receiver and it has created an entry in the DNS to allow access to the CSE across multiple M2M domains, then it shall delete the entry from the DNS. Editor’s note: if and how credentials are cleaned is FFS, in scope of WG4. |
| Exceptions | All exception described in the basic DELETE procedure (section 10.1.4) are applicable. |

* * * End of 2nd Change * * *