| CHANGE REQUEST |
| --- |
| Group Name:* | TP#10 |
| Source:* | Huawei |
| Format:* | WG2 |
| Date:* | <2014-03-31> |
| Contact:* | Mitch Tseng, Huawei Technologies, mitch @T-infoserv.com |
| Reason for Change/s:* | This contribution propose modifications related to Discovery CSF. |
| CR against: Release* | Release 1.0.0 |
| CR against: TS/TR* | TS-0001-Functional_Architecture-V0_4_3 |
| Clauses/Sub Clauses* | Section 6.2.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

# The current Discovery (DIS) CSF indicated the discovery of resources within a CSE; however, there are service scenarios, e.g. a data aggregator handling multiple application nodes or subservices which perform the data collecting individually, that an application/service will be to be discovered.  The current discovering mechanism via providing filter criteria seems to capable of achieve this objective but it was not clearly specified in the text.  This CR proposes to further clarifiy the concept so that an application/service registered with the Receiver CSE can be supported.  The current assessment is that the procedures in 10.2.5.2 can support this work already so no further modification is needed.

### -----------------------Start of change 1-------------------------------------------

### 6.2.5	Discovery

#### 6.2.5.1	General Concepts

Discovery (DIS) CSF is responsible for searching information i.e. supported attributes, description of applications/services and resources according to a Request from an Originator within a given scope, filter criteria and subject to permissions, including those allowed by M2M service subscription. An Originator could be an Application or another CSE. The scope of the search could be in one CSE, or in more than one CSE. The discovery results are returned back to the Originator.

#### 6.2.5.2	Detailed Descriptions

DIS CSF shall provide discovery of information,resources, or applications/services residing in its own CSE subject to permissions including the M2M service subscription. The DIS CSF shall be able to support various discovery methods through the Originator provided "filter criteria" that can limit the scope of information/resources that are returned based on various filters (e.g. keyword, identifiers, location, semantic information) or a combination of such filters.

The DIS CSF shall be triggered by sending a "request" to the address (e.g. URI) of the discovery resource. Upon receiving such request, the DIS CSF shall discover, identify and return the matching information/resources according to the filter criteria. A successful response may include the actual discovered information or address(es) (e.g. URI(s)) pertaining to the discovered resources residing in its own/registered CSE(s), then the Originator can retrieve the resources using the address. In addition, based on the policies or Originator request, the CSE which received the Discovery request may forward the request to other CSEs on its registered Middle/Infrastructure Node.

….

### -----------------------End of change 1---------------------------------------------