| CHANGE REQUEST |
| --- |
| Group Name:* | TP#10 |
| Source:* | Huawei |
| Format:* | WG2 |
| Date:* | <2014-03-31> |
| Contact:* | Mitch Tseng, Huawei Technologies, mitch @T-infoserv.com |
| Reason for Change/s:* | This contribution proposes modifications related to Registration CSF to clarify the support for Application Discovery. |
| CR against: Release* | Release 1.0.0 |
| CR against: TS/TR* | TS-0001-Functional_Architecture-V0_4_3 |
| Clauses/Sub Clauses* | Section 6.2.9 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

# The Registration CSF is defined at section 6.2.9. Although an Application is allowed to register with another Application or a CSE, the current text does not reflect the information covers Application.  This CR proposes to have add Registration information to explicitly include the application/service information so that an Application registrated on a CSE can be discovered via Discovery CSF with the same procedure as discovering a resource on a CSE.

### -----------------------Start of change 1-------------------------------------------

### 6.2.9	Registration

#### 6.2.9.1	General Concepts

Registration (REG) CSF is responsible for processing a request from an Application or another CSE to register with a CSE in order to allow the registered entities to use the services offered by the registered-with CSE. The REG CSF processes registration of a Device also, to allow registration of Device's properties/attributes with the CSE.

#### 6.2.9.2	Detailed Descriptions

Registration is the process of delivering AE or CSE information to another CSE in orderto use M2M Services.

An Application on an Application Service Node, a Middle Node, or an Infrastructure Node shall perform registration locally with the corresponding CSE in order to use M2M services offered by that CSE. An Application on an Application Dedicated Node shall perform registration with the CSE on a Middle Node or Infrastructure node in order to use M2M services offered by that CSE. A node-less AE shall perform registration with the corresponding CSE on an Infrastructure node in order to use M2M services offered by that CSE. A registered Application shall be able to have interactions with its local CSE (when it is the target CSE) without the need to have the local CSE register with other CSEs.

The CSE on an Application Service Node shall perform registration with the CSE in the Middle Node in order to be able to use M2M services offered by the CSE in the Middle Node. As a result of successful ASN-CSE registration with the MN-CSE, the CSE on the ASN Node establish a peering relationship and shall be able to exchange information.

The CSE on a Middle Node shall perform registration with the CSE of another Middle Node in order to be able to use M2M services offered by the CSE in the other Middle Node. As a result of successful MN-CSE registration with the other MN-CSE, the CSE on the Middle Nodes establish a peering relationship and shall be able to exchange information.

The CSE on an Application Service Node or on a Middle Node shall perform registration with the CSE in the Infrastructure Node in order to be able to use M2M services offered by the CSE in the Infrastructure Node. As a result of successful ASN/MN registration with the IN-CSE, the CSEs on ASN/Middle Node and Infrastructure Node establish a peering relationship and shall be able to exchange information.

For an Application/CSE registering with another CSE, it shall be possible that  the CSE can expose (assuming permission is granted) the resources and applications/services registeded locally through Discovery CSF.

Applications shall be able to exchange information via CSEs following successful registration of:

- Applications with their associated CSE

- One of these CSEs with the other CSE, as per Table 6.2.9.2-1

Such registrations are applicable to a single M2M Service Provider Domain.

A (physical) Device shall be able to register with its local CSE for registering its properties/attributes. Such registration enables correlation of Devices Identities such as M2M-Node-ID with the CSE-ID.

{6.2.9.2.a} Editor's Note: The need for Device Registration and the relationship with CSE Registration are FFS.

{6.2.9.2.b} Editor's Note: The use of External ID in Registration is FFS.

The following Table shows which oneM2M entity types may register with which other entity types.

Table 6.2.9.2-1: Entity Registration

| Originator (Registree) | Receiver (Registrar) | Registration Procedure |
| --- | --- | --- |
| ADN-AE | MN-CSE, IN-CSE | AE registration procedure see clause TBD |
| ASN-AE | ASN-CSE |  |
| MN-AE | MN-CSE |  |
| IN-AE | IN-CSE |  |
| Nodeless AE | IN-CSE |  |
| ASN-CSE | MN-CSE, IN-CSE | CSE registration procedure see clause TBD |
| MN-CSE | MN-CSE, IN-CSE |  |

The Originator (Registree) in Table 6.2.9.2-1 requests the registration and the Receiver (Registrar) is responsible for verifying the request, and checking the authentication and authorization of the Originator in order to establish a peer relationship.

{6.2.9.2.c} Editor’s Note: Authorization above might only be needed for AEs, this is FFS in Security WG

An instance of the same AE shall register to one CSE (ASN-CSE, MN-CSE or IN-CSE) at one time.

An instance of the same ASN-CSE shall register with one other CSE (MN-CSE or IN-CSE) at one time.

An instance of the same MN-CSE shall register with one other IN-CSE at one time.

An MN-CSE shall support only a single registration towards another MN-CSE or an IN-CSE. A concatenation (registration chain) of multiple uni-directional registrations shall not form a loop. E.g. Two MN-CSEs A and B, shall not register with each other. Three MN-CSEs A, B and C, where A registers to B, and B registers to C, then C shall not register to A.

{6.2.9.2.d} Editor’s Note: The use of “instance” above might be removed if other definitions are changed. If kept, the description regarding “instances” should be expanded.

Registration information shall be able to include:

Identifier.

Reachability schedules; which are elements of a node's policy, and specify when messaging may occur between nodes. Reachability schedules may be used in conjunction with other policy elements. When reachability schedules are not present in a node then that node is expected to be always reachable.

Description of resources or applications/services of the registeree Application/CSE.

{6.2.9.2.e} Editor's note: Further Registration information is FFS.

### -----------------------End of change 1---------------------------------------------