| CHANGE REQUEST |
| --- |
| Group Name:* | <WG2> |
| Source:* | Rajesh Bhalla, ZTE, rabhalla@ztetx.com Hao Wu, ZTE, wu.hao18@zte.com.cn +++ |
| Format:* | ARC #10.1 |
| Date:* | 2014-04-xx |
| Contact:* | Rajesh Bhalla, Hao Wu, ZTE +++ |
| Reason for Change/s:* | Support Partial Address in oneM2M |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.4.2 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes support for Partial Addressing in oneM2M.

Such partial addressing is proposed to be supported by the use of UPDATE and DELETE operations.

### -----------------------Start of change 1-------------------------------------------

### 8.1.1	Description

Figure 8.1.1-1 shows the general flow that governs the information exchange within a procedure, which is based on the use of Request and Response scheme. The scheme applies to communications such as:

between an AE and a CSE (Mca reference point); and

among CSEs (Mcc reference point).

The communications can be initiated either by AEs or by CSEs depending upon the operation in the Request message.

# Figure 8.1.1-1:  General Flow

### 8.1.2	Request

Request from an Originator to a Receiver includes the following information:

to: URI of the target resource or the target attribute for the operation. The to information shall conform to clause 9.3.1.

NOTE 1:   The to target resource or target attribute needs to be known by the Originator. It can be known either by pre-provisioning or by discovery.

Editor's Note: How pre-provisioning and discovery are performed is FFS.

NOTE 2: 	The term target resource always refers to the resource which is addressed for the specific operation. For example the to parameter of a Create operation for a resource “example” would be “/m2m.provider.com/exampleBase”. The to parameter for the Retrieve operation of the same resource “example” is “/m2m.provider.com/exampleBase/example”. When used for addressing a specific attribute (e.g., for partial addressing) with DELETE operation, the to parameter for "container" attribute in the above example is “/m2m.provider.com/exampleBase/example/container”.

fr:  Identifier representing the Originator.

NOTE 3:	The fr information shall be used by the Receiver to check the Originator identity for access privilege verification.

cn: resource content to be transferred.

op: operation to be executed: Create (C), Retrieve (R), Update (U), Delete (D).

The op information shall indicate the operation to be executed at the Receiver:

Create (C): a new resource addressable with to parameter is created.

Retrieve (R): an existing to addressable resource is read and provided back to the Originator.

Update (U): the content of an existing to addressable resource is replaced with the new content as in cn parameter. For partial addressing, the attributes in the cn parameter are created and assigned associated values.

Delete (D): an existing to addressable resource and all its sub-resources are deleted from the Resource storage. For partial addressing, the existing to addressable attribute is deleted.

Notify (N):  information to the Receiver, processing on the Receiver is not indicated by the Originator.

The ty information shall be present in Request for the following operations:

Create: ty is the type of the resource to be created.

cn: resource content to be transferred.

The cn information shall be present in Request for the following operations:

Create: cn is the content of the new resource with the resource type tag as in Table 9.2-1.

Update: cn is the content to be replaced in an existing resource. For partial addressing, cn is the new attributes and their associated values to be created at the resource addressed by the to parameter.

Retrieve: cn is the filter to be applied for discovery purposes.

Notify: cn is the notification information.

Note that the cn information can also be empty.

Other allowed information shall be as follows:

nm:  optional name of the resource to be created.

Example usage of the name includes a name that the Originator of the Create resource wishes to be used as the identifier of the newly created resource. For creating a container with the name “myContainer” the request will provide the parameter nm with the value “myContainer” and the created resource would be: /<SCEBase>/myContainer.

ot: optional originating timestamp of when the message was built.

Example usage of the originating timestamp includes: to measure and enable operation (e.g. message logging, correlation, message prioritization/scheduling, accept performance requests, charging, etc.) and to measure performance (distribution and processing latency, closed loop latency, SLAs, analytics, etc.)

rqet: optional request message expiration timestamp.

Example usage of the request expiration timestamp includes to indicate when request messages (including delay-tolerant) should expire due to their staleness being no longer of value, and to inform message scheduling/prioritization. When a request has set request expiration timestamp to a specific time and the Request demands an operation on a Hosting CSE that is not the CSE currently processing the request, then the current CSE shall keep on trying to deliver the Request to the Hosting CSE until the request expiration timestamp time, in line with provisioned policies.

rset: optional result message expiration timestamp.

Example usage of the result expiration timestamp includes to indicate when result messages (including delay-tolerant) should expire due to expected staleness of the result, being no longer of value, and to inform message scheduling/prioritization. It can be used to set the maximum allowed total request/result message sequence round trip deadline.

rt: optional response message type: indicates  what the response to the issued request shall contain and when the response is sent to the Originator:

Acknowledgement: In case the request is accepted by the Local CSE, the Local CSE responds after acceptance with an Acknowledgement confirming that the Local CSE will further process the request.

Result: In case the request is accepted by the Local CSE, the Local CSE responds with the result of the requested operation after completion of the requested operation.

Example usage of the response type set to Acknowledgment: An Originator that is optimized to minimize communication time and energy consumption wants to express a Request to the local CSE and get an acknowledgement on whether the Request got accepted. After that the Originator may switch into a less power consuming mode and retrieve a Result of the requested Operation at a later time.

rd: optional result message destination:

Local CSE: The Local CSE includes in the response to an accepted request a reference that can be used to access the status of the request and the result of the requested operation at a later time.

Originator: The result of the requested operation needs to be sent as a notification to the Originator.

Example usage of the result destination set to Local CSE includes when the result content is extremely large, or when the result consists of multiple content parts from a target group which are to be aggregated asynchronously over time.

rc: optional result message content: Indicates what are the expected components of the result of the requested operation. The Originator of a request may not need to get back a result of an operation at all. This shall be indicated in the rc information. Which exact settings of rc are possible depends on the requested operation specified in op. Possible values of rc are:

"resource": Only a representation of the requested resources will be returned as content, without any mention of the links of the requested resources to other resources. This is the default value.

"resource;links": A representation of the requested resources, along with all links to other resources (possibly limited by a maximum number of retrieved links), will be returned as content.

"links": Only the links of the requested resources to other resources (possibly limited by a maximum number of retrieved links), without any representation of the actual resources requested, will be returned as content.

"nothing": Nothing will be returned as content of the Response.

"result-notification": A notification will be returned when the operation is completed.

Editor's Note: Details on what settings for rc are possible can be added at a later when the specific operations that can be requested are defined (e.g. register an AE, modify content of a container, etc.)

rp: optional response persistence: indicates the duration for which the address containing the responses is to persist.

Example usage of response persistence includes requesting sufficient persistence for analytics to process the response content aggregated asynchronously over time. If a result expiration timestamp is specified then the response persistence should last beyond the  result expiration time.

ri: request Identifier

Example usage of request identifier includes enabling the correlation between a Request and one of the many received Responses.

oet: optional operational execution time: indicates the time when the specified operation op is to be executed by the target CSE. A target CSE shall execute the specified operation of a Request having its operational execution time indicator set, starting at the operational execution time. If the execution time has already passed or if the indicator is not set, then the specified operation shall be immediately executed, unless the request expiration time, if set, has been reached.

Example usage of operational execution time includes asynchronous distribution of flows, which are to be executed synchronously at the operational execution time.

NOTE 4:	Time-based flows may not be able to be supported depending upon time services available at CSEs.

ec: optional event category: Indicates the event category that should be used to handle this request. Event categories are impacting how Requests to access remotely hosted resources are processed in the CMDH CSF. Selection and scheduling of connections via CMDH are driven by policies that can differentiate event categories.

Example usage of "event category" set to specific value X: When the request is demanding an operation to be executed on a Hosting CSE that is different from the Local CSE, the request may be stored in the CSE that is currently processing the request on the way to the Hosting CSE until it is allowed by provisioned policies for that event category X to use a communication link to reach the next CSE on a path to the Hosting CSE or until the request expiration timestamp is expired.

da: optional delivery aggregation on/off: Use CRUD operations of <delivery> resources to express forwarding of one or more original requests to the same target CSE(s).

NOTE 4:	Since da is optional, there could be a default value to be used when not present in the Request. This parameter 	may not be exposed to AEs via Mca.

Example usage of delivery aggregation set on: The CSE processing a request shall use aggregation of requests to the same target CSE by requesting CREATE of a <delivery> resource on the next CSE on the path to the target CSE.

gid: optional group request identifier: Identifier added to the group request that is to be fanned out to each member of the group.

fc:  optional filter criteria: conditions for filtered retrieve operation are described in Table 8.1.2-1.

Table 8.1.2-1: Filter criteria conditions

| Condition tag | Multiplicity | Matching condition |
| --- | --- | --- |
| createdBefore | 0..1 | The creationTime attribute of the resource is chronologically before the specified value. |
| createdAfter | 0..1 | The creationTime attribute of the resource is chronologically after the specified value. |
| modifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically after the specified value. |
| unmodifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically before the specified value. |
| expireBefore | 0..1 | The expirationTime attribute of the resource is chronologically before the specified value. |
| expireAfter | 0..1 | The expirationTime attribute of the resource is chronologically after the specified value. |
| labels | 0..n | The labels attributes of the resource matches the specified value. |
| resourceType | 0..n | The resourceType attribute of the resource is the same as the specified value. It also allows discriminating between normal and announced resources. |
| sizeAbove | 0..1 | The contentSize attribute of the <instance> resource is equal to or greater than the specified value. |
| sizeBelow | 0..1 | The contentSize attribute of the <instance> resource is smaller than the specified value. |
| contentType | 0..n | The typeOfContent attribute of the <instance> resource matches the specified value |
| limit | 0..1 | Limitation the number of matching resources to the specified value. |
| attribute | 0..n | Attribute token name to be provided to reduce the scope of filtering to resource attributes. |

Example usage of filter criteria conditions in a HTTP query: an HTTP GET operation can be requested applying also a filter in the query part of the request itself:

GET /root?label=one&label=two&createdBefore=2014-01-01T00:00:00&limit=128

The example discovers a maximum of 128 resources matching the following logical condition: createdBefore < 2014-01-01T00:00:00 AND (label = one OR label = two).

Once the Request is delivered, the Receiver shall analyze the Request to determine the target resource.

If the target resource is addressing another M2M node, the Receiver shall route the request appropriately.

If the target resource is addressing the Receiver, it shall:

Check the existence of to addressed resource.

Identify the resource type with the tag value as in Table 9.2-1.

Check the previleges for fr Originator to perform the requested operation.

Perform the requested operation (using cn content when provided) according to the provided request parameters as described above.

Depending on the request result content, respond to the Originator with indication of successful or unsuccessful operation results. In some specific cases (e.g. limitation in the binding protocol or based on application indications), the Response could be avoided.

The message flow procedure started with an Originator Request message shall be considered closed when either:

A Request message is expired according to the rqet (request expiration timestamp).

A Response message is delivered to the Originator.

#### 8.1.2.1	Summary of Request Message Parameters

Table 8.1.2.1-1summarises the parameters specified in clause 8.1.2 for the Request message, showing any differences as applied to C, R, U, D or N operations. "M" indicates mandatory, "O" indicates optional, "N/A" indicates "not applicable".

# Table 8.1.2.1-1: Summary of Request Message Parameters

| Request message parameter \ Operation | Create: a new resource is created | Retrieve: an existing resource is read and the result is provided | Update: the content of an existing resource is replaced with new content | Delete: an existing resource and all its sub-resources are deleted | Notify: the content / address is transferred |
| --- | --- | --- | --- | --- | --- |
| Operation (op) - operation to be executed | M | M | M | M | M |
| To (to) – the address of the target resource or the target attribute on the target CSE | M | M | M | M | M |
| From (fr) – the identifier of the message Originator | M | M | M | M | M |
| Request Identifier (ri) – uniquely identifies a Request message | M | M | M | M | M |
| Resource Type (ty) - of resource to be created | M | N/A | N/A | N/A | N/A |
| Name (nm) - of resource to be created | O | N/A | N/A | N/A | N/A |
| Content (cn) - to be transferred | O | O | M | N/A | M |
| Originating Timestamp (ot) - when the message was built | O | O | O | O | O |
| Request Expiration Timestamp (rqet) – when the request message expires | O | O | O | O | O |
| Result Expiration Timestamp (rset) -when the result message expires | O | O | O | O | O |
| Operational Execution Time (oet) - the time when the specified operation is to be executed by the target CSE. | O | O | O | O | O |
| Response Type (rt) – local CSE response shall either indicate that the Request was accepted, or include the operation result | O | O | O | O | O |
| Result Destination (rd) – either a reference to where the result is stored, or the result is sent to the Originator | O | O | O | O | N/A |
| Result Persistence (rp) - the duration for which the reference containing the responses is to persist | O | O | O | O | N/A |
| Result Content (rc) – the expected components of the result | O | O | O | O | N/A |
| Event Category (ec) – indicates how and when the system should deliver the message | O | O | O | O | O |
| Delivery Aggregation (da) - aggregation of requests to the same target CSE is to be used | O | O | O | O | O |
| Group Request Identifier (gid) - Identifier added to the group request that is to be fanned out to each member of the group. | O | O | O | O | O |
| Filter Criteria (fc) – conditions for filtered retrieve operation | N/A | O | N/A | N/A | TBD |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 8.1.3	Successful Operation

For the case of successful completion of a requested operation, the Response from the Receiver to the Originator of that Request includes the following information:

to: Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request, "rd" information can be used.

fr: Optional. ID of the Receiver.

rs: operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc.

cn: optional resource content to be transferred or created (optional).

The meta information includes:

ot: optional originating timestamp of when the message was built.

rset: optional result expiration timestamp. The Receiver shall echo the result expiration timestamp if set in the Request message, or may set the result expiration timestamp itself.

Example usage of the Receiver setting the result expiration timestamp is when the value of the delivery time is dependent upon some changing Receiver context eg. Result message deadline for aircraft position based upon velocity.

ri: request Identifier

Note that ri in Response shall match the ri in the corresponding Request.

cs: optional, status codes (e.g. authorization timeout, etc.).

ra: optional, address for the temporary storage of end node Responses.

The cn information may be present in a Response in the following cases:

Create: cn is the address and/or the content of the created resource.

Update: cn is the content replaced in an existing resource. cn is the newly created attributes and their values for partial addressing.

Delete: cn is the content actually deleted.

The cn information shall be present in a Response in the following cases:

Retrieve: cn is the retrieved resource content or aggregated contents of discovered resources.

### 8.1.4	Unsuccessful Operation

The Response from the Receiver of a Request to the Originator of the Request, in the case of unsuccessful completion of the requested operation includes the following information:

to: Optional.  Identifier the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , "rd" information can be used.

fr: Optional. Identifier of the Receiver.

rs: operation result: e.g. Not okay.

cn: optional, status codes (e.g., authorization, timeout, etc.)

The meta information includes:

ot: optional originating timestamp of when the message was built.

rset: optional result expiration timestamp.

ri: Request Identifier.

Note that ri in a Response shall match the ri in the corresponding Request.

cs: optional, status codes (e.g. authorization timeout, etc.).

### 8.1.5	Summary of Response Message Parameters

Table 8.1.5-1 summarises the parameters specified in clauses 8.1.1 and 8.1.3 for the Response messages, showing any differences as applied to successful C, R, U, D or N operations, and unsuccessful operations. "M" indicates mandatory, "O" indicates optional, "N/A" indicates "not applicable".

# Table 8.1.5-1: Summary of Response Message Parameters

| Response message parameter \ success or not | Successful operation: Create: a new resource is created | Successful operation: Retrieve: an existing resource is read and the result is provided | Successful operation: Update: the content of an existing resource is replaced with new content | Successful operation: Delete: an existing resource and all its sub-resources are deleted | Successful operation: Notify: the content / address is transferred | Unsuccessful Operation |
| --- | --- | --- | --- | --- | --- | --- |
| To (to) –the identifier of the Originator | O | O | O | O | O | O |
| From (fr) – the identifier of the Receiver | O | O | O | O | O | O |
| Request Identifier (ri) – uniquely identifies a Request message | M | M | M | M | M | M |
| Result (rs) - operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., | M | M | M | M | M | M |
| Status codes (cs) - (e.g., authorization timeout, etc.) | O | O | O | O | O | O |
| Response Address (ra) - address for the temporary storage of end node Responses. | O | O | O | O | N/A | N/A |
| Content (cn) - to be transferred | O (The address and/or the content of the created resource) | M (the retrieved resource content or aggregated contents of discovered resources) | O (The content replaced in an existing resource. The content of the new attributes created for partial addressing). | O (The content actually deleted) | N/A | N/A |
| Originating Timestamp (ot) - when the message was built | O | O | O | O | O | O |
| Result Expiration Timestamp (rset) – when the message expires | O | O | O | O | N/A | O |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 10.1.3	UPDATE (U)

The UPDATE operation shall be used for updating the information stored for any of the attributes at a target resource. Especially important is the "expirationTime", since a failure in refreshing this attribute may result in the deletion of the resource. The Originator CSE or AE can request to update specific attribute(s) at the target resource by including the name of such attribute(s) and their values in the Request message.

UPDATE operation shall be used for "partial addressing" as well. Specific attributes can be created by the use of UPDATE operation by including the name of such attribute(s) and their values in the Request message.

Originator requests to update any of the attributes at the target resource by using UPDATE Request message. The Originator shall send new (proposed) values for the attribute(s) that need to be updated. The UPDATE operation allows to modify the attributes (defined in clause 9.6) that are indicated as “RW” (Read Write) for the specific resource type.

The Originator requests to create attributes at the target resource by using UPDATE Request message. The Originator shall send the name of the attributes to be created (defined in clause 9.6) that are indicated as "RW" (Read Write) for the specific resource type and their associated values in the Request message,

See clause 8.1.2 for the information to be included in the Request message.

Receiver once the Originator has been successfully authenticated, the Receiver verifies the existence of the addressed resource, the validity of the attributes provided and the privileges to modify them, shall update the attributes provided and shall return a Response message to the Originator with the operation results as specified in clause 8.1.3. For partial addressing, after verifying the existence of the addressed resource, the Receiver validates the attributes provided and the privileges to create them. On successful validation, the Receiver creates the attributes provided with their associated values and shall return a Response message to the Originator with the operation results as specified in clause 8.1.3.

# Figure 10.1.3-1: Procedure for UPDATing a Resource

Step 001: The Originator shall send the following information in the UPDATE Request message:

op:	U (Update)

to: 	URI to the target resource

# fr: 	ID of the Originator (either the AE or CSE)

cn: 	Information related to the attribute(s) to be updated or created at the target resource. The name of such attribute(s) and associated updated or assigned values in the cn parameter.

Step 002: The Receiver shall validate if the Originator has appropriate privileges to perform the modification to the target resource. On successful validation, the Receiver shall update the resource as requested. For partial addressing, the Receiver shall validate if the Originator has appropriate privileges to create the attributes at the target resource. On successful validation, the Receiver shall create the attributes with their associated values at the resource as requested.

Step 003: The Receiver shall respond with a Response message that shall contain the following information:

to:	Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

# fr:	Optional. ID of the Receiver.

rs:	Operation result

cn:	Optional. Content replaced or created

# General Exceptions:

- The targeted resource in to information does not exist. The Receiver responds with an Error.

- The Originator does not have the privilege to modify the resource or create attributes on the Receiver. The Receiver responds with Error.

- The provided information in the cn is not accepted by the Receiver. The Receiver responds with Error.

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 10.1.4	DELETE (D)

The DELETE operation shall be used by an Originator CSE or AE to delete a resource at a Receiver CSE.

The DELETE operation shall also be used by the Originator CSE or AE to delete a specific attribute from a target resource at the Receiver CSE.

The DETETE procedure shall consist of the deletion of all related information of the target resource.

Originator requests to delete a resource or attribute by using a DELETE Request message. See clause 8.1.2 for the information to be included in the Request message.

Receiver once the Originator has been successfully authenticated, the Receiver verifies the existence of the requested resource or attribute, and the privileges for deleting the resource or attribute.

# Figure 10.1.4-1: Procedure for DELETING a Resource or Attribute

Step 001: The Originator shall send a DELETE Request message to the Receiver.

op:	D (Delete)

to: 	URI of the target resource or attribute

# fr: 	ID of the Originator (either the AE or CSE)

Step 002: The Receiver shall verify the existence of the requested resource or attribute and if the Originator has the appropriate privilege to delete the resource/attribute. For the deletion of a resource, on successful validation, the Receiver shall check for children resources and delete all children resources and the associated references in parent resources and it shall remove the resource itself. For the deletion of an attribute, on successful validation, the Receiver shall delete the addressed attribute.

Step 003: The Receiver shall respond with a Response message that shall contain the following information:

to:	Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

# fr:	Optional. ID of the Receiver.

rs:	Operation result

# General Exceptions:

- The targeted resource/attribute in to information does not exist. The Receiver responds with an Error.

- The Originator does not have the privileges to delete the resource/attribute on the Receiver. The Receiver responds with an Error.

### -----------------------End of change 4-------------------------------------------