| CHANGE REQUEST |
| --- |
| Group Name:* | ARC WG2 |
| Source:* | ALU, NTT DOCOMO |
| Format:* | ARC 10.0 bis Ad Hoc – Sophia Antipolis |
| Date:* | 2014-04-28 |
| Contact:* | Tim Carey, timothy.carey@alcatel-lucent.com Syed Husain, shusain2016@live.com |
| Reason for Change/s:* | Cleanup of ASM CSF description |
| Clause/Sub Clause Affected* | 6.2.1 Application and Service Layer Management |
| Agenda Item:* | 6 |
| Work item(s): | Arch TS |
| Document(s) Impacted* | TS-0001 v0.5.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Move to architecture for inclusion in the Arch TS-0001. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes to clean-up the ASM CSF description in clause 6.2.1, based on the agreement reached at TP#10 on Option 1 of ARC-2014-1218R01. All the editor’s notes are addressed as well.

----------------------------------------- Start of changes ------------------------------------

### 6.2.1	Application and Service Layer Management

#### 6.2.1.1	General Concepts

The Application and Service Layer Management (ASM) CSF provides management of the AEs and CSEs on the ADNs, ASNs, MNs, and INs. This includes functions to configure, troubleshoot and upgrade the functions of the CSE, as well as to upgrade the AEs.

#### 6.2.1.2	Detailed Descriptions

The ASM CSF provides management capabilities for a CSE and the AEs.

# Figure 6.2.1.2-1: Management Layers and Functions

<Rapporteur Note: Picture above has been changed.

The ASM CSF utilizes the functions provided by the DMG CSF for interaction with the Management Server.

The management functions include:

Configuration Function (CF): This function includes the configuration of the capabilities and features of the CSE.

Diagnostics and Monitoring Function (DMF): This function includes the troubleshooting of the CSE through the use of operational status (e.g. local context) associated with the CSE capabilities and features.

Software Management Function (SMF): This function provides the lifecycle management for software components and associated artifacts <??> for different components such as CSE and AE.

ASM CSF does not include management of security capabilities. <Tim and Dragan to validate this statement>

##### 6.2.1.2.3	CSE Monitoring

CSE Monitoring provides operating characteristics of the CSE capabilities. These operating characteristics include attributes for operational status, configuration and statistics as well as management of alerts.

CSE Monitoring is provided by the following CSF's:

ASM Software Management Function:

Retrieval of log files associated with the software module.

Retrieval of the lifecycle state and associated information related to the artifacts and software modules of the Software Package.

Notifications for faults associated with software lifecycle state transitions.

A CSE's operational characteristics information exchange can be provided to an Application by the CSE as a result of a retrieval request or subscription to the resource.

----------------------------------------- End of changes ------------------------------------