| CHANGE REQUEST |
| --- |
| Group Name:* | ARC WG2 |
| Source:* | ALU, NTT DOCOMO |
| Format:* | ARC 10.0 bis Ad Hoc – Sophia Antipolis |
| Date:* | 2014-04-28 |
| Contact:* | Tim Carey, timothy.carey@alcatel-lucent.com Syed Husain, shusain2016@live.com |
| Reason for Change/s:* | Cleanup of ASM CSF description |
| Clause/Sub Clause Affected* | 6.2.1 Application and Service Layer Management |
| Agenda Item:* | 6 |
| Work item(s): | Arch TS |
| Document(s) Impacted* | TS-0001 v0.5.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Move to architecture for inclusion in the Arch TS-0001. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes to clean-up the ASM CSF description in clause 6.2.1, based on the agreement reached at TP#10 on Option 1 of ARC-2014-1218R01. All the editor’s notes are addressed as well.

----------------------------------------- Start of changes ------------------------------------

### 6.2.1	Application and Service Layer Management

#### 6.2.1.1	General Concepts

The Application and Service Layer Management (ASM) CSF provides management of the AEs and CSEs on the ADNs, ASNs, MNs, and INs. This includes functions to configure, troubleshoot and upgrade the functions of the CSE, as well as to upgrade the AEs.

#### 6.2.1.2	Detailed Descriptions

The ASM CSF provides management capabilities for a CSE and the AEs.

# Figure 6.2.1.2-1: Management Layers and Functions

<Rapporteur Note: Picture above has been changed.

The ASM CSF utilizes the functions provided by the DMG CSF for interaction with the Management Server.

The management functions include:

Configuration Function (CF): This function includes the configuration of the capabilities and features of the CSE (e.g., CMDH Policies).

Software Management Function (SMF): This function provides the lifecycle management for software components and associated artifacts (e.g., configuration files) for different entities such as CSE and AE.

----------------------------------------- End of changes ------------------------------------