| CHANGE REQUEST |
| --- |
| Group Name:* | <WG2> |
| Source:* | NTT DOCOMO, ZTE |
| Format:* | ARC# 10.0 bis Ad Hoc – Sohia Antipolis |
| Date:* | 2014-04-28 |
| Contact:* | Syed Husain, NTT DOCOMO – shusain2016@live.com Rajesh Bhalla, ZTE – rabhalla@ztetx.com |
| Reason for Change/s:* | Void Clause 6.3 – Functional Entities Comprising Enablers |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001 v0.5.0 |
| Clauses/Sub Clauses* | 3.1, 3.3, 6.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes to void current clause 6.3 in TS-0001 on Enablers, and its associated text in other clauses. The reason being that utilization of functional entities comprising enablers is not specified  in the current release, and therefore should be removed.

### ---------------------------------Start of change 1 -----------------------------------------

## 3.1	Definitions

For the purposes of the present document, the following terms and definitions apply:

Application Layer: The Application Layer comprises oneM2M Applications and related business and operational logic.

Common Services Layer: The Common Services Layer consists of oneM2M service functions that enable oneM2M Applications ( e.g., management, discovery and policy enforcement).

Common Services Function: A Common Services Function (CSF) is a service function that is common to the M2M environment and specified by oneM2M. A set of CSFs is contained in the CSE.

Device	(6.2.9.2)

Device Entity (6.2.9.2)

# Device Management Resource

Execution Environment: An Execution Environment is a logical entity that represents an environment capable of running some software modules.

Hosting CSE: A Hosting CSE is the CSE where the addressed resource is hosted.

# M2M Service Provider Domain: A M2M Service Provider Domain is the part of the M2M System that is associated with a given M2M Service Provider.

Managed Entity: A Managed Entity is an M2M Device, M2M Gateway, devices in the M2M Area Network as well as M2M Application Layer and M2M Service Layer software components.

# Management Adapter

# Management Client Management Resource

# Management Server

Network Services Layer: The Network Services Layer provides transport, connectivity and service functions.

Node: A functional entity containing one of the following:

one or more M2M Applications;

one CSE and zero or more M2M Applications.

Originator: The Originator is the actor that initiates a Request. An Originator can either be an Application or a CSE.

Receiver: The Receiver is the actor that receives the Request. A Receiver can be a CSE or an Application.

Registree: A Registree is an AE or CSE that registers with another CSE.

Registrar CSE: A Registrar CSE is the CSE where an Application or a CSE has reigstered.

# Request (7.1.7)

# Response (7.1.7

Resource: A Resource is a uniquely addressable entity in oneM2M System (e.g., by the use of a Universal Resource Identifier (URI)). A resource can be accessed and manipulated by using the specified procedures.

[3.1.g] Editor's Note: The above stated definition of Resource needs to be revisited. This is FFS.

[3.1.h] Editor's Note: It is expected that more definitions are needed. This is FFS.

# Role

Service Charging and Accounting: A set of functionalities within the M2M service layer  that enable configuration of information collection and charging policies, collection of Charging Records based on the policies, and correlate Charging Records to users of M2M common services.

Service Charging Record: Formatted collection of information about a chargeable operation.

Service Layer Offline Charging: Charging mechanism where charging information does not affect, in real-time, the service rendered.

Service Layer Online Charging: Charging mechanism where charging information can affect, in real-time, the service rendered, including real time credit control

Software Package: A Software Package is an entity that can be deployed on the Execution Environment.  It can consist of entities such as software modules, configuration files, or other entities.

Software Module: A Software Module is  ....

Structured Data: Structured Data is data that either have a structure according to a specified Information Model or are otherwise organized in a defined manner.

### ---------------------------------End of change 1 -----------------------------------------

### ---------------------------------Start of change 2 -----------------------------------------

## 3.3	Abbreviations & Acronyms

[3.3.a] Editor'  Note: Missing some Text

For the purposes of the present document, the following abbreviations and acronyms apply:

3GPP	3rd Generation Partnership Project

A/AAAA	Authentication, Authorization, Accounting and Auditing

ADN	Application Dedicated Node

ADN-AE	AE which resides in the Application Dedicated Node

AE	Application Entity

AID CSF	Addressing and Identification CSF

API	Application Programming Interface

ASM	Application and Service Layer Management

ASM CSF	Application and Service Layer Management CSF

ASN	Application Service Node

ASE-AE	Application Entity that is registered with the CSE in the Application Service Node

ASN-CSE	CSE which resides in the Application Service Node

CDR	Charging Data Record

CF	Configuration Function

CMDH 	Communication Management and Delivery Handling

CSE	Common Services Entity

CSE-PoA	CSE Point of Access

CSF	Common Services Function

DCF	Device Configuration Function

DDMF	Device Diagnostics and Monitoring Function

DHCP	Dynamic Host Control Protocol

DIS CSF	Discovery CSF

DFMF	Device Firmware Management Function

DTMF	Device Topology Management Function

DMF	Diagnostic and Monitoring Function

DNS	Domain Name Server

DMG CSF	Device Management CSF

DMR	Data Management and Repository

GMG CSF	Group Management CSF

GPS	Global Positioning System

GSMA	GSM Association (Global System for Mobile Communication Association)

IMEI	International Mobile Equipment Identity

IN	Infrastructure Node

IN-AE	Application Entity that is registered with the CSE in the Infrastructure Node

IN-CSE	CSE which resides in the Infrastructure NodeIP	Internet Protocol

JNI	Java Native Interface

LOC CSF	Location CSF

M2M	Machine to Machine

MN	Middle Node

MN-CSE	CSE which resides in the Middle Node

MSISDN	Mobile Subscriber Integrated Services Digital Network-Number

MTC	Machine Type Communications

OMA	Open Mobile Alliance

NSE	Network Service Entity

NSSE CSF	Network Service Exposure, Service Execution and Triggering CSF

OID	Object Identifier

PPP	Point to Point Protocol

REG CSF	Registration CSF

RPC	Remote Procedure Calls

SCA CSF	Service Charging and Accounting CSF

SCS	Services Capability Server

SDO	Standards Developing Organization

SEC CSF	Security CSF

SMF	Software Monitoring Function

SMS	Short Messaging System

SP	Service Provider

SSM 	Service Session Management

SSM CSF	Service Session Management CSF

SUB CSF	Subscription and Notification CSF

Tsp	(7.3.2.3.2)

Tsms	(7.3.2.3.2)

# UE	User Equipment

URI	Universal Resource Identifier

### ---------------------------------End of change 2 -----------------------------------------

### ---------------------------------Start of change 3 -----------------------------------------

## 6.3	Void

### ---------------------------------End of change 3 -----------------------------------------