| CHANGE REQUEST |
| --- |
| Group Name:* | ARC#10 ad-hoc |
| Source:* | LG Electronics |
| Format:* | F2F ad-hoc meeting |
| Date:* | 2014-04-28 |
| Contact:* | SeungMyeong Jeong (seungmyeong.jeong@lge.com) |
| Reason for Change/s:* |  |
| CR against: Release* | 1.0 |
| CR against: TS/TR* | oneM2M-TS 0001 Technical Architecture v 0.5.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

[ 10.2.3.1.a] Editor's Note: Clause x.y.z refers to the table which describes the attributes of <container> resource.

- Which attributes shall/may be included is already described right above the editor’s note. Hence this needs to be removed.

[ 10.2.3.2.a] Editor's Note: Clause 9.6.6 refers to the table which describes the attributes of <container>.

- Information is already described right above the editor’s note. Hence this needs to be removed.

[ 10.2.3.1.b] Editor's Note: The type of the resource to be created (ty) needs to be specified by the contributor as part of "Information on Request message".

- This should be added in clause 10.1.1.1Non-registration related CREATE procedure. This added in change 2 below.

### ----------------------- Start of change 1 -----------------------

#### 10.2.3.1	Create <container>

This flow is used for creating a <container> resource.

Originator: the Originator can be an Application Entity or a CSE.

Receiver: Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in clause xxx), the Receiver shall create a <container> resource.

# Table 10.2.3.1-1: <container> CREATE

| CREATE: Description |
| --- |
| Pre-Conditions | The Originating AE or CSE has to be successfully authenticated and access to the Receiver has been granted. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for the following attributes from clause 9.6.5 are mandatory for the request: nm: Name of <container> resource is optional, cn: The resource content shall provide the information as defined in clause 9.6.3. The following attributes from clause 9.6.3 are mandatory for the Request: “resourceType” which shall be set to the appropriate tag that identify the Container resource as defined in 9.6.1; “creator” which it contains the information provided in the fr parameter of the request. The following attributes from clause 9.6.3 are optional for the request: “expirationTime” “accessControlPolicyID” “Labels” “maxNrOfInstances” “maxByteSize” “maxInstanceAge” “locationID”: which is used only if the instances of the container are for location information. “ontologyRef” |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.1) |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for: cn: URI of the created <container> resource according to clause 10.1.1. |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedures (clause 10.1.1) are applicable. |

#### 10.2.3.2	Retrieve <container>

This flow is used for retrieving the attributes of a <container> resource.

Originator: the Originator can be an Application Entity or a CSE.

Receiver: Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in clause xxx), the Receiver shall retrieve the <container> resource.

# Table 10.2.3.2-1: <container> RETRIEVE

| RETRIEVE: Description |
| --- |
| Pre-Conditions | The targeted <container> has been created. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for: cn: void |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.2) |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for: cn: attributes of the <container> resource as defined in clause 9.6.6 |
| Post-Conditions | No changes on the resource as consequence of the RETRIEVE operation |
| Exceptions | All exceptions described in the basic procedure (clause 10.1.2) are applicable. |

### ----------------------- End of change 1 -----------------------

### ----------------------- Start of change 2 -----------------------

#### 10.1.1.1	 Non-registration related CREATE procedure

This procedure is valid for all resources which are not related to registration.

As a pre-condition for this procedure, the Originator has been already successfully authenticated, with the procedure described in XXX <xref to security related procedures>. Therefore all exceptions that are related to authentication failure are not described in this clause.

[10.1.1.1.a]  Editor's Note:  Add SEC reference.

Originator requests to create a resource by using the CREATE method. See clause 8.1.2 for the information to be included in the Request message.

Receiver, once the Originator has been successfully authenticated and that the request is allowed by the given privileges, shall validate request and shall create the resource.

# Figure 10.1.1-1: Procedure for CREATEing a Resource

Step 001: The Originator shall send the following information in the CREATE Request message:

op: 	C (Create);

to: 	URI of the target resource where the new resource should be created (parent resource)

# fr: 	ID of the Originator (either the AE or CSE)

[10.1.1.1.b]  Editor's Note: AE or CSE may not have the ID upon its registration request. Alternative information for fr is FFS.

ty:	a resource type of the resource

nm:  optional name of the resource to be provided by the Originator, where permitted by the resource type as specified in clause 9.6.

NOTE: Some of the resources defined in clause 9.6 have a predefined name. For these resources the parameter nm is not applicable.

cn: 	attributes of the resource to be provided by the Originator. Of particular importance for the CREATE Request message is the common attribute, from clause 9.6.1, resourceType which identifies the type of resource.

[10.1.1.1.c]  Editor’s Note: which parameters are deducted to be mandatory/optional in the request is for FFS. Clause 8.1 should provide a generic mechanism to identify mandatory params for a request by looking at how the resource is defined. E.g., if the attribute in the resource definition is identified as mandatory and it is of type RW, then it is also intended as mandatory in the request.

[10.1.1.1.d]   Editor's Note: references to elements defined in sect 8 have been added here. They may be removed if we decide to move sect 8.1.2-4 to stage 3 doc. In this case, these references will be removed and sect 1 of this document would replace sect 8.1.2-4 in the TS-0001.

Step 002: The Receiver shall:

- Check if the Originator has the appropriate privileges for performing the request. Privileges are part of the attribute accessControlPolicyID of the targeted resource. In case that such an attribute does not exist, the Receiver shall check the accessControlPolicyID of the parent resource.

[10.1.1.1.e]   Editor’s Note: how far should the Receiver go back to a parent to look for an accessControlPolicyID is FFS

- Verify that the suggested nm, if provided by the Originator in the Create Request message, does not already exist in its resource structure.

- Assign an identifier to the resource to be created if a nm is not provided by the Originator.

- Assign/modify default values for mandatory certain attributes of the resource, where allowed by the resource itself. If not provided by the Originator itself, the Receiver shall assign a value to the following common attributes from clause 9.6.1:

- parentID;

- creationTime;

- expirationTime: if not provided by the Originator, the Receiver shall assign the maximum value possible (within the restriction of the Receiver policies). If the value provided by the Originator cannot be supported, due to either policy or subscription restrictions, the Receiver will assign a new value.

- lastModifiedTime; which is equals to the creationTime

[10.1.1.1.f]   Editor’s Note: which parameter is allowed to be provided by the Receiver CSE is for FFS. There are few cases: RO in most of the cases, and in some cases the Receiver may also changes the RW attributes, e.g., the expirationTime or the max number of instances which could be related to subscription agreements or policies.

- On successful validation of the Create Request, the Receiver shall create the requested resource.

Step 003: The Receiver shall respond with a Response message that shall contain the following information:

to: Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

# fr: Optional. ID of the Receiver.

cn:	URI and optionally the content of the created resource. The Receiver shall provide the content if the created resource contains attributes which were modified by the Receiver in step 002.

See clauses 8.1.3 and 8.1.4 for the information to be included in the Response message.

# General Exceptions:

- The targeted resource in to information does not exist. The Receiver responds with an error.

- The Originator does not have the privileges to Create a resource on the Receiver. The Receiver responds with an error.

- The resource with the specified name (if provided) already exists at the Receiver. The Receiver responds with an error.

- The provided information in cn is not accepted by the Receiver (e.g., missing mandatory parameter). The Receiver responds with an error.

### ----------------------- End of change 2 -----------------------

### ----------------------- Start of change 3 -----------------------

### ----------------------- End of change 3 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?