| CHANGE REQUEST |
| --- |
| Group Name:* | ARC 10 ad hoc |
| Source:* | Philip Jacobs, Cisco Systems, phjacobs@cisco.com |
| Format:* | ad hoc |
| Date:* | 2014-04-25 |
| Contact:* |  |
| Reason for Change/s:* | Resolution of Editor’s notes in clause 9.1 |
| CR against: Release* |  |
| CR against: TS/TR* | ARC TS |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR addresses some of the editors notes in 9.1. It makes this clause consistent with Table 9.1.6-1. However it is not clear why this text is needed here since it is already in Table 9.1.6-1 and does not in my opinion, exemplify a simple resource structure. I suggest it be removed.

It also updates Table 9.1.6-1 to reflect the renaming of <application> to <AE>

### ----------------------Start of change 1---------------------------------------------

# 9 Resource Management

All entities in the oneM2M System, such as AEs, CSEs, "data", etc., are represented as "resources". A "resource structure" is specified as a representation of the "resources". Such "resources" are uniquely addressable. Procedures for accessing such resources are also specified.

## 9.1	General Principles

The following are the general principles for the design of the resource model.

The "type" of each resource shall be specified. New resource types shall be supported as the need for them is identified.

The root of the resource structure in a CSE shall be assigned an absolute address. See clause 9.3.1 for additional information.

The resource structure shall be kept simple. In particular:

<AE> resources shall be located directly under the <CSEBase> or <remoteCSE> resources.

<accessControlPolicy> resources shall be located directly under the <CSEBase>, <remoteCSE>, or  <AE> resources.

<group> resources shall be located directly under the <CSEBase>, <remoteCSE>, or <AE> resources.

<remoteCSE> resources shall be located directly under the <CSEBase> resource.

<container> resources shall be located directly under the <CSEBase> , <AE> resource, <remoteCSE> or under another <container> resource.

[9.1.c]  Editor’s note: local CSE terminology needs discussing.

[9.1.c-1]: If there are other agreed contributions from 5 items above, at least "belonging to Local CSE" should be removed from Local/Registrar CSE clarifications.

The attributes for all resource type shall be specified.

Each resource type can have multiple instances.

All resource and associated attributes shall be uniquely addressable via their associated Universal Resource Identifiers (URI), consisting of:

a structured URI based on the chain of child-parent relations;

a flat URI made of a unique identifier addressable via the base root.

[9.1.e]  Editor's Note: Contribution #0505R1 already address the fact that URI is not used in a proper manner in the TS. However the term structured and flat URI still use the term URI. Detailed definition on how to do addressing in oneM2M still needs to be drafted. Alignment of the proper terminology in the TS is needed.

[9.1.f]  Editor's Note: how the flat URI can be distinguished from the structured URI is for FFS.

[9.1.g]  Editor's Note: if there is a need to provide both structured URI or flat URI of a resource if for FFS.

Examples:

Root example "myCSE" (well known, common to structured and flat).

EXAMPLE 1:	The following two examples address the same resource:

//myCSE/123(structured).

//myCSE/123 (flat).

EXAMPLE 2:	The following two examples address the same resource:

//myCSE/myApplication/987 (structured).

//myCSE/234 (flat).

EXAMPLE 3:	The following two examples address the same resource

//myCSE//myContainer (structured).

//myCSE/mC (flat).

The flat URI is always stored in the parent attribute, that is a mandatory attribute.

In case of structured URI, the relationship parent-child and vice-versa is determined in the structured URI. When created via the flat URI, the parent child-relation is determined by the parentID attribute.

This, however, does not imply any specific storage structure for the <container> resource. The structure of a <container> resource is subject to implementations.

Parts (or all) of the URIs may be replaced with pseudonym (or shorten) URIs.

Both structured and flat URIs shall be supported simultaneously over Mcc, and Mca for IN-CSE and MN-CSE

Both structured and flat URIs should be supported simultaneously over Mcc, and Mca for ASN-CSE. For example, the structured URI can be supported for CREATE while both URI types can be supported for other operations (i.e. RETRIEVE, UPDATE and DELETE).

### ----------------------End of change 1---------------------------------------------

### ----------------------Start of change 2---------------------------------------------

Table 9.6-1 Resource Summary

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Stores a representation of privileges. It is associated with resources that shall be accessible to entities external to the hosting CSE., It controls "who" is allowed to do "what" and can be used for privacy protection. | subscription | AE, remoteCSE, CSEBase | 9.6.2 |
| instance | Represents a data instance in the container resource. | subscription | container | 9.6.7 |
| AE | Stores information about the AE. It is created as a result of successful registration of an AE with the registrar CSE. | subscription, container, group, accessControlPolicy, mgmtObj, commCapabilities, pollingChannel | remoteCSE, CSEBase | 9.6.5 |
| cmdhBuffer | Defines CMDH buffer usage limits | subscription | cmdhPolicy | D.12.7 |
| cmdhDefaults | Defines CMDH default values | cmdhDefEcValue, cmdhEcDefParamValues subscription | cmdhPolicy | D.12.1 |
| cmdhEcDefParamValues | Represent a specific set of default values for the CMDH related parameters | subscription | cmdhDefaults | D.12.3 |
| cmdhDefEcValue | Defines a value for the ec (event category) parameter of an incoming request when it is not defined. | subscription | cmdhDefaults | D.12.2 |
| cmdhLimits | Defines limits for CMDH related parameter values | subscription | cmdhPolicy | D.12.4 |
| cmdhNetworkAccessRules | Defines rules for the usage of underlying networks | cmdhNwAccessRule subscription | cmdhPolicy | D.12.5 |
| cmdhNwAccessRule | Defines a rule for the usage of underlying networks | schedule subscription | cmdhNetworkAccessRules | D.12.6 |
| cmdhPolicy | A set of rules defining which CMDH parameters will be used by default | cmdhDefaults, cmdhLimits, cmdhNetworkAccessRules, cmdhBuffer subscription | None documented | D.12 |
| container | Shares data instances among entities. Used as a mediator that takes care of buffering the data to exchange "data" between AEs and/or CSEs. The exchange of data between AEs (e.g. an AE on an node in a field domain and the peer-AE on the infrastructure domain) is abstracted from the need to set up direct connections and allows for scenarios where both entities in the exchange do not have the same reachability schedule. | container, instance, subscription, | AE, container, remoteCSE, CSEBase | 9.6.6 |
| CSEBase | The structural root for all the resources that are residing on a CSE. It shall store information about the CSE itself. | remoteCSE, node, AE, container, group, accessControlPolicy, subscription, mgmtObj, mgmtCmd, locationPolicy, statsConfig | None | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | subscription | None documented | 9.6.11 |
| eventConfig | Defines events that trigger statistics collection | subscription | statsConfig | 9.6.23 |
| execInstance | The Execution Instance resource contains all execution instances of the same management command mgmtCmd. | subscription | mgmtCmd | 9.6.17 |
| group | Stores information about resources of the same type that need to be addressed as a Group. Operations addressed to a Group resource shall be executed in a bulk mode for all members belonging to the Group. | members subscription | AE, remoteCSE, CSEBase | 9.6.13 |
| locationPolicy | Includes information to obtains and managemanages geographical location It is only referred from container, in case that the instances of the container provide location information. | subscription | CSEBase | 9.6.10 |
| members | Virtual resource containing target for group requests It is used for addressing bulk operations to all the resources that belong to a group. | None documented | group | 9.6.14 |
| mgmtCmd | Management Command resource represents a method to execute management procedures required by existing management protocols. | execInstance subscription | CSEBase | 9.6.16 |
| mgmtObj | Management Object resource represents management functions that provides an abstraction to be mapped to external management technology. It represents the node and the software installed in the node | parameters subscription | remoteCSE, CSEBase | 9.6.15 Annex D |
| m2mServiceSubscription | Data pertaining to the M2M Service Subscription | nodeInfo subscription | None documented | 9.6.19 |
| node | Represents specific Node information | schedule, mgmtObj subscription | CSEBase, remoteCSE | 9.6.18 |
| nodeInfo | Node information | subscription | m2mServiceSubscription | 9.6.20 |
| parameters | Provides a mechanism to describe the management object in a generic way to easily import information from existing management protocols. | parameters subscription | mgmtObj, parameters | 9.6.16 |
| pollingChannel | Represent a channel that can be used for a request-unreachable entity | None documented | remoteCSE, AE | 9.6.21 |
| remoteCSE | Represents a remote CSE for which there has been a registration procedure with the registrar CSE identified by the CSEBase resource. | AE, container, group, accessControlPolicy, subscription, mgmtObj, pollingChannel, node | CSEBase | 9.6.4 |

### ----------------------End of change 2---------------------------------------------