| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | ARC 10.0 bis Ad-Hoc |
| Date:* | 2014-04-25 |
| Contact:* | Josef Blanz, jblanz@qti.qualcomm.com Wolfgang Granzow, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | The details on using the <delivery> resource type have been defined in clause 10.2.4. Therefore, the Editor’s Note on this aspect can be removed. It is proposed to define that <delivery> resources shall be children of a <CSEBase> resource. If that is acceptable, also the Editor’s Note on the missing definition of a parent resource type for <delivery> can be removed. Furthermore, references to CSFs were removed (not normative any more). |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.5.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The details on using the <delivery> resource type have either already been defined in clause 10.2.4 or clarified by two additional sentences in the proposed changes below. Therefore, the two Editor’s Note on those aspects can be removed..

### -----------------------Start of change 1-------------------------------------------

### 9.6.11	Resource Type delivery

When a CSE is requested to initiate an operation (CRUDN) targeting resources on another CSE, then it needs to do scheduling and execution of delivery of data from the source CSE to the target CSE in line with the provisioned policies. It shall be done in one of the following ways: Using delivery aggregation or by forwarding the original request as a separate request on the Mcc reference point without changes.

In order to be able to initiate and manage the execution of data delivery in a resource-based manner, resource type delivery is defined. This resource type shall be used for forwarding requests from one CSE to another CSE when the da parameter in the request is set to ON. If the da parameter is set to OFF, the original request shall be forwarded without changes to the next CSE, i.e., without the use of <delivery> resource. If the da parameter is not present, the latter method shall be used.

Operations to Retrieve, Update or Delete a <delivery> resource shall allow authorized entities to inquire the status of a delivery, change delivery attributes or cancel a delivery.

As defined in clause 10.2.4, <delivery> resource can only be created by a CSE. A Request for the creation of a <delivery> resource can only be issued to a Registrar CSE. <delivery> resource is deleted on successful delivery of  the data in aggregatedRequest attribute to the next hop CSE.

The parent of a <delivery> resource is the <CSEBase> resource of the CSE that accepted the Request for creation of the <delivery> resource.

### -----------------------End of change 1-------------------------------------------

# Comments

All Details are defined in 10.2.4 and in the additional normative text added in the two paragraphs above.

The parent resource type has been defined now in the paragraph above.