| CHANGE REQUEST |
| --- |
| Group Name:* | <WG2> |
| Source:* | Intel, NTT DOCOMO |
| Format:* | ARC #10 bis Ad Hoc |
| Date:* | 2014-04-28 (Sophia Antipolis) |
| Contact:* | Puneet Jain – puneet.jain@intel.com Syed Husain – shusain2016@live.com |
| Reason for Change/s:* | Cleanup of GMG CSF description |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001 v0.5.0 |
| Clauses/Sub Clauses* | 6.2.6 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes to make the GMG CSF text informative by removing all normative text, based on agreement reached on ARC-2014-1218 at TP#10.

### -------------------------------Start of changes ------------------------------------

### 6.2.6	Group Management

#### 6.2.6.1	General Concepts

The Group Management (GMG) CSF is responsible for handling group related requests. The request is sent for the management of a group and its membership as well as for the bulk operations supported by the group. When adding or removing members to/from a group, it is necessary to validate if the group member complies with the purpose of the group. Bulk operations includes read, write, subscribe, notify, device management, etc. Whenever a request or a subscription is made via the group, the group is responsible for aggregating its responses and notifications. The members of a group can have the same role with regards to access rights control towards a resource. In this case, access control is facilitated by grouping. When the Underlying Network provides broadcasting and multicasting capability, the GMG CSF is able to utilize such capability.

#### 6.2.6.2	Detailed Descriptions

The GMG CSF enables the oneM2M system to perform bulk operations on multiple devices, applications, or resources that are part of a group. In addition, the GMG CSF supports bulk operations to multiple resources of interest and aggregates the results. It facilitates access control based on grouping. When needed and available, the GMG CSF may leverage the existing capabilities of the Underlying Network including broadcasting/multicasting.

When facilitating access control using a group, only members with the same access rights towards a resource is included in the same group. Also, only M2M AEs or CSEs which have a common role with regards to access rights is included in the same group. This is used as a representation of the "role" when facilitating role based access control.

The service functions supported by the GMG CSF are as follows:

- Handles the requests to create, query, update, and delete a group. An AE or a CSE may request the creation/retrieve/update/deletion of a group as well as the addition and deletion of members of the group.

- Creates one or more groups in CSEs in any of the Nodes in oneM2M System for a particular purpose (i.e., facilitation of access control, device management, fan-out common operations to a group of devices, etc.).

- Handles the requests to retrieve the information (e.g., URI, metadata, etc.) of a group and its associated members.

- Manages group membership, andhandles requests to add or remove members to and from a group's member list. A member may belong to one or more groups. A group may be a member of another group. When new members are added to a Group, the GMG CSF validates if the member complies with the purpose of the group.

- Leverages the capabilities of other CSFs in order to fulfil the functionalities supported  by the GMG CSF service functions. Examples include: NSSE CSF for leveraging broadcasting/multicasting capability from the Underlying Network, Security CSF for authentication and authorization, etc. The use of Underlying Network  broadcasting/multicasting capability is not specified in this release.

- Forwards requests to all members in the group. In case the group contains anothergroup as a member, the forwarding process is done recursively, i.e., the nested group forwards the request to its members. After forwarding the request to all members in the group, the GMG CSF generates an aggregated response by aggregating the corresponding responses from the Group members.

- Supports subscriptions to individual groups. Subscriptions to a group is made only if the subscriber is interested in all members of the group. If subscription to a group is made, the GMG CSF aggregates the notifications from the group members, and notifies the subscriber with the aggregated notification. Responses and event notifications relevant to a subscription may be selectively filtered by filtering criteria.

### --------------------------------End of changes -------------------------------------

# Comments

Requests for what? This seems to be covered in paragraph after next.