| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | ARC 10.0 bis Ad-Hoc |
| Date:* | 2014-04-30 |
| Contact:* | Josef Blanz, jblanz@qti.qualcomm.com Wolfgang Granzow, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Cleanup of ‘rc’ parameter in Clause 8.1.2. Removal of editor’s note (not needed anymore) and removal of redundant ‘result notification’ as this is already covered in ‘rt’ parameter. |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.5.0 |
| Clauses/Sub Clauses* | 8.1.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The definition of the ‘rc’ request parameter contains an outdated editor’s note and a redundant setting for rc (overlapping with ‘rt’ setting ‘nonBlockingAsync’). This CR is proposing to clean up those issues.

### -----------------------Start of change 1 ------------------------------------------------------

- rc: optional result content: Indicates what are the expected components of the result of the requested operation. The Originator of a request may not need to get back a result of an operation at all. This shall be indicated in the rc information. Which exact settings of rc are possible depends on the requested operation specified in op. Possible values of rc are:

- attributes: Representation of the requested resource shall be returned as content, without the URI(s) of the child resource(s). This is the default value. For example, if the request is to Retrieve a <container> resource, the URI(s) of the <contentInstance> child-resource(s) is not provided. This setting is not valid for a Notify operation.

- attributes+child-resources: Representation of the requested resource, along with the URI(s) of the child resource(s), possibly limited by a maximum number of retrieved links, shall be returned as content. For example, if the request is to Retrieve a <container> resource, the <container> resource and the URI(s) of the <contentInstance> child-resource(s) are provided. This setting is not valid for a Notify operation

- child-resource: URI(s) of the child resources, possibly limited by a maximum number of retrieved URI(s), without any representation of the actual request resource shall be returned as content. For example, if the request is to Retrieve a <container> resource, only the URI(s) of the <contentInstance> child-resource(s) is provided. This setting is not valid for  a Notify operation

- nothing: Nothing shall be returned as operational result content. This setting is not valid when a Retrieve operation. This setting is the default when a Notification was requested by the ‘op’ parameter.

- announced-resource: Representation of the announced resource at local CSE shall be returned without the URI(s) of the child resource(s). If such information is not available at the local CSE, information at original resource Hosting CSE as per "attribute" setting shall be returned. This option shall not be used if the optional parameter fc (filter criteria) is included. This setting is not valid for  a Notify operation.

[

### -----------------------End of change 1 --------------------------------------------------------

# Comments

A result message will contain not only the result of an operation. Therefore it is best to just state that this parameter specifies what is the desired result content. Beyond that there will be status information etc in a message that also carries a result of a requested operation.

A result notification can already be requested as part of the ‘rt’ parameter: Under the setting ‘nonBlockingRequestAsynch’, it is possible to ask for a notification of the result: “The result of the requested operation needs to be sent as a notification to the Originator”. Since ‘rc’ should not define HOW the result is communicated, but WHAT goes into the result, it is straight forward to keep the option to get a notification in rt and remove it here.

Operations are defined to be CRUD & N. There is no need to restrict usage of ‘rc’ setting based on any other information. With the clarifications on dependencies on particular CRUDN cases, the text above is supporting all CRUDN on all kinds of resources and procedures related to that. So the Editor’s Note can be removed.